SiD
ECAL R&D
Status and Prospects
05.03.2007
Marcel Stanitzki
STFC-Rutherford Appleton Laboratory

---
Introduction
The SiD Calorimetry System is build around the Particle Flow paradigm
  - High granularity
  - Located inside the solenoid
  - Well integrated with Tracking
The ECAL is designed as Imaging ECAL
  - Material of choice is Si+W
  - Sampling calorimeter
  - Good energy resolution
  - Compact
  - Segmentation smaller than rMoliere

---
SiD – a PFA detector
ECAL
Vertex
Detector
HCAL
Tracker
Solenoid
Flux Return and Muon chambers

---
Physics with the ECAL
Multi-jet final states (Higgs, Top ..)
  -  measurement should not limit jet resolution
  - identify and measure hadronic showers
  - track charged particles
 id and analyses
Photons
  - Energy resolution, e.g. h
  - Vertexing of photons ( b1 cm ), e.g. for SUSY studies
Electron ID
Bhabhas and Bhabha acollinearity
Hermiticity
 Imaging ECAL can do all this

---
Some Examples
4
Jet Environment
+  + (+o)

---
Mechanical layout
Baseline configuration:
longitudinal: (20 x 5/7 X0) + (10 x 10/7 X0)  17%/sqrt(E)
1 mm readout gaps  13 mm effective rMoliere

---
Two ECAL options
Si+W
Common Mechanical Design
Traditional Silicon Diodes
HEP-style silicon
16 mm2 hexagons
Analog readout
KPiX readout chip
SiD baseline
TeraPixel
CMOS MAPS
50 µ pixel size
Digital readout
readout integrated in pixel
Alternate option

---
SiD Requirements
Fit in common mechanical structure
Power pulsing (1 % duty cycle)
  - passive cooling
  - Requires < 40 mW/channel
Single Bunch Time stamping
Bump Bonds
Metallization on detector from KPix to cable
Kapton Data (digital) Cable
KPiX
Gap  1 mm
Si Detector
Kapton
Heat Flow
Thermal conduction adhesive
Tungsten
Tungsten

---
The “traditional” approach
6 inch wafers
1024 13 mm2 pixels
improved trace layout near KPiX to reduce capacitance
procurement in progress , 40 wafers from Hamamatsu
KPiX ASIC and sample trace

---
KPix readout chip
1024 channels
  - prototypes have 64 channels
bump-bondable
13 bit ADC and Dynamic Gain
selection
0.25 micron CMOS
~ 20 mW/channel
KPiX is also foreseen to be used in
  - Tracker
  - HCAL
  - Muon chambers

---
KPiX in Detail

---
Current Status
Working on first 1024 channel version
  - 64 channel protypes are tested extensively
  - 6th generation prototype available
  - Design work on 7th generation
  - One intermediate 256/512 channel version foreseen
Demonstrate Bump-bonding of KPiX
Build Test beam module (30 layers)
Start on a real mechanical design

---
TeraPixel Option
Build on MAPS technology
  - Using Deep p-well process
50 x50 micron pixels
Digital ECAL
  - Operates as a shower particle counter
First generation sensor has been manufactured
168x168 pixels, 8.2 million transistors

---
Integrated Readout
28000 pixels
Each pixel has
  - Amplifier
  - Comparator
  - Mask/Trim
42 pixels share (1 row)
  - SRAM memory
  - Logic
Power pulsing

---
Current Status
First generation chip delivered
  - A technology demonstrator
Testing has started
Put in DESY Testbeam Dec 2007
Started working on second iteration
  - using all input from 1st generation
  - design a more real world prototype
BEAM

---
The people involved
ECAL Contacts
Ray Frey & David Strom
Traditional Silicon Diodes
U Oregon
SLAC
UC Davis
Brookhaven
LAPP Annecy
TeraPixel
RAL
Imperial College
U. Birmingham

---
First mechanical design
Marco Oriunno, SLAC
Only 2 Si sensor mask-sets required

---
Where to contribute ?
Hardware projects always welcome more interested parties
Clearly have a lot of detector optimization to do as well
  - Needed for the LoI
Two key areas where we severely lack effort
  - Optimize Detector Layout
  - Physics studies and benchmarks

---
Detector Optimization
Segmentation
  - How small
  - Use for Tracking
Layers
  - How many layers
  - thickness ?
Calorimeter depth (How many X0)
Hybrid Designs
  - 10 layers MAPS + 20 layers diodes
  - Benefits

---
Physics
What performance do we need for e.g.
  - Photon ID
  -  id and analysis
  - Flavor tagging
  - Particle Flow
Do physics studies to test ECAL performance
  - stau studies
  - h
  -  polarization
  - more ideas ...

---
How to get involved ?
Talk to us during TILC08
Contact the ECAL coordinators
  - Ray Frey and David Strom
Come to our phone meetings
  - 2 pm (PST) / 10 pm (GMT)
Come to the next SiD Workshop
  - 14-16. April , RAL http://hepwww.rl.ac.uk/SiDmeetingUK/
Everyone is welcome !

---
Summary
From Ray Frey:
  - The recent political choices in the U.S. and U.K. have thrown a monkey wrench in the works.
But still making good steady progress ...
Still going strong for the LoI
Always open for interested people
Thanks to Ray Frey, John Jaros, David Strom, Mani Tripathi for comments & material