## Slide 1
S. Bettoni, R. Corsini, A. Vivoli
(CERN)
CLIC drive beam injector design

## Slide 2: Outline
CTF3 drive beam injector:
  Design, experimental verifications
CLIC drive beam injector layout:
  Optimization process and criteria
  Proposed layout
  Longitudinal and transverse beam dynamics simulations
  Critical view of the results and possible cures
Conclusions & outlook

## Slide 3: Drive beam injector: CTF3 example
odd buckets
even
buckets
  RF deflector n0 / 2
Gap creation and combination
Phase coding
180 phase switch
Acceleration n0
Deflection n0 / 2
Sub-harmonic bunching n0 / 2

## Slide 4: Drive beam injector: CTF3 experience
Key parameters for the SHB system:
    Time for phase switch < 10 ns
    Satellites (particles captured in 3 GHz RF buckets) population < 7 %
Phase switch:
Phase switch within eight 1.5 GHz periods (<6 ns).
Satellite bunch population:
Satellites bunch population
estimated to ~8 %.
Main
Satellites

## Slide 5: CTF3 first rescaling: the SHB system
Lshb = 3*LshbCTF3 (6 cells)
Gshb = GshbCTF3/3
Lshb = LshbCTF3 (2 cells)
Gshb = GshbCTF3
Lshb = 2/3*LshbCTF3 (4 cells)
Gshb = 3/4*GshbCTF3
Frequency (GHz) | 1.49928
Number of cells | 6
Iris diameter (mm) | 66
Cell length (mm) | 26
Input power (kW) | 40
Filling time (ns) | 10
 | SHB1 | SHB2 | SHB3
Phase advance/cell (º) | 74.82 | 70.21 | 68.23
Phase velocity/c | 0.63 | 0.67 | 0.69
CTF3

## Slide 6: The Matlab driven optimization tool
Starting distribution
Parmela file input
Parmela run
Analysis of the results
Automatic minimization
process

## Slide 7: The optimization process: some details
During the optimization:
  The code varies the parameters of the system and it does some checks on them
  From the output of Parmela the tool calculates the number of particles in the main of the reference particles cutting the distribution at the target bunch length
  The number of particles in this region is maximized

## Slide 8: CLIC drive beam injector layout
Thermionic gun
Prebuncher
Buncher
Slit
Quadrupole
Bend
Accelerating cavity
53 MeV
140 KeV
6 MeV
26 MeV
SHB
Solenoids

## Slide 9: Exit of the gun
Energy = 0.140 MeV
sE= 0.00016 MeV
DT= 6 ns
gb ex,y= 3.48 mm rad
CLIC parameter | Unit | Value
Pulse duration Repetition rate | ms Hz | 140.3 50

## Slide 10: SHB system
Energy = 0.138 MeV
sE= 0.029 MeV
DT= 9.68 ns
SHB1 | Unit | Value
Length N. cells Frequency Phase velocity Voltage Aperture radius | cm MHz c kV cm | 15.6 2 499.75 0.93 35.0 4.7
SHB2 | Unit | Value
Length N. cells Frequency Phase velocity Voltage Aperture radius | cm MHz c kV cm | 15.6 2 499.75 0.61 36.5 4.7
SHB3 | Unit | Value
Length N. cells Frequency Phase velocity Voltage Aperture radius | cm MHz c kV cm | 15.6 2 499.75 0.73 38.8 4.7

## Slide 11: Prebuncher
Energy = 0.147 MeV
sE= 0.035 MeV
DT= 9.7 ns
Satellites= 5.5 %
Parameter | Unit | Value
Length Number of cells Frequency Accelerating gradient Aperture radius | cm MHz MV/m cm | 6 1 999.5 1.2 4.7

## Slide 12
Energy = 4.20 MeV; sE= 1.01 MeV; st= 55.89 ps.
Buncher
Parameter | Unit | Value
Phase velocity: First 12 cells Last 6 cells Phase advance/cell Total length Accelerating field Beam aperture radius | c c p m MV/m cm | 0.68-0.99 1 2/3 1.681 4.2 4.7

## Slide 13: Exit of the solenoids (E30 MeV)
Energy = 26.34 MeV; sE= 2.16 MeV; st= 36.58 ps.
Accelerating cavities parameter | Unit | Value
Phase velocity Number of cells Phase advance per cell Total length Voltage Beam aperture radius | c p m MV cm | 1 10 2/3 0.9998 4.8 4.7

## Slide 14: Cleaning chicane
Bend length = 15 cm; Bend angle = 14.32 deg; Reference E = 26 MeV; Slit aperture = 7 mm;
Intensity decrease = 24%.
R5,6 = 78 mm
Before the chicane
After the chicane
CTF3

## Slide 15: After the cleaning chicane
Energy = 26.07 MeV; sE= 0.40 MeV; st= 17.14 ps.
Before the chicane
After the chicane

## Slide 16: Injector exit (E50 MeV)
Energy = 53.25 MeV; sE= 0.45 MeV; st= 9.45 ps. gbex= 32.92 mm rad; gbey= 28.73 mm rad.

## Slide 17: CLIC drive beam injector: transverse dynamics

## Slide 18: CLIC requests and simulation results
Parameter | Unit | Simulations | CLIC
Energy Bunch charge Bunch length (rms) Energy spread (rms) Horizontal normalized emittance (rms) Vertical normalized emittance (rms) Satellites population | MeV nC mm MeV mm rad mm rad % | 53.2 8.16 2.83 0.45 (@53 MeV) 32.9 28.7 4.9 |  8 3 (@ 50 MeV) < 0.50 (@ 50 MeV)  100  100 As less as possible
CLIC requets fulfilled

## Slide 19: CLIC drive beam injector design: a critical view
More optimizations still ongoing:
  Intensity decrease at the chicane = 24% (close to CTF3 20%)
  Additional chicane needed
  (power???)
  Satellites population = 4%

## Slide 20: Satellites minimization: possible cures
Identified two approaches to minimize the satellites content:
  Minimize the number of particles in the time interval of the satellites
  Use an additional SHB to shift the energy of the satellites
Starting from an idea by P. Urschütz (presently at Siemens)
CDR version
Modified version

## Slide 21: Efficiency: an alternative solution
Re-optimization using as a figure of merit the energy spread at a fixed bunch length and optimization of the accelerating cavities:
  Intensity decrease at the chicane = 19% (24%)
  Total losses from the start = 22% (30%)
  Particles to be lost in the additional chicane reduced by a factor 2
Particles in a more confined E-t region

## Slide 22: Conclusions
A design of the CLIC drive beam injector based on a thermionic gun has been studied
Parmela simulations verified that the challenging CLIC requests can be fulfilled (longitudinal & transverse)
Identified some possible improvements (beam losses, satellites content) and optimization already ongoing
Further studies (beam loading compensation, wakefields effects and beam stability) to be done
Proper RF design of the elements to be done

## Slide 23: If you don’t have other questions …

## Slide 24: Spare slide: space charge
Without space charge
With space charge