Micromegas DHCAL status report
Jan BLAHA
On behalf of the LAPP LCD group
CALICE Collaboration Meeting, 22 – 24 September 2010, Casablanca, Morocco

---
Outline
Micromegas basic performance
1m2 prototype – design and test
Test beam of the 1m2 prototype
Readout electronics and DAQ
Simulation studies
Test beam plans (2010/2011)
Conclusions

---
MICROMEGAS for DHCAL
- Proportional mode
- Low working voltage
- Standard gas mixtures
- Robust (Bulk technology)
- High rate capability
- Sparking
  - Depends on gain & rate
  - Protection exists (RD51)
- Large area
  - Relatively new
  - RD51: MAMMA, SDHCAL
3 mm gas, 1 cm2 pads, thickness < 8mm
Maximum gain:
40.000 for 55Fe X-rays
15.000 for MIPs
Energy resolution @ 5.9 keV ~ 7.5 % (FWHM = 17.6 %)

---
Basic performance (reminder)
Efficiency (th = 1.5 fC) about 97% with a variations less than 1%
Hit multiplicity (th = 1.5 fC) below 1.12
2009 JINST 4 P11023
MIP MPV ~20fC
with a variations
of 11% (th = 1.5 fC)
Over 96cm2
Ambient parameters
- Pressure: -0.6%/mbar
- Temperature: 1.4%/K
LAPP-TECH-2009-03

---
1 m2 MICROMEGAS prototype
Features
- 6 ASU of 48x32 cm2 (24 ASIC / ASU)
- Dead area < 2 % inside gas volume
- Total thickness of 1.2 cm (incl. 2+2mm steel covers)
- 3 DIF boards
Test of each ASU separately first
Assembly procedure validated on mechanical prototype in 2009
HR2
HR2
HR2
HR2
HR2b
dummy

---
HR2 calibration and test of 48x32 ASU
HR2b calibration with test charge
- Some fluctuations of signal over different channels (11% over 100 cm2) → Correct detector non-uniformity with individual channel gains
- Proof of principle on preamplifier gain distribution obtained → 1 % RMS after equalization
ASU test with X-rays
- Test of complete chain (Bulk/HR/DAQ) inside a test box
- Each readout cell can be measured individually
HR2b
8 % RMS
1 % RMS

---
HR2 calibration and test of 48x32 ASU
HR2b calibration with test charge
- Some fluctuations of signal over different channels (11% over 100 cm2) → Correct detector non-uniformity with individual channel gains
- Proof of principle on preamplifier gain distribution obtained → 1 % RMS after equalization
ASU test with X-rays
- Test of complete chain (Bulk/HR/DAQ) inside a test box
- Each readout cell can be measured individually
HR2b
8 % RMS
1 % RMS

---
HR2 calibration and test of 48x32 ASU
HR2b calibration with test charge
- Some fluctuations of signal over different channels (11% over 100 cm2) → Correct detector non-uniformity with individual channel gains
- Proof of principle on preamplifier gain distribution obtained → 1 % RMS after equalization
ASU test with X-rays
- Test of complete chain (Bulk/HR/DAQ) inside a test box
- Each readout cell can be measured individually
HR2b
8 % RMS
1 % RMS

---
HR2 calibration and test of 48x32 ASU
HR2b calibration with test charge
- Some fluctuations of signal over different channels (11% over 100 cm2) → Correct detector non-uniformity with individual channel gains
- Proof of principle on preamplifier gain distribution obtained → 1 % RMS after equalization
ASU test with X-rays
- Test of complete chain (Bulk/HR/DAQ) inside a test box
- Each readout cell can be measured individually
HR2b
8 % RMS
1 % RMS

---
Assembly of the 1 m2
Gluing of ASU slab on a vetronite mask

---
Assembly of the 1 m2
Gluing of ASU slab on a vetronite mask

---
Assembly of the 1 m2
Gluing of ASU slab on a vetronite mask

---
Assembly of the 1 m2
Gluing of ASU slab on a vetronite mask

---
Assembly of the 1 m2
1. Gluing of ASU slab on a vetronite mask
2. Spacers and frame gluing

---
Assembly of the 1 m2
1. Gluing of ASU slab on a vetronite mask
2. Spacers and frame gluing

---
Assembly of the 1 m2
1. Gluing of ASU slab on a vetronite mask
2. Spacers and frame gluing
3. Cathode and cover gluing
7680 pads!

---
Assembly of the 1 m2
1. Gluing of ASU slab on a vetronite mask
2. Spacers and frame gluing
3. Cathode and cover gluing

---
Assembly of the 1 m2
1. Gluing of ASU slab on a vetronite mask
2. Spacers and frame gluing
3. Cathode and cover gluing

---
Assembly of the 1 m2
1. Gluing of ASU slab on a vetronite mask
2. Spacers and frame gluing
3. Cathode and cover gluing
  After 1 week the 1 m2 is fully assembled!

---
Assembly of the 1 m2
1. Gluing of ASU slab on a vetronite mask
2. Spacers and frame gluing
3. Cathode and cover gluing
  After 1 week the 1 m2 is fully assembled!
Total thickness is 12 mm which includes 2+2 mm of steel
→ 8 mm effective thickness complies with ILC goal (easily could be
reduced to 7 mm)

---
Test beam of the 1 m2 - set-up
1m2 prototype
Telescope
SPS/H4 beam
- 4 weeks in June/July 2010
- 150 GeV/c muons and pions
Detectors
- 3 scintillators for triggering
- Telescope with 4 Gassiplex
  chambers
- 1m2 chamber downstream
  of the telescope
DAQ
- CAEN ADC/sequencer VME
  module and LabView Centaure
- DIF (synchronized with CCC)
  and LabView program
- Trigger obeys BUSY and READY signal logic → common event
  numbering for off-line reconstruction
Rates
- Beam rate and scintillators trigger rate ~1kHz,
- Acquisition rate ~ 100Hz

---
Test beam of the 1 m2 - goals
4 weeks CERN SPS H4: 2 weeks from 10th June (CALICE) and 2 week from 24th (RD51, beam shared with other groups)
TB program with muon beam (150 GeV/c) at low intensity
- Test overall functionality of the detector
- Reach high gas gains and the lowest detection threshold on chips
- Validate/rule out assembly and technological choices
- Measure efficiency, multiplicity and uniformity
- Compare performance with and without power-pulsing of chips
N.B. The 1m2 prototype efficiency will be low (Shaping time short w.r.t. Micromegas signals), nevertheless, several technological choices can be validated and unforeseen problems can be found before the next prototype with an optimised electronics (MICROROC)

---
Chip settings
Chip parameters:
- Shaping time (per chip) – set to max ~ 20 ns
- Threshold (per chip)
- Preamplifier gain (per channel)
Uniform response settings:
- Gain equalization by injection of test charges
- Proved to work in laboratory
- Charge threshold given by pedestal dispersion (~ 10 fC)
Low threshold settings:
- Align S-curve end-points (m+5s) using preamplifier gains
- Increase gain dispersion,
  but reduce thresholds
- Used in the test beam

---
Time stamping
Timing features
- Time-stamping with 200 ns precision
- Clock distributed to DIFs by CCC
- 127 event depth chip memory
Time stamping
- Time of hits, BCID_hit (24 bits)
- Time of readout, BCID_abs (48 bits)
- Time of readout, BCID_dif (24 bits)
Signal selection
- Delay of 1 us between PM signals and readout
- So hits from triggering particles have:
  - BCID_dif - BCID_hit ~ 5 clock cycles (1 ms)
- Chips S/N ratio > 100
- Noise hit probability/chip < 1 %
  after time cut on BCID
WM
BCID_Hit (24bit)
BCID_Hit (24bit)
WM
PM
RO
BCID_Dif (24bit)
BCID_Abs (48bit)
t
WM – write to memory
PM – trigger signal
RO – read memory
    - hit
→ t = BCID_Abs + (BCID_Dif - BCID_Hit)
WM
Dt = 1ms

---
First results on TB data analysis
- Runs @ 420 V to determine the maximum efficiency
  (given the shaping time issue)
- Runs @ 410 V to determine the efficiency/multiplicity
  values and uniformity
- Use telescope to extrapolate tracks to 1m2 prototype
  Same pad size (1x1 cm2) in telescope and 1m2 prototype
  → select straight tracks in telescope:
  single aligned hits in at least 3 of the 4 chambers
  → look for hits in 1m2 chamber in 3x3 cm2 area
  around extrapolated track impact
TELESCOPE
1m2 CHAMBER
13 cm
100 cm

---
Runs @ 420 V
- Gas gain of 15000 → expected Landau MPV ~ 20 fC
  - Only 10 % of the signal is seen → effective signal MPV is 2 fC !
- Approx. 40000 triggers recorded
  - 200 Hz muon beam centered on 1 chip of ASU 12
- S/N ratio in time peak of 208 (3 noisy channels switched OFF)
  - Peak contamination after time cut < 0.5 % for the chip
  - Noise hit probability after time cut ~ 0.01 % per channel
Noisy channels switched off
ASU 12 ON only

---
Runs @ 420 V
- Average efficiency of 45.2 +/- 4.1 %
  Remember: only 10 % of the signal is seen!
- Average multiplicity of 1.05 +/- 0.02 Compatible with previous measurements with Gassiplex
Efficiency error < 5%
Efficiency error < 2.5%

---
Runs @ 410 V
- Lower gas gain and higher threshold configurations → much lower efficiency
- Determine the uniformity of efficiency and multiplicity over the 1m2 chamber area → beam directed at a few chips with 400000 triggers per chip
- First results on 2 chips indicate that the mean and RMS remain the same
  - To be completed with more results on more chips
CHIP 124
Close to center
11.2 % +/- 1.5 %
1.07 +/- 0.02
CHIP 114
Close to spacers
12.7 % +/- 1.6 %
1.07 +/- 0.02
Efficiency error < 1%

---
Power pulsing
FE power comsumption:
DIF+InterDIF: ~ 1.2-1.3 A
HR2 of 1 ASU (analog) ~ 0.4-0.5 A , except for first ASU ~1.4A (12 deffect preamp)
HR2 of 1 ASU (DAQ or Digital) ~ 0.02A
Switch ON/OFF the analog part of all chips during SPS spill.
this corresponds to a current of ~ 3 A (4*0.4+1.4) during analog_OFF
t_ON = 2 ms and t_OFF = 10 ms
S/N ratio are similar
First encouraging results → quantitative analysis is ongoing
Without PP
With PP

---
Test beam summary
Mechanics
1m2 is gas tight and robust
Electronics
- Careful grounding - good noise condition
- Electronic gain equalized (only for HR2b)
- Successful synchronization between
  Gassiplex and HR DAQs
- The HR DAQ is stable and reliable
- Power Pulsing for the complete 1m2
Detector
- Meshes are stable (very few HV supply trips)
- High gain possible (Mesh tested up to 420V = Gas gain up to 15.000)
Software
- Reconstruction of simultaneous events from both DAQs (telescope + 1m2)
- Data file book keeping under development for next test beam
All 5 ASUs of the 1m2 have showed response (beam profiles). Lot of data have been taken with ASU with HR2b, for instance, efficiency scans on a few chips with 400.000 trigger per chips.
Beam profile with
one delta-ray event

---
Test beam analysis – next steps
- Uniformity studies, run on different chips
- High voltage studies (sparks, performance)
- Pion/muon runs comparison
- Pressure and temperature effects
- HV and noise rate studies
  ...

---
Next test beam
  Test of the 1 m2 chamber in the W-structure with AHCAL:
  - ~3 weeks (from 3rd November 2010) CERN PS T9
  - Objective:
    - First comparison between 1cm2 pad Micromegas and 3cm2 scintillating tile layers
      - need synchronisation AHCAL/DHCAL
      - limited performances due to low efficiency but compulsory for next year test beams
  - Road map:
    - Gas pipe for T9 ready - same gas installation for T7 and T9 as at H4 in June 2010
    - finalize DAQs synchronization
    - Integration with W-structure at T7 (Installation foreseen around the 13rd October) and first test with muons

---
Progress on FE and DAQ electronics
Detector Interface (DIF)
  - 170 DIF board have been produced and tested
  - 165 out of 170 DIFs are fully operational and
    ready to be used
  - Intermediate DAQ with CCC fully operational
MICROROC
  - New readout chip MICROROC
  - Development with LAL/OMEGA
  - Shaping time matching the detector signal duration
  - Same digital part as HARDROC (same DAQ)
  - First prototypes have been produced
WHCAL test beam
  - Work on DAQ synchronization for AHCAL/DHCAL
  - Solution uses 2 DIFs to generate common event number
For more details see G. Vouters' talk in electronics section

---
Simulation studies
SiD HCAL performance for different mechanical designs
  - Comparison projective and tilted geometries
  - Boundary effects and impact of dead zones
  - Study completed, analysis note coming soon
Optimization of the semi-digital readout
  - Focus to improve calorimeter linearity
    and energy resolution
  - Comparison of several numerical techniques
    to determine optimal weights and thresholds
  - Promising results, study in progress,
Test beam study
  - Help to establish physics program for future test
    beams
  - Comparison of simulation and test beam data
    → Geant4 validation

---
Conclusions
Success of the first 1m2 Micromegas prototype:
  - Mechanical design and assembly procedure of the 1m2 prototype have been validated
  - Smooth functioning during test beam over one month
  - Test beam main goals have been successfully reached. First results are available
1. Design and production of an optimized readout ASIC
2. DIFs for 1m3 have been produced and successfully tested. An intermediate DAQ is available for large number of DIFs readout
3. Simulation work has allowed a better understanding of the SiD detector and has given valuable informations for test beams

---
Current work
1. Data analysis of the 1 m2 prototype test beam in June/July 2010
2. Test beam of actual 1 m2 prototype with the W-structure in November 2010
3. Work towards the production of several 1 m2 chambers with new frontend electronics
4. Participation in the new CALICE DAQ effort
5. Test of the new readout electronics for future 1 m2 chamber. First MICROROC chips have been received