## Slide 1: CLIC Energy Stages
D. Schulte for the CLIC team

## Slide 2: Current CLIC Energy Stages
Currently have two CLIC parameter sets
optimised and well studied 3TeV
not optimised 500GeV
main linac accelerating structure is not identical
  driven by more conservative emittance target at 500GeV
Considered upgrade from 500GeV to 3TeV
using same structure lengths, RF pulse lengths, drive beam components, …
small glitch is slightly larger structure input power at 500GeV
  should be corrected in next iteration
could re-use 500GeV structure at 3TeV

## Slide 3: Current CLIC Energy Stages

## Slide 4: Layout at 3 TeV
Main Beam Generation Complex
Drive Beam Generation Complex

## Slide 5: Layout for 500 GeV
Main Beam Generation Complex
Drive beam
Main beam
Drive Beam Generation Complex
Only one DB complex
Shorter main linac
Shorter drive beam pulse
2.5 km
797 klystrons
15 MW, 2x29µs=58µs

## Slide 6: Energy Stages Strategy
CLIC has focused on demonstration of 3TeV, only indicative 500GeV
Require input from physics
will have to wait
Need to have a real strategy
solid physics case, cost and schedule for each stage
optimise machine for different requirements at different energies
experience will help to improve following stages
Prepare an example staging
low energy machine for Higgs, top, …
medium energy for SUSY, triple Higgs, …
high energy for more SUSY, …

## Slide 7: Potential CLIC Staged Parameters
First stage ML structures are re-used

## Slide 8: Potential CLIC Staged Parameters
First stage ML structures are not re-used

## Slide 9: Concept First Stage
Concept! Not to scale

## Slide 10: Concept Second Stage

## Slide 11: Concept Third Stage

## Slide 12: General Construction and installation schedule
Commissioning @ 500GeV
Comm.
Comm.
Comm.
Commissioning @ 3.TeV
Comm.
Comm.
Comm.
Operation at 500 GeV
Injectors modification & first sector reinstallation
Tunnel excavation
Tunnel construction
Survey
El. Gen. services
Piping
Cabling
Machine transport
Machine inst.
Site installation
Shaft construction
Ph. Lebrun, K. Foraz, et al.

## Slide 13: Beam Parameters at Other Energies Preliminary, Indicative Choice
Based on design at energy Emax we can easily derive indicative parameters for E<Emax
leave injection complex the same
shorten the linac
adjust BDS
Obviously the beam parameters do not change before the BDS
slight changes would yield slightly better performance
correction with O(E-1/8) could be possible
Use the CLIC 3TeV and 500GeV structure to design lower energy versions of CLIC
will optimise later

## Slide 14: Potential CLIC Luminosity Above 500GeV
Blue line indicates luminosity that we can achieve with current BDS design

## Slide 15: Potential CLIC Parameters Based on 3TeV
B. Dalena, D.S.

## Slide 16: Potential CLIC Parameters Based on 500GeV

## Slide 17: Reminder: 3TeV Parameter Optimisation
Optimisation 1
  Luminosity per linac input power
Optimisation 2
  3TeV total project cost
A.Grudiev, W. Wuensch, H. Braun, D.S.

## Slide 18: Issues for Energy Stages
Consolidate the current cost/power model for 3TeV
e.g. use of permanent magnets reduces power (J. Clarke et al.)
Need to review figure of merit
luminosity needs
  so far optimised for maximum energy
  will need (generic) running plan
cost, cost and power/energy consumption, average or maximum power?
cost of initial stage, integrated cost of all stages?
Need to develop a cost/power/energy consumption model for varying energy

## Slide 19: Conclusion
Have design for
3TeV, fully optimised
500GeV, partly optimised
Can stage the two designs
almost complete re-use of components possible
Can derive preliminary designs at lower energies based on the above
Can improve our design
improved cost/power estimates
improved input on requirements from physics
adding intermediate stage
to maximise physics at each stage
to best balance performance vs. cost and power

## Slide 20: Reserve

## Slide 21
Low Energy Operation

## Slide 22: Sub-Stages: CLIC Higgs and Top Stage
Could consist of two installation stages
Build tunnel long enough for top
But install only enough structures for Higgs and run
Then add structures for top
Or only run at the top threshold
more tops but fewer Higgs
impact of missing mass analysis or others for the Higgs?

## Slide 23: Luminosity and Parameter Drivers
Beam Quality
(+bunch length)
Can re-write normal luminosity formula
Luminosity
spectrum
Beam current
In the classical limit for beamstrahlung

## Slide 24: Luminosity and Parameter Drivers
Full optimisation done, but experience shows parameters are determined as shown
Main linac structure and design
Damping Ring
BDS
(RTML)
Main linac
BDS
RTML
Damping Ring
Beam-beam

## Slide 25: Parameter and Structure Choice
Potential structures designs
RF limitations
Beam physics constraints
Parameter set
Cost model
Design choice
Physics requirements
Structure chosen to work for beam physics
Will tell the story as if we had a structure given

## Slide 26: Potential CLIC Staged Parameters

## Slide 27: Corresponding Background
Background will go down
significantly
In particular coherent pairs
nγ number of photons per beam particle
Nhad number of hadronic events with Wγγ>5GeV
Ncoh Number of coherent pairs, next slide coherent pair particles
Ninc Number of incoherent pair particles