## Slide 1: Status of the CLIC main beam injectors
Overview of the CLIC main beam injectors complex as documented in the CDR

## Slide 2: Layout
Primary 5 GeV e- Linac
Injector Linac
Booster Linac
2 GHz
Pre-injector
e+ Linac
Pre-injector
e- Linac
e- DR
gun
PDR
e+ DR
DL’s
BC1
DC gun
target
9 GeV
2.86 GeV
0.2 GeV
PDR
Spin rotatator
Two hybrid positron sources (only one needed for 3 TeV)
Common injector linac
All linac at 2 GHz , bunch spacing 1 GHz before the damping rings

## Slide 3
Zoom
e- transfer line
e+ transfer line
e- and e+ sources
e- and e+ Damping Rings
CLIC Main Beam complex

## Slide 4: Beam timing and operational modes
Before damping ring (1 GHz bunch spacing)
e-
e+
e+
e-
2314 ns
717 ns
717 ns
156-556 ns
156-556 ns
156-556 ns
156-556 ns
After damping ring (2 GHz bunch spacing)
e-
e+
1100 ns
156-556 ns
156-556 ns
Operational mode | Charge per bunch (nC) | Number of bunches
Nominal | 0.6 | 312
500 GeV | 1.2 | 312
Low energy scans | 0.6, 0.45, 0.4, 0.3, 0.23 | 312, 472, 552, 792, 1112

## Slide 5: Beam parameters
Parameter | Unit | CLIC polarized electrons | CLIC positrons | CLIC booster
E | GeV | 2.86 | 2.86 | 9
N | 109 | 4.3 | 4.3 | 3.75
nb | - | 312 | 312 | 312
Dtb | ns | 1 | 1 | 0.5
tpulse | ns | 312 | 312 | 156
ex,y | mm | < 100 | 7071, 7577 | 600,10 ∙10-3
sz | mm | < 4 | 3.3 | 44 ∙10-3
sE | % | < 1 | 1.63 | 1.7
Charge stability shot-to-shot | % | 0.1 | 0.1 | 0.1
Charge stability flatness on flat top | % | 0.1 | 0.1 | 0.1
frep | Hz | 50 | 50 | 50
P | kW | 29 | 29 | 85

## Slide 6: Polarized electron source
DC-gun, 140 kV GaAs cathode
1 GHz buncher
2 GHz buncher + accelerator
Polarized laser
Classical polarized source wit bunching system
Charge production demonstrated by SLAC experiment
Simulations showed 87 % capture efficiency (F. Zou, SLAC)

## Slide 7: Polarized electron source parameters
 |  | POLARIZED SOURCE FOR CLIC | 
 | Electrons | CLIC 1 GHz | CLIC DC/ SLAC Demo
Number of electrons per bunch (*10^9) |  | 3.72 | 1365
Charge/single bunch (nC) |  | 0.96 | NA
Charge/macrobunch (nC) |  | 300 | 300
Bunch spacing(ns) |  | 1 | DC
RF frequeny (GHz) |  | 1 | DC
Bunch length at cathode (ps) |  | 100 | DC
Number of bunches |  | 312 | NA
Repetition rate (Hz) |  | 50 | 50
QE(%) |  | 0.3 | 0.3
Polarization |  | >80% | >80%
Circular polarization |  | >99% | >99%
Laser wavelength (nm) | Laser | 780-880 | 865
Energy/micropulse on cathode (nJ) |  | 509 | NA
Energy/macropulse on cathode (μJ) |  | 159 | 190
Energy/micropulse laser room (nJ) |  | 1526 | NA
Energy/macrop. Laser room (μJ) |  | 476 | 633
Mean power per pulse (kW) |  | 1.5 | 2
Average power at cathode wavelength(mW) |  | 8 | 9.5
Laser scheme
For the 1 GHz approach cathode current densities of 3-6 A/cm2 would be needed, the dc approach uses < 1 A/cm2

## Slide 8: Polarized electron source
CLIC Goal 0.5 TeV: 35e11
J. Shepard

## Slide 9: Positron source conventional ?
Primary beam
Linac for e-
2 GHz
AMD
Gun
5 GeV
Primary beam
Linac for e-
200 MeV
Hybrid target
AMD
Primary beam
Linac for e-
200 MeV
Hybrid target
RF-deflector
Bunch compressor
AMD: 200 mm long, 20 mm radius, 6T field

## Slide 10: Hybrid target
Target Parameters Crystal |  | 
Material | Tungsten | W
Thickness (radiation length) | 0.4 | 0
Thickness (length) | 1.40 | mm
Energy deposited | ~1 | kW
Target Parameters Amorphous |  | 
Material | Tungsten | W
Thickness (Radiation length) | 3 | 0
Thickness (length) | 10 | mm
PEDD | 30 | J/g
Distance to the crystal | 2 | m

## Slide 11: Primary electron beam and linac
Parameters |  | 
Energy | 5 | GeV
Number of e- / bunch | 1.1x1010 | 
Charge / bunch | 1.8 | nC
Bunches per pulse | 312 | 
Pulse repetition rate | 50 | Hz
Beam radius (rms) | 2.5 | mm
Bunch length (rms) | 1 | ps
Beam power | 140 | kW
Can be done with thermionic gun or photo injector (CTF3 and Phin are nice references)
2 GHz rf system as used for other injector linac’s

## Slide 12: Yield simulations capture and pre-injector linac
Accelerating mode
decelerating mode
Energy density at 200 MeV
O. Dadoun
Positron yield: after target: ~8 e+/e- at 200 MeV: 0.9 e+/e- into PDR: 0.39 e+/e-

## Slide 13: Common injector linac

## Slide 14: Injector linac rf system
Structure Parameter | Value
Frequency | 1998 MHz
Structure length (30 cells) | 1.5 m
Filling time | 389 ns
Cell length and iris thickness | 50 mm, 8 mm
Shunt impedance | 54.3 – 43.3 MW/m
Aperture a | 20 – 14 mm
Cell size b | 64.3 – 62.9
Group velocity vg/c | 2.54 -0.7 %
Phase advance per cell | 2p/3
Acc 1
Acc 2
Acc 3
Acc 4
Quad
BPM
Mod
Pulse compressor
Kly 1
Kly 2
50 MW, 8 ms
250 MW, 1.5 ms

## Slide 15: Linac structure beam loading and power flow
Parameters:
tapered
f= 1998 MHz
L= 1.5 m
Pin= 53.4 MW
Nb= 312
N = 4.0 e9
Eacc = 16 MV/m
Eff = 16.5%
Almost full loading for 500 GeV parameters, will need amplitude modulation for beam loading compensation

## Slide 16: Bunch compressors
Two stages of bunch compressors, CSR, wake fields and tolerances have been studied
 | BC1, 2.86 GeV | BC2, 9 GeV
Rf frequency | 2 GHz, 15 MV/m | 12 GHz, 74 MV/m
Phase tolerance | 0.1 deg | 0.1 deg
Bunch length after compression | 300 mm factor 5.3 | 44 mm factor 6.8
Enegy spread after compression | 0.25 % | 1.7 %
Voltage | 447 MV | 1776 MV

## Slide 17: Linac Parameters
Primary 5 GeV e- Linac
Injector Linac
Booster Linac
2 GHz
Pre-injector
e+ Linac
Pre-injector
e- Linac
e- DR
gun
PDR
e+ DR
DL’s
BC1
DC gun
target
9 GeV
2.86 GeV
0.2 GeV
PDR
Spin rotatator

## Slide 18: CDR, what’s next ?
Start work on low energy machine
Cost optimization, Pre-damping ring, positron driver linac
Follow up some issues from the CDR within the CLIC work package structure
More focus on polarized positron studies in the future,
revisit undulator scheme, study polarization transport

## Slide 19
Potential for cost reduction
Cut pre-damping ring for electrons:
Which transverse and longitudinal emittance is needed from 200 MeV linac ?
Emittance possible: 25 - 50 mm, do we need more energy ?
Reduce beam power of positron drive linac:
Lower beam current and use multiple injection into PDR, timing ?
Lower beam energy (less yield) and use multiple injection
Saving potential ?
Use booster linac as well as positron drive linac:
Save entire linac +tunnel (>160 MCHF), need more rf power in booster linac,
Put injector linac in same tunnel as booster (see layout)

## Slide 20
Alternative layout
Without positron driver linac
Injector Linac
Booster Linac
2 GHz
Pre-injector
e- Linac
e- DR
gun
PDR
e+ DR
DL’s
BC1
DC gun
target
6 GeV
2.86 GeV
0.2 GeV
PDR
e-
e-
3300 ns
156ns
156ns
e+
Positron production pulse

## Slide 21: Pre-Damping ring acceptance

## Slide 22: Omori’s ERL scheme for CLIC

## Slide 23: Omori’s ERL scheme for CLIC

## Slide 24: Omori’s ERL scheme for CLIC

## Slide 25: Omori’s ERL scheme for CLIC

## Slide 26: Compton-ring for CLIC

## Slide 27: Compton-ring for CLIC

## Slide 28: Compton-ring for CLIC
Compton Ring Parameters:
E=1 GeV, 2 GHz, 312 bunches, 6.2 1010 e-/bunch,
156 ns Circumference
60% polarization
Laser Energy 590 mJ
Yield: 2.1 109 photons/turn/bunch
107 e+.turn/bunch
440 turn stacking in Pre-damping ring to get 4.2 10 9 positrons
Compton Linac option:
10 laser IP’s, 4 GeV linac with 5 nC/bunch,
(could we use the drive beam linac)
How realistic are 10 laser IP’s ?

## Slide 29: CLIC Compton schemes for polarized positron production
Not much done since 2010, ring scheme by Eugene et al., ERL scheme by Omori-san, Linac scheme studied as well
Stacking needed either in PDR or dedicated rings
Compton-ring was considered most promising
Difficult to judge how realistic the schemes are Any comments ?
How about direct conversion from polarized electrons as done by JLAB ? Any feelings ?
Conversion yield ~10-3, 1000 x times stacking ?
What would be optimized parameters

## Slide 30: Conclusions
Big effort to get the conceptual design of the CLIC main beam injectors, rather conceptual in many places but main problems studied and identified
General believe that the injectors are feasible and relatively conservative approaches are used
Obviously more work remains to be done

## Slide 31: Collaborations
Polarized electron source: SLAC, TJNAF
Positron source: KEK, LAL
Polarized positrons: KEK, LAL, ANL, CI, KIPT, Ankara University

## Slide 32: Linac Parameters and cost
Primary 5 GeV e- Linac
Injector Linac
Booster Linac
2 GHz
Pre-injector
e+ Linac
Pre-injector
e- Linac
e- DR
gun
PDR
e+ DR
DL’s
BC1
DC gun
target
9 GeV
2.86 GeV
0.2 GeV
PDR
Spin rotatator
LINAC | Energy Gain (MeV) | Bunch charge (10^9) | rf pulse length (ns) | Power per structure (MW) | Loaded gradient (MV/m) | Configuration (structure/2 klystrons) | No of rf modules | pulse compressor gain | No of structures | Length (m) | Energy gain per module (MeV) | Cost
e- pre-injector | 200 | 4.3 | 1300-1700 | 54 | 18 | 4 | 2 | 2.3-2.5 | 8.0 | 30 | 108 | 5830
e+ pre-injector | 200 | 11 | 1300-1700 | 56 | 15 | 4 | 3 | 2.3-2.5 | 9.0 | 40 | 90 | 8745
injector linac | 2660 | 6 | 3600-4000 | 44 | 15 | 2 | 60 | 1 | 119.0 | 300 | 45 | 127950
positron drive linac | 5000 | 11 | 1300-1700 | 56 | 15 | 4 | 56 | 2.3-2.5 | 223.0 | 400 | 90 | 163240
booster linac | 6140 | 4 | 1700-2000 | 53 | 16 | 4 | 64 | 2-2.3 | 256.0 | 473 | 96 | 186560

## Slide 33: Linac structure beam loading and power flow
Parameters:
tapered
f= 1998 MHz
L= 3 m
Pin= 77 MW
Nb= 624
N = 4.0 e9
Eacc = 15 MV/m