## Slide 1: STF-LLRF system and its study plan
Shin MICHIZONO (KEK)
Outline
STF system configuration
  S1-Global (~2011 Feb.)
  Quantum Beam (QB) (2012 Mar. ~)
Digital feedback system at STF (cPCI, uTCA, IF-Mix)
Performance of llrf system upto S1-global
Study plan during QB operation
  Beam based calibration
  PkQl control
  High Ql operation
  Other items

## Slide 2
(2010,2011)
No beam

## Slide 3: KEK STF Quantum Beam Project
Photo-cathode RF gun*
(5 MW Klystron on ground level)
800 kW klystron
with capture cryomodule (CCM)
including two superconducting
9-cell cavities*
Optical cavity for
X-ray creation
(not yet installed)
X-ray detector
Beam dump
*operated using digital LLRF
control techniques
Demonstration of high brightness X-ray generation
by inverse laser Compton scattering.
Pulse length: 1 ms
Repetition rate: 5 Hz
Bunch spacing: 162.5 MHz
Bunch number: 162500
Beam current: 10 mA
Energy: 40 MeV
Charge: 62 pC
(2012)
With beam

## Slide 4: Beam Operation of STF Accelerator
Beam length of 1 ms at RF gun
（March/2012）
Beam acceleration with 20% beam power
(40 MeV, 15 pC/bunch, 162500 bunches)
（June/2012）
⇒ Demonstration of ILC-like beam acceleration
(beam length: 1 ms, beam intensity: 3.2-6.5 mA)
1ms
Fiber Beam loss monitor
Beam on gate
BPM signal
PIN Beam loss monitor
1ms
BPM signal
Beam on gate
RF Gun
Capture cryomodule

## Slide 5: STF-LLRF system and its study plan
Shin MICHIZONO (KEK)
Outline
STF system configuration
  S1-Global (~2011 Feb.)
  Quantum Beam (QB) (2012 Mar. ~)
Digital feedback system at STF (cPCI, uTCA, IF-Mix)
Performance of llrf system upto S1-global
Study plan during QB operation
  Beam based calibration
  PkQl control
  High Ql operation
  Other items

## Slide 6: cPCI digital FB system (2007~)
cPCI system has been used from STF-1 (2007~).
FPGA board is a daughter card of a commercial DSP board.
ADC-inputs
(Multi-connector)
I,Q DAC outputs
cPCI crate
10ch 16-bit ADC (LTC2208)
2ch 14-bit DACs (AD9764)
CPU
board
Digital
I/O board
FPGA digital
FB board
FPGA
FB calc.
FPGA
Complex calc. like derivation of QL
Data communication
DSP

## Slide 7: Micro-TCA digital FB system (2011~)
16-bit ADC x 4
(LTC2208)
Clock input
16-bit DAC x 4(AD9783)
DIO
RF gate
AMC(Advanced Mezzanine Card)
FPGA
Virtex5-FX
The board has been developed for cERL-project (CW operation) at KEK.
For DRFS, the logic was changed for pulse operation.
MCH
uTCA1
(for KLY#1)
uTCA2
(for KLY#2)
Power Module
Data communication is performed through Gb Ethernet bus at the backplane.
EPICS was installed in the digital board for communication control.
EPICS: Experimental Physics and Industrial Control System
Shelf
uTCA system is a new system developed for cERL and is used from 2011.
FPGA board is a inteligent EPICS-IOC.

## Slide 8: STF-LLRF system and its study plan
Shin MICHIZONO (KEK)
Outline
STF system configuration
  S1-Global (~2011 Feb.)
  Quantum Beam (QB) (2012 Mar. ~)
Digital feedback system at STF (cPCI, uTCA, IF-Mix)
Performance of llrf system upto S1-global
Study plan during QB operation
  Beam based calibration
  PkQl control
  High Ql operation
  Other items

## Slide 9: Stabilities at 26 MV/m operation
0.0067%rms（in amplitude),16.5mdeg.rms(in phase) @690～1590us
By T. Matsumoto

## Slide 10: IF mixture
The number of ADCs in a FPGA board is limited due to the substrate. The idea is based on the ‘digital radio’ and obtaining cavity signals with a ADC.
Mixture of two signals decrease the resolution of analog signals but averaging increases the resolution.
Example of 3 signal IF-mix
Vector sum stabilities
⊿A/A：7×10^-4(rms)
⊿φ：0.06deg.(rms)

## Slide 11: STF-LLRF system and its study plan
Shin MICHIZONO (KEK)
Outline
STF system configuration
  S1-Global (~2011 Feb.)
  Quantum Beam (QB) (2012 Mar. ~)
Digital feedback system at STF (cPCI, uTCA, IF-Mix)
Performance of llrf system upto S1-global
Study plan during QB operation
  Beam based calibration
  PkQl control
  High Ql operation
  Other items

## Slide 12: Beam based calibration
Mathieu OMET | 9回日本加速器学会年会 | The 9th Annual Meeting of Particle Accelerator Society of Japan | 2012/08/10 | 12
Scan phase shifter and observe beam loading

## Slide 13: PkQl control
In case of the Pk-Ql control near the quench limit condition, the values of Pks and Qls are calculated as followings.
Select operational gradient of each cavity (Vcav)
Find out the Pk and Ql of each cavity under the specific beam current (Ibeam) and injection timing (Tinj).
PkQl control at FLASH

## Slide 14: High Ql operation
ilc operation requires high Q operation (Ql 6e6~1e7)
It is difficult to examine at FLASH because of the limitation of Qls (some of them are max. 3e6) and fixed Pks.
In KEK, we can change Qls ~1e7 and variable Pks.
PkQl control at high Qls will be possible (same to ilc spec.)
Ql
Gradient

## Slide 15: Other itmes (off-line studies)
Detuning monitor with beam
Beam based rf correction
RF gun pick-up calibration (directivity compensation)