## Slide 1: An Accurate Model of Beam Ion instability & its application to ILC DR and SPEAR3*
Lanfa Wang, M. Pivi, T. O. Raubenheimer and J. Safranek
LCWS2012
Arlington, Texas, USA
October 22-26.
*Submitted to Phys. Rev. ST Accel. Beams

## Slide 2: Contents
Brief Review of observations
Brief Review of FII theory
Our model
Application to ILC Damping ring and SPEAR3
Summary

## Slide 3: Introduction
Ions generated by beam-gas ionization
Ions are trapped along the electron-bunch train;
The ions created by the head of the bunch train perturb the bunches that follow.
Occur in rings, linacs or beam transport lines;
Broad-band spectrum
Normally only in vertical direction due to the small vertical beam size

## Slide 4: Observations-Beam Size Blow-up
C. J. Bocchetta, et. al. 1994
ELETTRA
The instability has been observed at many laboratories when vacuum is not good
    Artificially increasing the vacuum pressure (ALS, PLS, ATF)
    At commissioing times or restart after a long shutdown (ESRF, DIAMOND,…)
    After installation of new (insertion device) chambers (SPring-8, ESRF, …)
KEK ATF
Notes: - Mostly when the vacuum was temporarily not good:

## Slide 5: Observations---Coupled bunch instability
ALS
ALS y~30m
Dual sweep streak camera image of a bunch train
(M. Kwon et al., Phys. Rev. E57 (1998) 6016)
(J. Byrd et al., PRL, 79 (1997) 79)
Beam spectrum at different beam current

## Slide 6: FII at SSRF with nominal vacuum (Bocheng Jiang, et. al. NIMA 614, 2010)
Single bunch train with bunch Number 450, 37.5% gap (0.54s)
Beam current: 200mA
Vertical emiittance: 27.3pm
Horizontal emittance 3.9nm

## Slide 7: FII@SPEAR3
Beam spectrum at 200 mA with a single bunch train filling pattern
Measured vertical amplitude along
the bunch train (200mA)
Small vertical oscillation (~10 µm) has been observed when a single bunch train beam filling pattern is used

## Slide 8: Main Parameters of SPEAR3 and the ILC DTC02 damping Ring
Physics | Symbol/Unit | SPEAR3 | ILC DTC damping ring
Beam Energy | E0 [GeV] | 3 | 5
Circumference | C [m] | 234 | 3238.76
Horizontal Emittance | x [nm] | 10 | 0.637
Vertical Emittance | y [pm] | 14 | 2
Beam Current | I [mA] | 200-500 | 389/779
Bunch Number | M | 280 | 1312/2625
Harmonic Number | h | 372 | 7022
Bunch Spacing | ns | 2.1 | 6.2/3.1
RF Frequency | fRF [MHz] | 476.315 | 650
Revolution Frequency | f0 [MHz] | 1.280 | 0.09
Tune | nx / ny / ns | 14.1/6.18/0.01 | 48.36/27.22/ 0.03
Momentum Compaction Factor |  | 1.610-3 | 3.3610-4
Energy Spread | e | 9.810-4 | 1.010-3
Bunch Length | l [mm] | 6 | 6
Radiation Damping Time | x /y /z [ms] | 4.0/5.3/3.2 | 22/22/11
Total Vacuum Pressure | P [nTorr] | 0.1~0.5 | 0.5

## Slide 9
Parameter | KCS | DRFS | FP upgrade
Energy[GeV] | 5.0 | 5.0 | 5.0
Circumference[m] | 3238.76 | 3238.76 | 3238.76
Emittance ex/ey [pm] | 637/2 | 637/2 | 637/2
Harmonic number | 7022 | 7022 | 7022
Number of bunches | 1312 | 1312 | 2625
Beam current[mA] | 389 | 389 | 779
Bunch spacing [RF] | 4 | 4 | 2
Beam Filling period | 19 | 14 | 29
Fill pattern (1period) |  |  | 
Train [bunch number] | 34 | 22 | 44
Gap [in RF] | 45 | 33 | 31
Train [bunch number] | 34 | 22 | 45
Gap [in RF] | 49 | 33 | 31
Train [bunch number] |  | 22 | 
Gap [in RF] |  | 33 | 
 |  | 23 | 
 |  | 33 | 
Bunch length[mm] | 6 | 6 | 6
Energy spread, sd | 1 x 10-3 | 1 x 10-3 | 1 x 10-3
Mom. compaction, a | 3.36 x 10-4 | 3.36 x 10-4 | 3.36 x 10-4
Tunes, nx / ny / ns | 48.36 /27.22 /0.03 | 48.36/27.22/ 0.03 | 48.36/27.22 /0.03
Damp times tx /ty /ts [ms] | 22 / 22 / 11 | 22 / 22 / 11 | 22 / 22 / 11
E loss/turn, U0 [MeV] | 4.87 | 4.87 | 4.87
RF voltage, VRF [MV] | 12.83 | 12.83 | 12.83
Beam filing patterns of ILC DTC02 damping ring

## Slide 10: Summary of beam-ion instability Theory
Growth rate is proportional to the ion density and Q of the wake!!
FII (single bunch train with long gap)
(Gennady Stupakov, KEK Proceedings 96-6)
Uniform/Multi-bunch-train filling (Includes both nonlinear space charge and optics)
(T. O. Raubenheimer and Frank Zimmermann, PRE,51,5487,1995)
Nonlinear regime (nonlinear space charge regime)
(I)
(III)
(IV)
Quasi-exponential growth (linear force)
Exponential growth (Linear space charge + Optics with large frequency spread)
(S. Heifets, PEP-II AP note, 95-20)
(II)
(E. Kim and K. Ohmi, Japanese Journal of Applied Physics 48 (2009) 086501)
Exponential growth (includes nonlinear space charge force)
(L. Wang, et. al. PRSTAB 14, 084401, 2011)
(only when time is small?)
Can we include all effects together?
Nonlinear space charge;
Arbitrary Beam optics;
Arbitrary Multiple gas species vacuum

## Slide 11: Our method: Wake function
The nonlinear space charge force is included. The Q of the wake represents the nonlinearity of the E-force. Typically, it is below 10.
The wake has good linearity when the bunch offset is smaller than the beam size where the fastest instability occurs
E-field of ion cloud
Comparison with analysis
(L. Wang, et. al. PRSTAB 14, 084401, 2011)

## Slide 12: Effects of Optics & multiple gas species
Ion frequency along the ILC damping ring with the KCS beam
Beam size varies along the ring, this frequency spread due to optics provide damping to the instability. How to accurately model it?
There are multiple gas species in the real vacuum. Does the superposition rule apply?

## Slide 13: Wake and impedance with arbitrary Optics and Vacuum
Ion Frequency:
The total wake function of ions along the whole ring
A is the mass number of ion; so the wake is ion species dependent.
SPEA3R
ILC DR

## Slide 14: Impedance of ion cloud
A
B
C
A
A
C
B
B
Impedance provides a rich source of information:
Easy to know the contributions from individual gas species and also from ions at different location along the accelerator.
Instability growth rate is directly related to impedance(next page)
Impedance of ion cloud in ILC DR with KCS configuration. The total pressure is 0.5nTorr.
The partial pressure is 48%, 5%, 16%,14% and 17% for H2, CH4, H2O, CO and CO2 gas,
respectively.

## Slide 15: Analysis Beam ion instability in ILC DR
The unstable modes driven by various types of ions for the ILC KCS (Left) and FP upgrade (right) configuration. The total vacuum pressure is 0.5 nTorr
KCS
FP upgrade
When the beam is evenly filled along the ring, the coherent frequency shift for mode number µ is
Damping effect of H2 ion on the most unstable modes

## Slide 16: Simulation of FII in ILC DR
Simulated vertical beam ion instability in the ILC damping ring with KCS configuration: 3D plot (a) and 2D plot (b) of the growth of vertical amplitude; growth of unstable modes(c) Total pressure 0.5nTorr
The fastest exponential growth times for the three configurations shown in Table are 0.61 ms, 0.91 ms and 0.40 ms, respectively. Again the simulations agree with our analyses (0.89ms, 1.2ms, 0.7ms)
Simulation is done with PIC code (L. Wang, et. al. PRSTAB 14, 084401, 2011)
The simulation is expensive , >100 CPU hrs

## Slide 17: FII at ILC DR with DCT04
Simulated vertical beam ion instability with DCT04 lattice for various beam configurations
The optics of DCT is recently updated. There is a smaller vertical emittance of 1.2pm in DCT04 design compared with 2pm as in DCT02. Therefore the growth time becomes shorter: they are 0.59ms, 0.80ms and 0.29 ms for KCS, DRFS and FP upgrade beam, respectively (SLAC-PUB-15268)

## Slide 18: Beam filling patter effect@SPEAR3
Observation
Multiple bunch train can mitigate the beam ion instability with high intensity beam by reducing the ion density (Theory and simulation, see L. Wang, et. al. PRSTAB 14, 084401, 2011)

## Slide 19: Mitigation with Chromaticity
Observed oscillation amplitude of beam’s vertical lower sidebands with varying vertical chromaticity in SPEAR3.
Calculated growth rate of the beam ion instability in SPEAR3 at different chromaticity, P=0.37nTorr. 1tr

## Slide 20: Chromaticity effect
damping effect of chromaticity to the beam ion instability in SPEAR3 and the ILC damping ring. The vertical axis is the normalized growth rate
Chromaticity is more effective for machines with low momentum compaction factor, small ring and long bunch length

## Slide 21: Comparison of the damping effect of nonlinear space charge force and beam optics
The real part of the impedance (a) and growth rate of beam ion instability (b) in ILC damping ring with KCS configuration for various effects
In SPEAR3, the two damping effects are similar
In ILC, beam optics provides stronger damping

## Slide 22: Summary
We analyze the multi-bunch train beam ion instabilities with arbitrary beam optics, multi-gas species vacuum, nonlinear space charge force and realistic beam filling pattern together. All these factors provide damping to the instability.
Our analyses agree well with expensive simulation, and the observations in SPEAR3.
It is critical to use multiple gas species….
Both beam optics and nonlinear space charge provide strong damping effect to the instability;
A large chromaticity can mitigate the instability at the expense of reduced lifetime

## Slide 23: Acknowledge
Thanks the SPEAR3 team for its great help on the SPEAR3 observations
Thanks the organizers of the working group on Damping Rings :
David Rubin
Yannis Papaphilippou
Junji Urakawa
etc..
Thank You!