## Slide 1: Summary of Calorimetry/Muon Sessions
Burak Bilki
University of Iowa
Argonne National Laboratory

## Slide 2
Calorimetry Requirements
Jet energy resolution ( ) ≤ 3.5 – 5 % for jet energies ~ 1 TeV – 50 GeV
Excellent e/γ ID
Low noise, fit inside the coil, radiation hard (for forward calorimeters)
Precision timing (~1 ns) needed for CLIC
Conventional  Novel
Two major methods
Dual Readout Calorimetry: Imaging/PFA Calorimetry:
Different hardware concepts under beam test Has large scale prototypes with ~ established principles
J. Incandela
C. Gatto

## Slide 3
SiD SciW-ECal
GEM
SPiDeR DECAL w/MAPS
Micromegas
CALICE RPC SDHCal
CALICE RPC DHCal
Experiments:
CALICE SiW-ECal
CALICE W-Scintillator HCAL
CALICE SciW-ECal
Common Features:
Fine granularity
Embedded front-end electronics

## Slide 4
2nd Generation Prototypes:
~ Realistic dimensions (partly equipped)
Technological solutions for the final detector
Calice AHCAL
Calice SiW ECAL
K. Kruger
T. Frisson

## Slide 5
Overall Achievements
A lot of data – Successful test beams at FNAL, CERN and DESY; 100Ms of events
300 GeV π in W-DHCAL
SDHCAL
SiW-ECAL
Comparison with MC and testing the reliability of detector simulations.
Immediately accessible after/during test beam  Excellent understanding of the calorimeters!
Very beautiful images.
W-AHCAL
W-DHCAL
J. Repond
V. Boudry
T. Frisson
F. Sefkow
J. Repond

## Slide 6
In addition to PFA, software compensation is also possible
Particle ID and separation
Utilization of multiple thresholds (very preliminary)
SiW ECAL + Fe - AHCAL
SDHCAL
Fe - AHCAL
SDHCAL
F. Sefkow
V. Boudry
Local compensation: re-weighting based on single cell energy density
Global compensation: correction factor calculated on event-by-event basis

## Slide 7
Precision Timing for CLIC
CALICE T3B
Measure the time structure of the signal within hadron showers
w/ W - AHCAL
w/ W - AHCAL
w/ W - AHCAL
F. Simon

## Slide 8
Forward Calorimetry SiD Muon Detector
Radiation damage studies underway.
SiD Muon Detector Baseline Design
Large planar modules ~ 5.54m X 3.8m ~ 21m2.
Si avalanche photo-diodes-pixelated photon det.
Common electronics: KPiX.
E. Fisk
W. Lohmann

## Slide 9
Conclusions and Outlook
Several projects at different stages of prototyping.
Full scale beam test series completed for all major technologies.
First test beam results from 2nd generation prototypes addressing integration issues available.
Viability of PFAs and imaging calorimetry not questioned anymore.
No expectation of breakthrough in basic principles and technology in the near future.
BUT, the calorimeters already started to produce unprecedented physics results well before collider detector integration.