CLIC FFS overview
 R. Tomas
O. Blanco, H. Garcia, A. Jeremie,
Y. Levinsen, D. Popescu,Y. Renier

---
Contents
- CLIC 3 TeV FFS fully characterized in CDR
- New philosophy for the 350 GeV FFS:
  - New optimization at 350 GeV with lower betax
  - Compatibility with ILC FFS:
    - Tolerances
    - QD0
  - ATF2 as common ILC-CLIC R&D ground
- Tools development:
  - Synchrotron radiation optimization tools
  - Parallel Mapclass2 with new functionalities
  - Evaluation of Solenoid induced luminosity loss

---
CLIC 500 GeV CDR parameters

---
Redefining IP beta functions: Total luminosity
Computing luminosity with ideal distributions versus beta functions

---
Redefining IP beta functions: Luminosity in the energy peak
See Hector's talk on Thursday
Optimum betay between 0.06-0.08mm
Concerning betax we have to explore 4mm & lower

---
Using CLIC FFS lattice for ILC?
- CLIC lattice can also operate at ILC parameters with similar performance (Hector's talk on Thursday)
- Hardware aspects are under investigation (Michele Modena's talk on Thursday)

---
ILC + ATF2 tolerances

---
ILC tolerances with CLIC-based FFS
Dy_static
CLIC-based tolerances similar or more relaxed than for the current ILC lattice

---
ILC-CLIC low-E parameters
- ILC CM energies are 250 and 500 GeV
- CLIC is 350 GeV
- This poses extra constrains in a common path
- Higgs mass is well known now, how come the target energies are not the same?
- CLIC detector is OK with 18-20mrad crossing angle, why ILC needs 14mrad?

---
CLIC QD0 prototype
- Compact
- Robust (no SC coil vibration)
- Demonstrated technology
- Should ILC take it?
- See Michele's presentation on Thursday

---
ATF2
- Great progress
- Need to think on new challenging R&D goals
- To serve both for CLIC and ILC
Kubo

---
Andrea Jeremie & Yves Renier

---
Ultra-low beta* and new QD0 based on CLIC technology?
- Current QD0 is OK for nominal ATF2 optics
- For ultra-low beta* there are 3 options:
  - Increase beta_x → σy = 23 nm
  - Replace QD0 → σy = 26 nm
  - New! 2 new octupoles→ σy = 23 nm
- See Eduardo Marin's talk on Wednesday

---
SR effects
4d
- Analytical estimates of SR in MAPCLASS
- Allow to optimize lattice including SR
- Allow to compare to tracking codes
- PLACET 6D SR option proves more accurate than the previously default 4D.
6d
Oscar Blanco

---
MAPCLASS upgrades
- Parallelization limited by load imbalance
- Turning libraries to C++
- New features

---
Field quality tolerances, e.g. QF1
See Yngve's talk
On Thursday
ILC and CLIC have similarly challenging tolerances for skew components in QF1

---
Solenoid luminosity loss evaluation
See Yngve's talk
On Thursday
Automatic procedures to determine luminosity loss from solenoid+SR

---
Summary & outlook
- A new CLIC-ILC path with a common FFS seems possible, but not obstacle free:
  - QD0 technology
  - Design energies, crossing angles
- ATF2: the excelent playground for both projects
- CLIC is redesigning low energy with probably more pushed IP parameters:
  - Parameter optimization
  - Tools development: MAPCLASS, SR, solenoid, etc