W-DHCAL Digitization
T. Frisson, C. Grefe (CERN)
CALICE Collaboration Meeting at Argonne

---
DHCAL prototype
Active element: Thin Resistive Plate Chambers (RPC)
- Glass as resistive plates (~1 mm)
- single 1.15 mm thick gas gap
- 1x1 cm² pads
- digital readout:
1 bit discriminator per pad/channel
Timestamp (100 ns time resolution)
1 layer:
- 3 RPCs (32 x 96 cm²)
⇒ 96x96 pads = 9216 pads
DHCAL: 54 layers
- main stack: 39 layers with tungsten absorber
- 10 mm thick W plate
- tail catcher:
- 8 layers with steel absorber (25.4 mm thick)
- 7 layers with steel absorber (100 mm thick)
⇒ ~500'000 channels
Active element: Thin Resistive Plate Chambers (RPC)
- Glass as resistive plates (~1,1 mm)
- single 1.15 mm thick gas gap
- 1x1 cm² pads
- digital readout: 1 bit per pad/channel
1 layer:
- 3 RPCs (32 x 96 cm²)
⇒ 96x96 pads = 9216 pads
DHCAL: 54 layers
- main stack: 39 layers with tungsten absorber
- 10 mm thick W plate
- tail catcher: 15 layers with steel absorber
- 8 steel plates
==> ~500'000 channels
Active element: Thin Resistive Plate Chambers (RPC)
- Glass as resistive plates (~1,1 mm)
- single 1.15 mm thick gas gap
- 1x1 cm² pads
- digital readout: 1 bit per pad/channel
1 layer:
- 3 RPCs (32 x 96 cm²)
⇒ 96x96 pads = 9216 pads
DHCAL: 54 layers
- main stack: 39 layers with tungsten absorber
- 10 mm thick W plate
- tail catcher: 15 layers with steel absorber
- 8 steel plates
==> ~500'000 channels

---
Simulation
S. Arfaoui (CERN)
- RPC cassette contents, layout, and sensitive detector description from steel DHCAL simulation
- Octogonal tungsten absorbers + support from W-AHCAL simulation
- Beam instrumentation (scintillators, Cerenkov counters,
and Wire Chambers) from W-AHCAL simulation
- Only the main stack is included in the simulation
→ only 39 layers in the next slides
- Beam profile	→ 5 cm width Gaussian
→ 30 mrad angular spread
- Secondary particle production cut → 5 m
Simulation

---
Digitization
Re-implementation of RPCSim as a Marlin Processor
- Intro : RPCSim
- Strategy for tuning RPCSim
- Event Selection
- Results

---
Charge generation
- Collect all energy deposits from Mokka
→ avalanche starting points
- Charge generation parametrized from data taken with analog RPC
→ The charge is randomly generated from distribution
→ Shift applied to charge distribution to accommodate possible differences
in the operating point of RPCs Q0 (Qe = Q – Q0)
→ Correct in average:
- Do not take into account the distance of the ionization from anode
- Ignore higher ionization probabilities of non-MIP particles
- Local inefficiencies
→ avalanche depletes electric field and	prevents secondary avalanches within a small radius
→ apply a distance cut dcut :
- One point of a pair of points randomly discarded if closer than dcut
- To be tune with e+/- data
dcut

---
Charge spread
- Charge distributed in the XY plane :
→ Several spread models
→ Need to determine charge integral for each individual pad (MC method)
- Pre-calculated look up table
- Take into account symmetry
→ Tune spread model parameters with MIPs :
- S1 : Slope of the exponential decrease of charge induced in the readout plane
- S2 : Slope of 2nd exponential, to improve the description of the tail
- r : Relative contribution of the 2 exponentials
- Apply trigger threshold

---
Strategy for tuning RPCSim
50 GeV gamma → EM shower
1)
- Select 'pure' MIPs (muons without secondary EM showers)
- Tune spread and trigger threshold parameters
→ Minimization using 'Nhits per layer' distribution
→ 10'000 events per parameter set (~30 min)
→ Huge parameter space
- Select all muons
- Tune dcut and Q0 parameters
→ plan: Q0 in the previous step, e- for dcut
- Check with electron and pions data
To do : Tune parameters in clean regions (see Christian's talk)
Z (mm)
2)
3)
X (mm)

---
Event selection
Preselection :
→ Filter box events, dead RPC modules, noisy/dead channels/ASICs
→ Remove duplicate hits (same position, different timestamps)
Reconstruction
→ Remove out-of-time hits: only keep events in a 300 ns window
→ Nearest neighbor clustering of adjacent cells
→ Hough transform based track reconstruction
(not the most efficient in this case but useful for forthcoming studies)
Final selection
→ Ntracks = 1
→ Ncluster > 15
→ pure MIP muons : remove events with 2 consecutive layers with Nhits > 9
To do :
Slope less than 3 degrees
180 GeV μ

---
Parenthesis about Hough transform
300 GeV pions
Black = clusters not linked to a track
1 color per track
Track of the pion before hadronic interaction
Same event
← all clusters
Only track clusters →

---
Digitizer tuning with muons
Run 660356 – 180 GeV μ
Data
Simulation
Data
Simulation
Tail seems OK
Core is not well reproduced
S1	0.4 mm
S2	4 mm
r	2%
TT	0.012
dcut	1.8 mm
Q0	0.2 pC
Data
Simulation
To do:	- needs further improvements
- compare parameter values with Steel-DHCAL digitization

---
First look at pions
Preselection :
→ Filter box events, dead RPC modules, noisy/dead channels/ASICs
→ Remove duplicate hits (same position, different timestamps)
Reconstruction
→ Remove out-of-time hits: only keep events in a 300 ns window
→ Nearest neighbor clustering of adjacent cells
Final selection
→ interaction layer < 15
→ nHits > 20
→ hit density > 3
→ at least 20 layers with hits
Run 660259 – 80 GeV π
Data
Simulation
Data
Simulation
NOTE : This result seems too good, probably some mistakes are hidden somewhere

---
Summary and outlook
Re-implementation of RPCSim as Marlin processor
Digitizer parameters are tuned with muons
→ ongoing work
→ prediction for electrons and pions
→ First results look promising
Finalize Mokka model including beam line instrumentation
→ Need to include local effects in simulation / digitization
- eﬀects of ﬁshing lines and borders (already implemented in Mokka)
- local eﬃciencies are crucial for data–Monte Carlo comparison

---
Back up

---
Test beam setup (2012)
PS (2 weeks)
- 1 – 10 GeV/c
- electrons, pions, protons
- RPC rate capability OK
 - Data taking with ~500 triggers/spill
SPS (4 weeks)
 - 10 – 300 GeV/c
 - electrons, pions
 - RPC rate capability problem → running with limited rate: 250 – 500 triggers/spill
 ~ 30 million events recorded
Three wire chambers → beam profile
Two Cerenkov counters for particle ID
10 x 10 cm² scintillator triggers (30 x 30 cm² for dedicated muon runs)

---
Data quality
Box events:
- box shaped pattern in individual layers
- hits created along boundary of front end board
H. Holmestad (CERN, University of Oslo)
Dead RPC modules:
Noisy and dead cells:
Noisy and dead ASICs:
⇒ Taken away from the data

---
Reconstruction
Remove duplicate hits (same position, different timestamps)
Remove out-of-time hits: only keep events in a 300 ns window
Nearest neighbor clustering of adjacent cells
300 ns