What We Discuss in the Morning Session
Masao KURIKI (Hiroshima University)

---
The morning session
CFS + Source G joint session.
  - Radiation Environment of Target and Photon Dump Area by A. Ushakov and P. Sievers
  - Target Maintenance Scenarios by M. Kuriki
  - Current CFS Design of Positron Source Area by M. Miyahara
Source WG I
  - Target Maintenance Scenario by T. Okugi
  - Target Maintenance Scenario by P. Sievers
  - Window and Dump for the ILC-Photon Beam by P. Sievers
  - Photon Dump Design in TDR by M. Kuriki

---
ILC Positron source schematic with key components
Undulator ILC Positron source
147m active undulator length, additional 73.5m is reserved
for the polarization upgrade.
500m drift space between the undulator and target.
NC RF up to 400 MeV for capturing.
SC RF up to 5 GeV
Energy Compressor
Spin rotator (SC solenoid)

---
- Thicker Ti window > 0.2mm lead excessive temperature rise after each pulse.
- 12 bar pressurized Water Dump is not compatible because the window is too thin.
- The lifetime regarding to the radiation damage (<0.5DPA) is also a big problem.
- The photon-dump design is re-considered from scratch.

---
Tumbling Window
- Double wall thin windows cooled by He gas.
- Tumbling to mitigate the radiation damage of Ti window.
- He Flow 17 g/s.
- Tumbling ± 25mm makes 1/32 radiation damage.

---
- To avoid any strong pressure and temperature gradient on the thin Ti window, the dump are is not filled with a pressurized water.
- Instead, bunch of water flow channels.

---
Proposal by Jia Xuejun (TDR)

---
Proposal by T. Okugi

---
Proposal by Peter Sievers

---
Target Maintenance Scenarios Summary
- TDR scenario is the most matured, but it is not optimized from the facility point of view.
- We have to fix the boundary conditions for
  - How many used target should be stored to,
  - Where?
  - How long?
  - What is the installation and extraction path?
Once we have fix the conditions, we are able to make the design including the maintenance scenario.