Summary of PosiPol2016
Masao KURIKI (Hiroshima University)

---
PosiPol2016
- 11th PosiPol WS
- 22 participants(16 EU, 1 US, 5 Japan) + online
- 2016/9/16-18 @ LAL-Orsay
- Laser Compton : 6
- E-Driven : 9
- Undulator : 7
- Other : 2

---
Active Sliding Contact Cooling Demo Conceptual Illustration
W. Liu
- Rotating 1meter diameter Target Wheel at 2000 rpm (100 m/s) while extracting ~10kW by using active sliding contact cooling.
- Target wheel is driven by a magnetically coupled drive motor which separates the motor from the vacuum.
- Stability of wheel controlled by heavy duty machine spindle.
- Temperature of wheel controlled by 4 Active Sliding Contact Cooling Pads with luburicant.
- Cooling Pad’s temperature controlled by water/coolant.
- Heat applied to wheel using UHV radiant filament heaters.
Full Size Target Wheel Ready for Operations in Vacuum

---
Cooling Demonstration in Air
stage	heater	Cooling pads	dT/dt (oc/s)		Estimated cooling /heating power (W)
			Upstream	Downstream	Upstream	Downstream
1	Off	Removed	9.36E-05	2.29E-05	---	---
2	Off	Applied	-1.51E-04	-2.83E-04	-14.6	-27.4
3	On, medium	Removed	1.17E-03	1.38E-03	113.5	133.8
4	On, medium	Applied	4.18E-04	4.40E-04	-72.9(equivalent)	-91.2(equivalent)
5	On, medium	Removed	1.26E-03	1.41E-03	122.2	136.7
6	On, medium	Applied	2.26E-04	2.51E-04	-100.3(equivalent)	-112.4(equivalent)
7	On, medium	Removed	1.01E-03	1.24E-03	97.8	120.2
8	On, medium	Applied	-3.73E-04	-4.66E-04	-36.2(net)	-45.2(net)
9	Off	Applied	-1.16E-03	-1.32E-03	-112.5	-128.0

---
e+ target for Ecm = 250 … 500GeV
Cooling of the ILC e+ target by thermal radiation
S. Riemann
Ecm and luminosity determine energy deposition in target
Ø = 1m; 2000rpm, 0.4X0 Ti6Al4V (Pe+ ≤30%)
Edep ≤ 7kW  cooling by thermal radiation is an option
Ebeam [GeV]	Edep [kW]	DTmax/pulse [K]	dpa	Edep [kW]	DTmax/pulse [K]
	Nominal luminosity			High luminosity
120	5.0	66	0.035	-	-
175 (ILC EDMS)	3.9	125	0.06	-	-
250 (ILC EDMS)	2.0	130		4.1	195
250	2.3	85	0.05	4.6	128
A. Ushakov,
 2015
A. Ushakov,
Update 2015

---
Radiative cooling model
Rotating wheel consists of Ti rim (e+ target) and Cu (radiator)
Heat path:
thermal conduction Ti  Cu
Thermal radiation from Cu to stationary water cooled coolers
Target, radiator and cooler are in vacuum
Radiating area is adjusted by fins
Goal:
keep target temperature below limit for failure of Ti6Al4V
Reliable fatigue limit at elevated temperatures?
Felix Dietrich
Ti6Al4V
Cooler (Cu)
photons

---
Target Material Test at MAMI, Mainz
A. Ignatenko

---
Thermomechanicle Examination :F. Dietrich