## Slide 1: The ILC BDC Final Focus: 250 GeV option(s).
Dr. Larisa Malysheva
Oxford University

## Slide 2: ILC BDS lattice status and changes
Push-pull operation decks (A. Seryi)
3 version for different L*:
L*=3.51m, L*=4.5m, L*=4.0m
Optics was not tuned
Beta_x=15mm, bet_y=40mm (500GeV) option
Dipoles were not decimated.
New IP parameters (see table on next slide)
Operation for low energy ( possibility of swithing part of final doublet)

## Slide 3: The ILC new set of IP parameters)
 | Centre-of-mass energy | Ecm | GeV | 200 | 230 | 250 | 350 | 500
 | Beam energy | Ebeam | GeV | 100 | 115 | 125 | 175 | 250
 | Lorentz factor | g |  | ####### | ####### | ####### | ####### | #######
 | Collision rate | frep | Hz | 5 | 5 | 5 | 5 | 5
 | Electron linac rate | flinac | Hz | 10 | 10 | 10 | 5 | 5
 | Number of bunches | nb |  | 1312 | 1312 | 1312 | 1312 | 1312
 | Positron bunch population | N+ | ×1010 | 2.0 | 2.0 | 2.0 | 2.0 | 2.0
 | RMS bunch length | sz | mm | 0.3 | 0.3 | 0.3 | 0.3 | 0.3
 | Electron RMS energy spread | Dp/p | % | 0.206 | 0.194 | 0.190 | 0.158 | 0.125
 | Positron RMS energy spread | Dp/p | % | 0.187 | 0.163 | 0.150 | 0.100 | 0.070
 | Horizontal emittance | gex | mm | 10 | 10 | 10 | 10 | 10
 | Vertical emittance | gey | nm | 35 | 35 | 35 | 35 | 35
 | IP horizontal beta function | bx* | mm | 16.0 | 14.0 | 13.0 | 16.0 | 11.0
 | IP vertical beta function (no TF) | by* | mm | 0.34 | 0.38 | 0.41 | 0.34 | 0.48
 | IP vertical beta function (TF) | by* | mm | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
 | IP RMS horizontal beam size | sx* | nm | 904 | 789 | 729 | 684 | 474
 | IP RMS veritcal beam size (no TF) | sy* | nm | 7.8 | 7.7 | 7.7 | 5.9 | 5.9

## Slide 4: Low energy (125 GeV) beam option.
MAPCLASS code based on MAD-X PTC was chosen ( R.Tomas )
Use 2 version of optics: L*=3.51m and L*=4.05m
Rematch the linear optics to the new IP parameters.
Second and higher order aberrations tuning
Decimate dipoles (keep space reserved)
Check the possibility of Half QD0/QF1 operation

## Slide 5: v.351LD0_135D1B (old version)
Original plot ( Dx=-1.735x10-3 !)
βx = 0.015 ;
βy =0.00040; Dx=-1.73528e-02
Corresponding beam sizes:
sx1 =3.39e-06
sy1 =7.57e-09

## Slide 6: v.351LD0_135D1B ( new IP parameters)
Used QDO, Qf1, QD2A,Qf3, QD6,Qf5,QD4, QD2B + matching quads+ Sextupoles
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6
sx/sx0 | 1 | 1.0222 | 1.0601 | 1.0723 | 1.0466 | 1.0225
sy/sy0 | 1 | 1.0119 | 1.0785 | 1.1542 | 1.1268 | 1.1084
sx/sx0_dp=0 | 1 | 1.0048 | 1.0071 | 1.007 | 1.0064 | 1.0069
sy/sy0_dp=0 | 1 | 1.0027 | 1.0066 | 1.0223 | 1.0233 | 1.0236
Beam size up to maximum order considered
sx,y / s0x,y
Corresponding beam sizes:
sx1 =7.36e-07
sy1 =7.66e-09
sx2 =7.55e-07
`sy2 =7.75e-09
sx3 =7.83e-07
`sy3 =8.26e-09 .
sx4 =7.92e-07
`sy4 =8.41e-09
.
sx5 =7.73e-07 sx6 =7.72e-07
sy5 =8.63e-09 sy6 =8.58e-09
βx = 0013 ;
βy =0.00041; Dx=-6.25e-05;
αx =O(e-09);
αy =O(e-09);

## Slide 7: v.450LD0_205D1B –new optics
Used QDO, Qf1, QD2A,Qf3, QD6,Qf5,QD4, QD2B + matching quads to rematch to new Twiss
Used QDO, Qf1, QD2A,Qf3, QD6,Qf5,QD4, QD2B + sextupoles
βx = 0.01300000001 ;
βy =0.000410000219;
αx = O(e-010); αy =O(e-9)
Dx =O(e-6);0
Corresponding beam sizes:
sx1 =7.29e-07
sy1 =7.66e-09
sx2 =7.41e-07
`sy2 =7.78e-09
sx3 =7.521e-0
`sy3 =8.01e-09 .
sx4 =7.67e-07
`sy4 =8.72e-09
.
sx5 =7.54e-07
`sy5 =8.52e-09

## Slide 8: v.450LD0_2055D1B-new optics
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6
sx/sx0 | 1 | 1.0315 | 1.0493 | 1.0534 | 1.0342 | 1.0329
sy/sy0 | 1 | 1.0158 | 1.0458 | 1.1294 | 1.1046 | 1.0994 | 1.1033
sx/sx0_dp=0 | 1 | 1.0205 | 1.0219 | 1.0068 | 1.005 | 1.0068
sy/sy0_dp=0 | 1 | 0.99358 | 0.99358 | 0.99358 | 0.99358 | 0.99489
Corresponding beam sizes:
sx1 =7.29e-07
sy1 =7.66e-09
sx2 =7.41e-07
`sy2 =7.78e-09
sx3 =7.521e-0
`sy3 =8.01e-09 .
sx4 =7.67e-07
`sy4 =8.72e-09
.
sx5 =7.54e-07
`sy5 =8.52e-09

## Slide 9: 500 GeV CoM final doublet (orig.)

## Slide 10: 250 Gev CoM Half of FD is off
Replaced by drifts
Re-matched with
slight variation of QD0 and QF1
KQD0:=-0.30059( was -0.3046)
KQF1:= 0.11861 (was 0.14470)

## Slide 11: v.351LD0_135D1B (Half-quads)
Used QDO, Qf1, QD2A,Qf3, QD6,Qf5,QD4, QD2B + QF7,QD8,QD10, QF9+matching quads+ sextupoles
βx = 0.013;
βy =0.0004100; αx = 4e-05;
αy =-1.5e-09; Dx =O(e-5);
Corresponding beam sizes:
sx1 =7.30e-07
sy1 =7.69e-09
sx2 =7.67e-07
`sy2 =7.78e-09
sx3 =7.86e-0
`sy3 =7.88e-09 .
sx4 =8.74e-07
`sy4 =9.19e-09
.
sx5 =8.58e-07
`sy5 =9.09.e-09

## Slide 12: v.351LD0_135D1B-new optics ( Half FD Quads)
Corresponding beam sizes:
sx1 =7.30e-07
sy1 =7.69e-09
sx2 =7.67e-07
`sy2 =7.78e-09
sx3 =7.86e-0
`sy3 =7.88e-09 .
sx4 =8.74e-07
`sy4 =9.19e-09
.
sx5 =8.58e-07
`sy5 =9.09.e-09
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6
sy/sy0 | 1 | 1.0169 | 1.0294 | 1.1999 | 1.1873 | 1.1876
sx/sx0 | 1 | 1.0501 | 1.0768 | 1.1928 | 1.1749 | 1.1738
sx/sx0_dp=0 | 1 | 1.0008 | 1.0036 | 1.0833 | 1.0836 | 1.0826
sy/sy0_dp=0 | 1 | 1.0047 | 1.014 | 1.0694 | 1.0692 | 1.0679
Used QDO, Qf1, QD2A,Qf3, QD6,Qf5,QD4, QD2B + QF7,QD8,QD10, QF9+matching quads+ Sextupoles

## Slide 13: Decimation of dipoles
Replaced and checked that all the matching is still valid
New version of beamlines available.
“So, for 250 GeV only two of these BS1 will be installed (i.e. one, 2.4 m long magnet) and other four 2.4 m long magnets will be installed in corresponding in ...SPACE at 500 GeV beam. The total angle at both 250 GeV and 500 GeV remains the same, so the footprint of the BDS does not change but dipoles are weaker at 500 GeV to keep the SR low.”
from D. Angal-Kalinin
Used the replacement “anzatz” from
B. List.

## Slide 14: v.351LD0_135D1B-new optics ( Half FD Quads )-1
Chart: 
| 1 | 2 | 3 | 4
sx/sx0 | 1 | 1.0121 | 1.0233 | 1.0582
sy/sy0 | 1 | 1.0308 | 1.0367 | 1.1266
sx/sx0_dp=0 | 1 | 1.0051 | 1.0059 | 1.0035
sy/sy0_dp=0 | 1 | 1.015 | 1.0196 | 1.0186
Corresponding beam sizes:
sx1 =7.30e-07
sy1 =7.66e-09
sx2 =7.39e-07
`sy2 =7.90e-09
sx3 =7.48e-07
`sy3 =7.93e-09 .
sx4 =7.73e-07
`sy4 =8.63e-09
Beam size up to maximum order considered
sx,y / s0x,y

## Slide 15: Conclusions/plans
R. Tomas’s code was tasted for Linear collider
250 Gev CoM lattice v.351LD0_304D1B with new IP parameters, new bending section and with half QD0/QF1 is ready
v. 450D0_205D1B with new IP parameters, new bending section is ready
v. 450D0_205D1B with half of QD0/QF1 requires more tuning
Tracking through lattices obtained (should be done