## Slide 1: CTF3 Results R. Corsini for the CTF3 Team & the CLIC Collaboration
OUTLINE:
Short introduction to CTF3
Feasibility studies
  Drive beam generation
  Deceleration and RF power production
  Two-Beam acceleration
    (Conceptual Design Report)
Timelines and program for the coming years
Conclusions

## Slide 2: CLIC Layout at 3 TeV
Drive Beam Generation Complex
Main Beam Generation Complex
140 ms train length - 24  24 sub-pulses
4.2 A - 2.4 GeV – 60 cm between bunches
240 ns
24 pulses – 101 A – 2.5 cm between bunches
240 ns
5.8 ms
Drive beam time structure - initial
Drive beam time structure - final

## Slide 3
Drive beam scheme
Detector (experimental conditions)
Luminosity
Operation and Machine Protection System (robustness)
Main linac gradient
Accelerating structure
Drive beam generation
PETS (power extraction and transfer structures)
Two beam acceleration
Drive beam deceleration
Main beam emittance generation, preservation and focusing
Alignment and stabilisation
CTF3
(CTF3)
(CTF3)
(CTF3)
CLIC Feasibility Benchmarks

## Slide 4
CLIC Test Facility (CTF3)
High current, full
beam-loading operation
Operation of isochronous lines and rings
Bunch phase coding
Beam recombination and current multiplication by RF deflectors
12 GHz power generation by drive beam deceleration
High-gradient two-beam acceleration
4 A, 1.4us
120 MeV
30 A, 140 ns
120 MeV
30 A, 140 ns
60 MeV

## Slide 5
Drive Beam Generation
SiC load
damping
slot
10 m
RF pulse at output
RF pulse at structure input
95.3% RF to beam efficiency
Stable high current acceleration
Current stability
Isochronicity, phase coding
Factor 8 current & frequency multiplication
Pulse charge measurement
Full beam loading acceleration
Factor 8 combination
Most RF power
to beam
High beam current
RF in
No RF to load
“short” structure – low Ohmic losses

## Slide 6
Beam recombination
Fast bunch phase switch in SHB system
Operation of isochronous rings and beam lines
6 ns
Drive Beam Generation

## Slide 7
333 ps
Streak camera images of the beam, illustrating the bunch combination process in the ring
t
x
83 ps
Drive Beam Generation

## Slide 8
Beam recombination
Factor 4 - OK
Factor 8
  basic principle demonstrated
  Still need some improvement (stability, emittance)
Beam recombination - Emittance
Best results in CLEX
for factor 4: eH= 250 um eV= 140 um
for factor 8: eH= 550 um eV= 170 um
Different turns are ~ ok, no unknown effects
Emittance increase due to non perfect orbit
Drive Beam Generation

## Slide 9
Repeatibility and long term current stability improved
Pulse charge stability at end of the linac better than CLIC requirements
P [MW]
RF power feedback, MKS 13
Time [h:m]
Feedback on
Feedback off
Feedback on
Several feed-back loops operational, for temperature, RF phase and power and gun current.
5 10-4
1 10-3
Charge stability – Factor 4
18th November 2011
3 to 4 10-3
S [m]
CLIC requirement
Drive Beam Stability

## Slide 10
Two-Beam Test Stand
(TBTS) Layout
The Two-Beam Test Stand (TBTS)
PETS – Power Extraction & Transfer Structure
Two-Beam Test Stand in CLEX
PETS tank
Structure tank

## Slide 11
PETS operated routinely above 200 MW peak RF power
providing reliably pulses ~ 100 MW peak to accelerating structure.
About twice the power needed to demonstrate 100 MV/m acceleration in a two-beam experiment with TD24 structure.
t [ns]
135 MW
CLIC target
Two-Beam Test Stand
(TBTS) Layout
Power production in TBTS

## Slide 12
Demonstration of PETS of-off mechanism
Considered a feasibility issue
Ability to:
  Switch off power from individual PETS to accelerating structure in case of breakdown
  Reduce substantially power in PETS, to cope with PETS breakdowns
PETS on-off principle fully tested
Conditioned at high power
(135 MW - nominal) by recirculation
PETS , forward RF
ON
OFF
Simulation vs. experiment
Spectra
comparison
TBTS – PETS On-off mechanism

## Slide 13
TD24
Maximum stable probe beam acceleration measured: 31 MeV
 Corresponding to a gradient of 145 MV/m
Two-Beam Acceleration demonstration in TBTS
Up to 145 MV/m measured gradient
Good agreement with expectations (power vs. gradient)
CLIC Nominal, loaded
CLIC Nominal, unloaded
Drive beam ON
Drive beam OFF
Two-Beam Acceleration

## Slide 14
TBTS layout
Breakdown kick studies
  Uppsala
  University

## Slide 15
2011 run
Limited amount of events
Using only screen
2012 run
Many events, larger statistics
Using BPMs and screen
Time resolution
Subtraction of systematic effects
Analysis ongoing, but basically confirming 2011 results
Breakdown kick studies
  Uppsala
  University

## Slide 16
Histogram of number of pulses between breakdowns, showing the presence of clusters.
BD count evolution shows several period of intense BDs activity: clusters
Inside clusters the BD probability becomes very high.
Discarding clusters, good fit by a Poisson law as in low BD rate regime
Breakdown physics & statistics
  CEA-Dapnia & Uppsala University

## Slide 17
Breakdown physics & statistics
Measurement of intensity and energy distribution of electrons/ions produced during a break-down event
  Uppsala
  University

## Slide 18
13 Power Extraction & Transfer Structures (PETS)
installed and running in 2012
(9 PETS in 2011)
Full beam transport to end-of-line spectrometer, stable beam
Power produced (70 MW/PETS) fully consistent with drive beam current (21 A) and measured deceleration.
PETS tank during installation
TBL line in CLEX
More than half a GW of 12 GHz power!
Beam deceleration, measured in spectrometer and compared with expectations
~ 30 MeV
26%
Test Beam Line
end 2011

## Slide 19
Test Beam Line
2012: Reached 30% deceleration
Potential to exceed 40%

## Slide 20
Conclusion of our CDR studies
Two-beam scheme
Drive Beam generation fully tested
Nominal parameters for RF production reached and exceeded
Deceleration as expected
Used to accelerate test beam - 150 MV/m gradient measured with beam
Improvements on operation, reliability, losses
More deceleration and improvements on drive beam quality expected this year
Feasibility of the CLIC Two-Beam scheme has been established in the CLIC Test Facility CTF3

## Slide 21
CLIC project time-line

## Slide 22
Drive Beam phase feed-forward tests
Phase monitor
  Not just a single experiment – series of related studies:
  Measure phase and energy jitter, identify sources, devise & implement cures, extrapolate to CLIC
  Show principle of CLIC fast feed-forward
Fast kickers
CLIC drive beam phase feed-forward concept
  Close link to collaborating partners:
  INFN-LNF: Phase monitors, stripline kickers
  Oxford University/JAI: feedback electronics, amplifiers
CTF3 - Phase feed-forward
Phase stability 2.5° @ 12GHz
0.2° @ 1GHz
Phase stability 0.2° @ 12GHz
FONT5 board
(Oxford)
Stripline kicker (INFN-LNF)

## Slide 23
  Phase monitor tests – 2 monitors installed in summer 2012
  First system tests planned in summer 2013
Cable hole
Beam direction
Feed-forward tests in CTF3
Test starting in 1-2 weeks
Phase monitor
(INF-LNF, EuCARD)

## Slide 24
CLEX
LINAC
DELAY LOOP
COMBINER RING
BL - BDR experiment
From X-band klystron
X-band structure TD24
X-band components
1 A, 240 ns pulse from CTF3 linac
G. Riddone, A. Solodko
Beam loading reduces field locally in the structure ⇨ is it the break-down rate lower (or higher)?
CLEX probe beam has only limited current/pulse length, CLEX Drive beam has limited rep rate
⇨ use CTF3 drive beam and klystron driven X-band structure
Reactivate the old ‘30 GHz PETS’ line, 1 A DB current, can reach 50 Hz
Measure BDR with/without beam to get a direct comparison
Present schedule: Install in winter shutdown 2012-2013
Run experiment in 2013
Experiment on the effect of Beam-Loading on BD rate

## Slide 25
Upgrade TBL to a test facility relevant for future CLIC program
12 GHz power production for structure conditioning
  Working experience with a real decelerator
  Beam dynamics studies, pulse shaping, feedbacks, etc
Timeline:
Last batch of PETS will be adapted to high-power testing (using internal recirculation)
One (or two slots) tested at beginning of 2013
Gradual increase of slots to 4-8 slots and rep rate to 25-50 Hz
PETS tank
Accelerating structure under test
Beam
RF
S. Doebert
Improved PETS design, mini-tank + input coupler
Evolution of TBL

## Slide 26
Two-Beam Modules
Next Step: Installation and test of full-fledged Two-Beam Modules in CLEX
First module in development, installation end 2013
Three modules in 2014-2016
Ongoing: Fabrication of 4 modules to be mechanically tested in laboratory

## Slide 27
3D model of integration of
the first CLIC Module in CLEX (2013)
CLEX - Three two-beam modules
(2014)
TBTS PETS tank
Module T0
Present schedule:
First module installation end 2013
(At least one year of testing)
Module string installation end 2014
Drive Beam line
Main Beam line
Two-Beam Modules

## Slide 28
Beam loading/BDR
experiment
Two-Beam Modules, Wake-field monitors, Two-beam studies
RF pulse shaping
Power production,
high-power testing,
RF conditioning with DB & further decelerator tests
Phase feed-forward,
DB quality,
DB stability studies
Consolidation, energy upgrade,
Increased rep-rate
CLIC Diagnostics tests
CTF3 program in 2012-2017

## Slide 29
Feasibility of the CLIC Two-Beam scheme has been established in the CLIC Test Facility CTF3
Original experimental program basically completed
Drive Beam generation demonstrated – emittance and stability shall be further improved this year
Nominal parameters for RF production & two-beam acceleration reached and exceeded – 150 MV/m gradient measured with beam
Deceleration by 30% of a 20 A beam of the drive beam with no losses, expect > 40% this year
CTF3 experimental program for the next five years established and under way
Drive beam phase feed-forward experiment
Beam loading / breakdown experiment
High-power testing of structures in TBL
Full fledged two-beam modules tested with beam in CLEX
CONCLUSIONS

## Slide 30
Current CLIC & CTF3 Collaboration
Gazi Universities (Turkey)
Helsinki Institute of Physics (Finland)
IAP (Russia)
IAP NASU (Ukraine)
IHEP (China)
INFN / LNF (Italy)
Instituto de Fisica Corpuscular (Spain)
IRFU / Saclay (France)
Jefferson Lab (USA)
John Adams Institute/Oxford (UK)
Joint Institute for Power and Nuclear Research SOSNY /Minsk (Belarus)
PSI (Switzerland)
RAL (UK)
RRCAT / Indore (India)
SLAC (USA)
Sincrotrone Trieste/ELETTRA (Italy)
Thrace University (Greece)
Tsinghua University (China)
University of Oslo (Norway)
University of Vigo (Spain)
Uppsala University (Sweden)
UCSC SCIPP (USA)
ACAS (Australia)
Aarhus University (Denmark)
Ankara University (Turkey)
Argonne National Laboratory (USA)
Athens University (Greece)
BINP (Russia)
CERN
CIEMAT (Spain)
Cockcroft Institute (UK)
ETH Zurich (Switzerland)
FNAL (USA)
John Adams Institute/RHUL (UK)
JINR (Russia)
Karlsruhe University (Germany)
KEK (Japan)
LAL / Orsay (France)
LAPP / ESIA (France)
NIKHEF/Amsterdam (Netherland)
NCP (Pakistan)
North-West. Univ. Illinois (USA)
Patras University (Greece)
Polytech. Univ. of Catalonia (Spain)
CLIC multi-lateral collaboration - 44 Institutes from 22 countries
MANY THANKS TO ALL COLLABORATION MEMBERS!