## Slide 1
Application of laser-plasma accelerators to future linear colliders
Work supported by the U.S. DOE, Office of Science, Office of High Energy Physics, under Contract No. DE-AC02-05CH11231
Carl Schroeder, C. Benedetti, J. Osterhoff, K. Nakamura, E. Esarey
Lawrence Berkeley National Laboratory
Wednesday July 10, 2024
University of Tokyo, Japan

## Slide 2
Outline
Laser-plasma accelerators (LPAs) produce ultra-high field gradients (~1-100 GV/m), accelerating ultra-short bunches (~1-10 micron)
LPA-based collider design (10 TeV CM):
  High gradient collider linacs (geo. gradient ~1TeV/km)
  High charge/bunch, maximize L/P
Example of LPA stage for plasma-based linac
  High efficiency with beam quality preservation
Laser driver characteristics for collider application
  R&D toward high average power laser drivers based on coherent combination of fiber lasers
Intense laser (red) drives a density wave (blue to yellow) in plasma, electrons (white) are trapped and accelerated with fields of order 10 GeV/m
WarpX

## Slide 3
Plasma accelerator, laser driver, and accelerated beam characteristics set by plasma density
Laser energy:
Pulse duration:
Accelerating gradient:
Charge/bunch:
Energy gain:
Accelerator length limited by laser energy depletion:
Lower plasma density yields higher energy beams; requires more laser energy.
Laser depletion (and high gradient) necessitates LPA staging to reach high energy.
Plasma density choice determines required laser parameters; in practice, available laser (with laser energy/pulse and wavelength) determines plasma density
Schroeder et al. PRL (2011); Benedetti et al PRE (2015)
laser propagation direction
C. Benedetti
~ plasma wavelength, λp

## Slide 4
Higher energy beams requires staging plasma accelerators
In laser-driven plasma accelerator: (energy gain) ~1/(plasma density)
For resonant plasma wake excitation: (laser energy) ~ λp3 ~(plasma density)3/2
Beam Energy gain [GeV]
Laser energy [J]
Gradient [GV/m]
Once driver energy is depleted, new driver must be coupled into plasma

## Slide 5
Interstage coupling determined by e-beam not laser driver
LPA stage
LPA stage
laser
plasma
mirror
e-beam
focusing
e-beam
Lc, e-beam
Space required for laser coupling Lc, laser determined by laser intensity @ plasma mirror (Ipm~1016 W/cm2); for example Lc, laser = 0.2 m @ n=1017 cm-3
Determined by focusing gradient and beam energy  Lc, e-beam ~ (energy)1/2 , for fixed gradient
Beam energy [TeV]
Lc, laser = 0.2 m
@ n=1017 cm-3
Lc, e-beam (assuming ideal active plasma lens w/ gradient 2000 T/m)
Coupling distance [m]
Lc, laser
Inter-stage distance grows as energy increases

## Slide 6
Minimizing linac length (“construction cost”)
Staged LPAs:
Advantage of laser-drivers: compact driver coupling with plasma mirrors
Lc, interstage coupling distance
LINAC length [km] (to 5 TeV)
Operational plasma density [cm-3]
<Lc> = 5 m

## Slide 7
Operating density determines required laser driver
High density: higher gradient (reduced linac length, reduced construction costs) and low charge/bunch (reduced L/P, increased operation costs)
Low density: Lower gradient (increased linac length, increased construction costs) and high charge/bunch (increased L/P, reduced operation costs)
Beamstrahlung may limit charge/bunch for e+/e- collider
          Operating density range: ~ 1017 cm-3
          Laser technology requirements:
          Laser energy/pulse ~ 1-100 J
          Rep rate ~ 1-10s kHz
          Average laser power ~100kW
Operational plasma density [cm-3]
UL[J]
f[kHz]
Laser bandwidth:
Luminosity / Power
[1034cm-2s-1 / 100MW]
@ 10 TeV CoM
assuming ε2 =104 nm2
Pavg[kW]
Laser wavelength λ=1µm

## Slide 8
Example LPA stage for laser-plasma-based linac
Laser: U=50 J, λ0=1.0 um, a0=4.5, T0=80 fs, w0=36 mm
Plasma: n0= 3.4x1017 cm-3, stage length = 3.1 cm, linear taper (+74%)
ΔWbunch= 3.1 GeV (~100 GV/m)
Qbunch= 1.2 nC, Lbunch =9.3 um, Energy spread = 0.1%
Wake-to-bunch energy transfer = 43%
Laser driver depletion = 20%
325 stages/TeV
Schroeder et al. J. Inst. (2022)

## Slide 9
Emittance growth by Coulomb scattering in plasma
Scattering of beam on background ions leads to emittance growth
Final beam energy [TeV]
Normalized emittance growth [nm]
Emittance growth (very) weakly dependent on plasma density (reduction in density or targets compensated by increase length to achieve target energy, reduction in focusing force)
Strong focusing suppress emittance growth
Ez/E0 =0.5
Sub-nm normalized emittance growth from scattering with plasma for TeV-scale collider
Schroeder et al. Phys. Plasmas (2013)

## Slide 10
Synchrotron radiation in plasma linacs
Energy spread growth linearly proportional to emittance (betatron amplitude):
Final beam energy [TeV]
Wiggler/betatron period:
Wiggler strength parameter:
n=1017 cm-3
Energy spread induced by synchrotron radiation from plasma betatron motion (assuming low-emittance matched beam) sub-%
Schroeder et al. JINST (2022)
100nm
Fraction of beam power rad.
10nm
Rel. energy spread

## Slide 11
Hosing instability must be suppressed
Hosing (aka BBU): exponential growth of beam centroid displacement (misalignment) owing to coupling transverse beam-driven wake (beamloading) of beam head to beam tail
  results in emittance growth and beam loss.
  transverse (focusing) wakefield ~ longitudinal (accelerating) wakefield in plasma accelerators
  since wakefields are large (>GV/m), hosing can be severe in plasma accelerators
  High beam loading (efficiency) = large long. wakefield = large trans. wakefield = loss of stability
Whittum et al., PRL (1991)
Schroeder et al., PRL (1999)
Huang, et al., PRL (2007)
Lehe et al., PRL (2017)
Mehrling Phys. Plasmas (2018)
Lindstrom et al., PRL (2018)
Lebedev et al., PRAB (2017)
centroid displacement:
number of betatron periods
beam length
R. Lehe

## Slide 12
Ion motion mitigates hosing instability growth
Stability to hosing/BBU achieved via BNS damping:
  Requires large (~10%) energy chirp, owing to strong beam loading
  large chirps have transport challenges
Stability also achieved with head-to-tail density variation
  Naturally created by ion motion
Centroid displacement
Normalized emittance
Propagation distance
Stable beams may be efficiently accelerated in plasma accelerators with emittance preservation with proper matching
Mehrling, Benedetti, Schroeder et al., PRL (2018)
Hosing suppressed
emittance preserved

## Slide 13
Ion motion couples horizontal/vertical:
Emittance growth for flat beams
Transverse wakefields with ion motion
Coupled nonlinearity:
enables x-y coupling and emittance growth
Benedetti, Schroeder et al. PRAB 2017
Diederichs,…Schroeder, Thevenet, arXiv 2023; submitted to PRL

## Slide 14
Laser technology R&D required for collider
Present ~10sJ-class Ti:Sa laser systems operate at 1-10Hz (~10-100W average power), with low efficiency (quantum defect fundamentally limits efficiency for Ti:Sa laser systems: 532 nm pumping / 800 nm lasing; ~33% thermal loss)
Collider application will require ~100kW average power with >30% efficiency
  Promising emerging laser architectures
  Tm:YLF (λ=1.9µm), R&D at LLNL
  Coherent combination of fiber lasers (λ=1µm), R&D at LBNL, Michigan, Jena
    potential for highest efficiency (~50%)
    1µm (minimize # of accelerator stages)
    monolithic design for robustness, serviceability, etc.
NSF OPAL (Rochester, planned; OPCPA)
MEC-U (SLAC, planned; glass)
Can not address collider needs
~100kW
~100TW
> 30% effic.
collider requirements
technically
feasible
(available
near-term)
peak laser power [TW]
average laser power [kW]
ZEUS (Michigan)
L3-HAPLS (ELI-BL)
CoReLS (Korea)
BELLA (LBNL)
existing
laser
systems
Ti:Sa perf. ceiling (quantum defect, cooling)
KALDERA (DESY) – Ti:Sa, planned
~30 mJ
fiber lasers
fibers scalable, efficient
J-class kHz systems kBELLA (LBNL) – fiber, planned
coherent combination
Laser tech path for collider

## Slide 15
Coherent combing of fiber lasers path to high average power
power
amplifiers
l1
spatial
combiners
temporal
stackers
spectral
combiners
pulse compressor
stretchers and
pre-amplifiers
spectral
splitter
l2
l3
output
oscillator
…
Concept: Use high efficiency, high average power fiber lasers, and add them coherently for high pulse energy
Combine 100’s fibers spatially x 100 pulses temporally for collider energy needs
  Stack 100 pulses in 1 fiber to get >10mJ, sub-kW
  Combine 100’s fibers to get Joules, 100’s kW
  Relies on control of laser phase of each pulse
Yb-doped fibers:
diode pump at 976 nm , lase at 1030 nm
Large surface/vol. ratio = excellent thermal energy handling
total efficiency wall-to-laser of ~40-50%:
- electrical-to-optical of diode pumped lasers = 60%
- optical-to-optical of fibers = 90%
- combining fibers = 85%
Achieved to-date:
81 pulses stacked temporally (>10 mJ)
Spatially combined 8, 100fs beams (90% efficiency)
3 channels spectrally combine to 42 fs
Next step: 27 spatial beams, 81 temporal pulses, 3 spectral bands (200mJ, 1kW)

## Slide 16
Conclusions
Linacs based on staging plasma accelerators: ~1 TeV/km geo. gradient
  Proper beamloading and tapering: low energy spread (0.1%), high efficiency (>40%), high gradient
  Minimal emittance growth (<nm) owing to scattering in plasma (due to strong focusing)
  Synchrotron emission low (dE/E~10-3 ) for collider-relevant emittances (<100nm)
  Hosing suppressed via coherent ion motion
  Ion motion results in horizontal-vertical coupling and round beams
Laser-plasma-based collider:
  Positron acceleration is a challenge, requires R&D and demonstrations of new concepts
  Gamma-gamma (or e-e-) colliders are promising option with demonstrated wakefield technology
    Scattering using 0.33um (~10J laser) with 5TeV beam, yields x~300>>4.82
  Collider sub-systems (BDS, damping, injector, etc.) require development
High average power laser system R&D required
  coherent combination of fiber lasers promising path to high average, high peak power, and high efficiency short-pulse lasers