## Slide 1: ILC Damping Ring Design: Changes from TDR
2024.7.10 K. Kubo

## Slide 2: Change of ILC DR Design from TDR
For Higher Luminosity (especially at 250 GeV ECM)
  Normalized horizontal emittance 6.3 um  4 um
(Already reported and approved)
e.g. Presentation in ALCW2018 (https://agenda.linearcollider.org/event/7826/sessions/4644/#20180531)
Make Design Realistic
  Change positions and lengths of magnets

## Slide 3
TDR
Changes keep
Same beamline geometry
Basically the same optics

## Slide 4: Horizontal emittance design (normalized)
TDR
At IP: 10 um
In DR: 6.3 um
Growth in RTML: 0.9 um (designed synchrotron radiation)
New
At IP: 5 um
In DR: 4 um
Growth in RTML: 0.7 um (designed synchrotron radiation)
(by changing turnaround design)

## Slide 5
Possible choices for emittance reduction
Stronger focusing (smaller beta-function) in arcs
  Dynamic aperture significantly reduce.
    Probably not acceptable.
Longer and weaker bending magnets
  Space exist for lengthening magnet from 3m (TDR) to 5 m
  Simple and easy
  No negative impact to dynamic aperture
  This is chosen
+ In Wiggler dominant ring (as ILC DR):
emittance ~ 1/(radius)^2 in arc
damping time not changed significantly

## Slide 6: Optics of Arc Cell
TDR, 3 m bend
5 m bend
 | TDR | New (long bend)
Horizontal normalized Emittance (um) wo/w intra-beam scattering | 5.74, 6.27 (IBS) | 3.14, 3.97 (IBS)
Damping time x/y/z (ms) | 23.9/23.9/11.9 | 25.5/25.5/12.8

## Slide 7: Dynamic Aperture calculation
Tool prepared in SAD
Set initial orbit and energy deviation and perform tracking
Survived in 1000 turns tracking  “accepted”
No errors included.
No special treatment of wiggler’s magnetic field.

## Slide 8: Dynamic aperture
TDR design 3 m bend
New arc cell: long (5 m) bend
Aperture is larger than requirement

## Slide 9: Additional Changes after ALCW2018
Realistic Design (consideration of construction, transportation, etc.)
Insert spaces between magnets
Divide one 5 m bend into two 2.4 m bends
Arc Optics Design in 2018
Present Arc Optics Design

## Slide 10: Additional Changes after ALCW2018 cnt’d
Basically the same optics
  Dynamic aperture checked. No significant change.
Reduction of total bend magnets length
  emittance increase slightly, not significant
Horizontal normalized emittance
Bend | No intra-beam scattering | With intra-beam scattering (nm)
5 m | m | m
2.4 m+ 2.4 m | m | m
Bend | No intra-beam scattering | 
5 m |  | 
2.4 m+ 2.4 m |  | 

## Slide 11: SUMMARY
Longer and weaker bending magnet for lower horizontal emittance
Divide long bending magnet into two
(5 m  2. 4 m + 2.4 m).
Spaces between magnets
Same beamline geometry
Basically the same optics
Changes give no negative effect to dynamic aperture
(However, more realistic estimation of dynamic aperture is desirable.)