## Slide 1: Positron source for CEPC
环形正负电子对撞机
Circular Electron Positron Collider
Xiaoping Li, Cai Meng, Jingru Zhang, Zhe Duan, Jindong Liu, Jie Gao

## Slide 2
Parameters and layout of the CEPC Linac
Positron source for CEPC
  Electron beam for positron production
  Positron generation and Pre-acceleration
  R&D of key components for positron source
Other sources related research activities
Summary
Content

## Slide 3
Parameters and layout of the CEPC Linac
Positron source for CEPC
  Electron beam for positron production
  Positron generation and Pre-acceleration
  R&D of key components for positron source
Other sources related research activities
Summary
Content

## Slide 4
Parameter | Symbol | Unit | Baseline
Energy | Ee-/Ee+ | GeV | 30
Repetition rate | frep | Hz | 100
Bunch number per pulse |  |  | 1 or 2
Bunch charge |  | nC | 1.5 (3)
Energy spread | σE |  | 1.5×10-3
Emittance | εr | nm | 6.5
Parameters and layout of the CEPC Linac
Baseline design of the CEPC Linac
  A 30GeV room temperature Linac
  A combination of S-Band (2860MHz) and C-Band (5720MHz)
  The Linac tunnel length is 1.8km

## Slide 5
Parameters and layout of the CEPC Linac
Layout of the CEPC Linac
  FAS+PSPAS+SAS：S-Band
  TAS：C-Band（Higher gradient  Shorter linac tunnel length）

## Slide 6
Parameters and layout of the CEPC Linac
Positron source for CEPC
  Electron beam for positron production
  Positron generation and Pre-acceleration
  R&D of key components for positron source
Other sources related research activities
Summary
Content

## Slide 7
Electron source and bunching system (Baseline)
  Electron Gun
    A traditional thermionic triode gun
    3nC for electron injection
    11nC for positron generation
  Bunching
    Two SHBs (158.89MHz/476.67MHz)
    Buncher(2860MHz)
    Accelerating structure (2860MHz)
  Energy: 50MeV
  Normalized Rms Emittance: 80mm-mrad
  Transmission
    90%
  Verified at BEPCII and HEPS Linac
Positron source for CEPC
Electron beam for positron production

## Slide 8
Acceleration: 50MeV4GeV
  18+3(redundancy) S-band klystron
  1 klystron 4 accelerating structures
  Gradient: 22MV/m
Simulation results
  Energy: 4GeV
  Bunch charge: 10nC
  Energy spread: 0.63%
Positron source for CEPC
Electron beam for positron production
10nC@4GeV electron beam for positron production

## Slide 9
Parameters and layout of the CEPC Linac
Positron source for CEPC
  Electron beam for positron production
  Positron generation and Pre-acceleration
  R&D of key components for positron source
Other sources related research activities
Summary
Content

## Slide 10
Positron source
  Target (Conventional)
    Electron beam: 10nC@4GeV
    Tungsten@15 mm
    Beam size: 0.5 mm
AMD (Adiabatic Matching Device)
  A flux concentrator
  Magnetic field: (5.5T0T) + 0.5T Solenoid
Capture & Pre-accelerating section
  1 klystron  2 accelerating structures
    Larger aperture S-band accelerating structure with aperture is 25 mm, gradient is 22 MV/m and length is 2 m
Chicane @ 200MeV
  Wasted electron separation
  Exit: ~5.5nC, Nor. Emittance: 2370mm-mrad
Positron source for CEPC
Positron source and Pre-acceleration
Notes: .

## Slide 11
Acceleration：200MeV1.1GeV
  8+1(redundancy) S-band klystron
  1 klystron 2 accelerating structures
    10 Larger aperture S-band accelerating structure@22MV/m
    8 normal S-band accelerating structure@27MV/m
Transverse focusing
  Triplet quadrupoles are outside of
  each accelerating structure
Simulation results
  Energy: 1.1GeV
  Energy spread: 0.4%
  Bunch charge: ~4.5nC
  Normalized rms Emittance: 2500mm-mrad
Positron source for CEPC
Positron source and Pre-acceleration

## Slide 12
Parameters and layout of the CEPC Linac
Positron source for CEPC
  Electron beam for positron production
  Positron generation and Pre-acceleration
  R&D of key components for positron source
Other sources related research activities
Summary
Content

## Slide 13
A flux concentrator prototype has been successfully developed
  Manufactured under a cooperation MOU with KEK
  A trumpet-shaped copper coils：12 turns
  The inner diameters：7 to 52 mm
  Coils distance: 0.2 mm
  Total length: 100 mm
  Peak current: 15A
  Max pulse magnetic field: >6T@15kA
Positron source for CEPC
R&D of key components for positron source
Notes: .

## Slide 14
A new pulse modulator has been developed for FC
  All-solid-state switching components IGCT instead of hydrogen thyratron (BEPC II)
  Obtained a higher peak current without high-frequency ripples
  Will be used for BEPCII operation this September
Parameters | Value
Input voltage | 380 V ±10%
Output pulse current | 15 kA
Pulse width | 5 μs
Output waveform | Half sine
Capacity peak voltage | 15 kV
Current stability | < 0.1%
Positron source for CEPC
R&D of key components for positron source
Notes: .

## Slide 15
Test results of the FC
  A test bench has been built up for performance verification of the FC
  The test results of FC agreed well with the designed parameters
  A peak magnetic field of 6.2 T had been obtained inside the FC at a 15kA driving current
  Can meet the requirements of CEPC positron source baseline design
Positron source for CEPC
R&D of key components for positron source
Notes: .

## Slide 16
Parameters and layout of the CEPC Linac
Positron source for CEPC
  Electron beam for positron production
  Positron generation and Pre-acceleration
  R&D of key components for positron source
Other sources related research activities
Summary
Content

## Slide 17
Other sources related research activities
A thermionic triode gun
  A prototype of electron gun and its test platform had been built up
    Used for domestic cathode-grid assembly R&D
    The cathode emission capacity had been tested up to 12A@150kV
    The emission capacity does not decrease within 7000 hours operation
Notes: .

## Slide 18
Other sources related research activities
A polarized electron source R&D plan
  Based on a 500kV photocathode dc-gun has been built up at PAPS, Huairou, Beijing
    Superlattice photocathodes R&D collaborating with a domestic company (Acken, Suzhou)
    Research on the polarization manipulation and measurement (Collaborate with JGU, Mainz)
    Two-stage experiments will be considered in near future (200kV/400kV)
Notes: .

## Slide 19
Other sources related research activities
A L-Band photocathode RF Gun
  A L-Band photocayhode RF Gun has been developed (Under processing now)
  Potential for generating high bunch charge electron beam (≥10nC）
    An alternative solution for the thermionic gun of CEPC Linac
    Avoiding additional frequency introduced by SHBs which lead to a complex timing system for CEPC
  Developed for PWFA experiment research on BEPCII (A project has been approved by CAS)
Parameters | Value | Unit
Frequency | 1299.48 | MHz
Cell | 1.55 | cell
Input power | 6.5 | MW
Q factor | 24291 | -
Gradient at cathode | 60 | MV/m
RF pulse length | 10 | μs
Notes: .

## Slide 20
Other sources related research activities
Polarized positron beam generation
  Preliminary consideration on a Compton Ring and a Stacking Ring for the generation of polarized e+ beams~1×1012e+/second
    A potential solution to generate polarized positrons in CEPC
    Up to now, just a conceptual consideration (requires a lot of further simulation works in future)
  Using the self-polarization to generate polarized e+ beams in DR
    Need a higher energy in DR around 2GeV and a strong dipole strength
    Current research shows that extracted beam polarization @ 10min ~ 44%
Very promising for resonant depolarization
Notes: .

## Slide 21
Parameters and layout of the CEPC Linac
Positron source for CEPC
  Electron beam for positron production
  Positron generation and Pre-acceleration
  R&D of key components for positron source
Other sources related research activities
Summary
Content

## Slide 22
Summary
The CEPC Linac is a 30 GeV room temperature S-band and C-Band combined linear accelerator working at 100Hz.
Positron source for CEPC adopting a conventional scheme.
A flux concentrator prototype and its pulse modulator has been developed and tested.
Other sources related research activities in IHEP are mentioned.

## Slide 23
Thank you for your attention!

## Slide 25: Introduction: CEPC Layout
CEPC as a Higgs (ttbar,H, W, Z) Factory
  Linac, 30GeV, 1.8km
  Full energy Booster, 100km
  Collider, 100 km
  Transport lines
Linac design
  Meet requirements
  High availability
  Reserve upgrade potential

## Slide 26: Introduction: Linac energy
The maximum energy of booster is 180GeV and circumference is 100 km
  Large circumference & Low injection energy  Low magnetic field
    design difficulty in magnet (field) and power supply (stability)
  Large extraction energy  Large field range
    design difficulty in magnet (excitation efficiency) and power supply (power)
Increasing the energy of the Linac is the easiest way: 30 GeV
Magnet |  | Low injection energy |  |  | Max. Extraction energy | Cost
 |  | 10GeV | 20GeV | 30GeV | 180GeV | 
CT Air-core coil |  | Yes | Yes | Yes | No | Very high
iron-corn magnet | oriented silicon steel sheet | No | Yes | Yes | Yes | high
 | Non-oriented silicon steel sheet | No | No | Yes | Yes | low
effect of residual magnetism
Wen Kang
Session M2-2: #1

## Slide 27: Positron Linac: TAS
Simulation results( including Wakefield & CSR)
Parameter | Unit | Value | Simulated | 
 |  |  | Positron | 
Beam energy | GeV | 30 | 30.50 | 30.01
Repetition rate | Hz | 100 | / | 
Bunch charge | nC | 1.5 | 1.5 | 3.0
Energy spread | 10-3 | 1.5 | 1.33 | 2.19
Emittance(x/y) | nm | 6.5 | 3.37/1.68 | 3.90/1.71
Bunch length (RMS) | mm | / | 0.4 | 0.4
@3nC

## Slide 28: Positron damping/polarizing ring
DR V4.0 | unpolarized e+ | polarized e+
Energy (Gev) | 1.983 | 
Circumference (m) | 144.2 | 
Number of trains | 2(4) | 
Number of bunches/trian | 1(2) | 
Total current (mA) | 12.4 | 
Dipole strength B0 (T) | 1.92 | 
U0 (kev/turn) | 397.9 | 
Damping time x/y/z (ms) | 4.8/4.8/2.4 | 
Momentum compaction | 0.0078 | 
Storage time | 20 ms | 10 min
0 (%) | 0.0917 | 
0 (mm.mrad) | 132 | 
injection z (mm) | 6 | 
Extract z (mm) | 6.7 | 6.6
inj (mm.mrad) | 2500 | 
ext x/y (mm.mrad) | 133/13 | 132/13
inj /ext (%) | 0.18 /0.092 | 
RF acceptance (%) | 1.85 | 
Longitudinal tune | 0.025 | 
Using the self-polarization to generate polarized e+ beams
  For Resonant depolarization (very promising)
    extracted beam polarization @ 10min ~ 44%
    No physics dead time, improved availability & int. luminosity
  for polarized colliding beams (under study)
    Higher energy and/or asymmetric wigglers
    More bunches

## Slide 29: 基于BEPCII，打造正电子加速、级联加速独特研究平台
BEPCII 2 GeV正负电子束流
针对正电子加速、尾场级联加速及外注入级联等关键科学挑战的研究需求，基于BEPCII高能正负电子束流，结合大电量电子驱动器，建设世界独有的束流驱动尾场加速研究平台

## Slide 30: 激光等离子加速器 + 储存环 test facility @ 河南