## Slide 1: ILC Beam Line Changes from TDR
LCWS2024 2024.7.10 K. Kubo

## Slide 2
This report is based on activities of the meetings
ILC Beamline Related to CFS (2019~)
Members:
Y. Enomoto, H. Hayano, K. Kubo, T. Okugi, T. Sanuki, N. Terunuma, K. Yokoya,

## Slide 3
IP
e- ML
e+ ML
Undulator
BDS
BDS
Virtical bend
Virtical bend
Longer turnaround
Longer turnaround
Shift Damping Ring
ML reserve space
ML reserve space
e- source
Undulator,
e+ source
E compress
E compress
Changes of beamlines from considerations of
CFS & beam dynamics

## Slide 4: Specify curved and flat regions
(Details are not described in TDR. )
Between end of e+ ML to end of e- ML, including undulator section for e+ production is in the same plane, which is horizontal at IP.
MLs are following earth’s curvature.
Insert vertical bends at ML ends and approximately same locations for return lines.
(0.58 mrad for e- ML and 0.40 mrad for e+ ML)
Returns lines are straight or curved, following the corresponding beamlines.
As a result, the elevation of e- ML is less than that of e+ ML by 43 cm.
IP
e- ML
e+ ML
Undulator
BDS
BDS

## Slide 5: Specify curved and flat regions (cont’d)
One alternative was putting the undulator in curved region, before the bending downstream of e- ML. However,
  Different angles of e+ source beamline and e- BDS. Complicated tunnel configuration.
It is desirable to make IP region horizontal for the physics detectors.
  Otherwise, if mid point of the straight region is horizontal, the inclination of the detector would be 0.064 mrad.
IP
e- ML
e+ ML
Undulator
BDS
BDS

## Slide 6: Main Linac reserved space
Downstream -> upstream
Length is adjusted to satisfy the timing constraint.
Same reserved length for e- and e+
(Already approved)
ML
ML
Reserved
Reserved
ML
ML
Reserved
Reserved
Old
New

## Slide 7
( L1 + L2 + L3 ) – L4 = n x CDR
Timing constraint
L1
L4
L2
L3
CDR
e+
e-
IP
e+ production
Each positron bunch (A) is injected in the same bucket of the bunch (B) which is collided with the electron bunch producing the bunch (A).
Or,
An electron bunch produces positron bunch (A), collides with positron bunch (B).
Then, (A) should be injected in the same bucket of the ring as the bunch (B)
Construction error will be corrected by
“timing adjusting chicane” located at the end of e+ 5 GeV booster linac.

## Slide 8
Turnaround

## Slide 9: Longer Turnaround
Problems of the original design:
Horizontal normalized Emittance growth 390nm (even larger number is in TDR, 480nm) is not acceptable for the new (250 GeV) design with lower horizontal emittance at collision.
Space between bending magnets is too tight. (0.7m)
Old parameters:
Horizontal normalized Emittance growth 390nm
Total length 274.9 m
New parameters:
Horizontal normalized Emittance growth: 175nm
Total length 353.18 m

## Slide 10
Longer Turnaround (cont’d)
Old
New
Arc Cell
Old parameters:
Bend length 2.3 m, bend angle 0.109 rad
Bend to bend space 0.7 m
New parameters:
Bend length 1.9 m, bend angle 0.082 rad.
Bend to bend space 1.1 m

## Slide 11
Undulator, e+ source

## Slide 12: e- beamline for e+ production (undulator, dogleg, e+ production target and photon dump)
Change total length of undulator from 147 to 231 m.
  Increase number of undulator magnets from 84 to 132 magnets (each is 175 cm long).
Move the undulators downstream by 168.8 m. Make the dogleg shorter accordingly.
---- For keeping the positron yield with 125 GeV electron beam energy, lower than TDR,
  Longer undulator is needed.
  Distance to the positron production target cannot be too long because of the increased production angle of photons due to the lower energy of electrons.
Note: Dogleg should be replaced with longer one when the beam energy is increased to 250 GeV

## Slide 13: e- beamline for e+ production (cont’d) (undulator, dogleg, e+ production target and photon dump)
Move photon dump farther from the positron production target.
--- For avoiding destruction of photon dump, transverse size of photon beam should be large, requiring larger distance from the target and the dump.
Move e+ production target downstream by 6.0 m. The positron capture section and the booster linac are also moved accordingly. (Distance from the undulator center to the target is 407.1 m)
--- For avoiding interference of target room shield and quadrupoles in e- BDS.
.

## Slide 14
 | TDR | New | Difference
BDS start to IP | 2241 | 2274 | 33
Undulator center to target | 559 | 401 | -158
Undulator end to BDS | 464.1 | 306.1 | -158
Dogleg bend to bend | 316.0 | 151.2 | -164.8
Undulator start to end | 317.9 | 317.9 | 0
Space befor undulator | 0 | 165 | 165
Undulator section start to BDS | 802.8 | 809.8 | 7.0
Comparison of TDR and new length (unit: m)

## Slide 15
Positron Source Beamline
Replace 125 MeV capture section by 400 MeV capture section
--- For better capture efficiency.
Shift beamline by 3.6 m, replacing chicane by dogleg
--- 3.6 m for making space of transporting cryomodules.
--- Dogleg for making space for the photon beam to its beam dump

## Slide 16
e- source

## Slide 17
Old e- source
New e- source
e+ ML
e+ BDS
Damping Ring
Electron Source Beamline
Move e- source upstream, close to the end of e+ ML.
Long beam transfer line is inserted between the booster linac and LTR line.
--- For
  Reducing LHe transfer line length
  Avoiding interference with collimators in BDS.
The exact position of e- gun is chosen for avoiding interference between the gun laser room and the LHe transfer line.

## Slide 18
New energy compressor
5 GeV booster linac
Damping Ring
Move energy compressor from LTR to downstream of booster linac.
--- For consolidating the RF and LHe systems in one place
Make the chicane of the energy compressor vertical.
--- For reducing necessary width of the tunnel
Common changes in e- and e+ source Beamline
Old energy compressor

## Slide 19: e- and e+ source tuning dump (5 GeV) positions
Source and 5 GeV linac
Damping Ring
Old dump
New dump
Move from middle of LTR to before LTR.
--- For reducing lengths of beamline and number of magnets.

## Slide 20
Common changes in e- and e+ source Beamline
Make the super conducting booster linac region close to horizontal. (The linac is laser straight, but vertical bend is inserted for making the center of the linac horizontal)
--- For making LHe supply easier
Bend the beam transport line slightly, before LTR, following the BDS.
--- For eliminating need to widen the tunnel
e+ source
SC
SC
e- source
To Damping Rings
Horizontal at IP
BDS
IP
To Damping Ring
Linacs
Old
New

## Slide 21
LTR/RTL

## Slide 22: LTR/RTL Geometry
Change e+ LTR, e- RTL line geometry
  Longer straight regions at both sides of the e+ spin rotator solenoids
  e- RTL is changed accordingly.
  e+ side and e- side become asymmetric.
--- For keeping long enough regions for switching two spin rotators
(Details are not described in TDR)
Kicker magnet
Kicker magnet
solenoide
solenoide
Two solenoides with opposite fields for switching polarization of e+ beam
Need space
Need space

## Slide 23: e+ Damping Ring injection line
Damping Ring is 0.35 m higher than the LTR.
2nd e+ Damping Ring will be 2.5 m higher than the 1st Ring (if constructed).
Make a simple vertical dogleg for 0.35 m elevation
If two e+ rings are needed, reconstruct beamline as:
Raise 1.6 m first, then, branch into two lines, up and down by 1.25 m
  (two beamlines the same length)
e+ beamline length 0.14 m increase. Timing adjusting chicane is designed to address this change.
--- This design is simple at the beginning.
The second damping ring may not be necessary.
(Details not in TDR)
LTR
DR1
DR2

## Slide 24: Position of Damping Rings, LTR/RTL
Change in 2022:
Shift Damping Ring 2.1 m farther from Linac and IP
--- Result of e+ source dogleg change (from 1.5 m to 3.6 m), for keeping straight-line lengths in e+ LTR line.
Change in 2023:
Additional shift of Damping Ring, 100 m farther from Linac and IP
--- For making enough space around IP and Linac-RTL/LTR branches for beam dumps.
Damping Ring
IP
e- BDS
e+ BDS
e+ source
e- source
e+ source dump
e+ main dump
photon dump
e- RTL dump

## Slide 25: Position of Damping Rings, LTR/RTL (cnt’d)
Shift DR by ~100 m
RTL
~250 m increase
Return
~230 m decrease
Total ~20 m longer
Old
New

## Slide 26: Damping Ring – lower horizontal emittance
2017
Longer bending magnet, 3 m -> 5 m
  For reducing horizontal emittance
   Presentation in ALCW2018 (https://agenda.linearcollider.org/event/7826/sessions/4644/#20180531), etc.
2023
Divide bending magnet, 5 m -> 2.4 m x 2
  For easier construction and transfer, etc.
Add space between magnets.
  For realistic design
   Will be reported in DR session of this workshop

## Slide 27: Main linac reference points (PM-8, PM+8)
Move the reference point, PM-8 and PM+8, upstream (farther from IP) by 2 m.
(The reference points are the centers of the LHe domes)
--- For avoiding interference between the LHe transfer line and quadrupole magnets.

## Slide 28
IP
e- ML
e+ ML
Undulator
BDS
BDS
Virtical bend
Virtical bend
Longer turnaround
Longer turnaround
Shift Damping Ring
ML reserve space
ML reserve space
e- source
Undulator,
e+ source
E compress
E compress
Changes of beamlines Summary