## Slide 1
Walid Kaabi Valencia, October 22nd 2025
ERL-based initiatives for luminosity upgrade
Energy-efficient paths to higher luminosity
International Workshop on Future Linear Collider- LCWS 2025

## Slide 2: Motivation:
ESPP- Accelerator R&D Roadmap Report (2022):
“A particularly interesting prospect is to design and possibly build, in the further future, an energy-efficient, ultra-high-luminosity ERL-based electron positron collider at 500 GeV, termed HH500, which would enable the exploration of the Higgs vacuum potential with a measurement of the tri-linear Higgs coupling in e+e−”
Excerpt of the executive summary
Measurement precision at the % level requires a luminosity of 1036 cm-2 s-1.
Increasing the luminosity by orders of magnitude beyond the existent proposals requires significant change in the overall approach on technological choices.
https://arxiv.org/ftp/arxiv/papers/2201/2201.07895.pdf
In this talk, we will highlight several ERL-based concepts, proposed to address this challenge.
2 of them were presented in the LC vision report: https://arxiv.org/pdf/2503.19983

## Slide 3: Introduction: Luminosity enhancement in a collider
Where:
nb : number of bunchs per beam
fr : collision frequency
N1 , N2 : particles per bunch in each beam
: RMS transverse beam sizes in the interaction point
R: geometric reduction factor
R
In a linear collider, for two beams with Gaussian transverse profiles, colliding with a crossing angle or having longitudinal bunch length , luminosity is given by the following formula:
Significant increase of luminosity implies an increase of particle production and therefore additional wall-plug power to handle the high beam current generated.

## Slide 4: Introduction: Average power needs for future HEP projects
https://accelconf.web.cern.ch/eefact2022/papers/frxas0101.pdf
This table is the result of dedicated discussion session on Power budget and performance considerations for future Higgs factories held during eeFACT2022 workshop in Frascati.

## Slide 5: Introduction: Average power needs for future HEP projects
Example 1: FCC-ee (ZH mode)
The total power consumption for a e+ e- Higgs factory is 300 MW. The power breakdown is as the following:
  RF for beam acceleration 51 % (145 MW)
  Cryogenic cooling 5 % (14 MW)
  Magnets 9 % (26 MW)
  Others 35 % (98 MW)
FCC Conceptual Design Report, Eur. Phys. J. Special Topics 228, 261–623 (2019)
The total power consumption is 340 MW for the operation on Higgs mode, assuming a SR power of 50 MW/beam. The power breakdown is as the following:
  RF for beam acceleration 52 % ( 177 MW)
  Cryogenic cooling 3,2 % ( 11 MW)
  Magnets 17 % ( 58 MW)
  Others 27,3 % ( 93 MW)
CEPC Technical Design Report, December 2024 (page 967)
Example 2: CEPC in Higgs factory mode
* “Others” includes vacuum system, instrumentation, radio protection, control system, experimental devices, utilities, general services…

## Slide 6: Introduction: Average power needs for future HEP projects
From 2 examples of Higgs factory, the total power consumption (300-340 MW) represent an estimated annual energy consumption of nearly 2 TWh for a typical yearly operating cycle.
It represent 1 to 6 % of the yearly consumption of some middle size European countries
Half of this consumption is for RF power, to accelerate the beam and compensate SR.
Production, Consumption and Exchange of the electrical power in some European countries (2023 data, updated in February 2024)
https://analysesetdonnees.rte-france.com/bilan-electrique-2023/europe#Introduction
Efficiency enhancement of future large-scale facilities is an obligation toward:
Societal acceptability
Political commitments of hosted countries toward reaching carbon neutrality.
 R&D on high Q0 cavities, high efficiency klystrons development, permanent magnets, efficient cryoplant design

## Slide 7: Introduction- ERL Concept
Injector
Beam dump
Superconducting Linac
ERL Loop
acceleration
deceleration
Acceleration to the top energy
Beam used in IP
Kinetic energy of used beam recycled to re-excite cavities
New beam injected in ERL loop
More advantages:
Linac-like beam quality with extremely flexible time structure
High operating efficiency
Multi-pass configuration: High current carrying capability (no RF power limit) + High beam power in a compact machine
The benefits:
Important reduction of RF power consumption
Dumping the beam at injection power
Fresh beam in IP with the same characteristics
Acceleration:
RF power provided to cavities
The idea:
(1)
(2)
(3)
(4)
(1’)
ERL Loop
(2’)…
Deceleration:
180° RF Phase shift
Notes: By recovering the Energy of accelerated beams, Energy Recovery Linacs (ERLs) make large beam powers possible that would otherwise be prohibitively expensive.
Linacs produce high beam qualities for scientific experiments and for industrial applications, but their beam power is limited by the available electrical power.
ERLs surpass this power limit: much larger beam currents and beam powers become available because the beam energy is recaptured.
How do ERLs compare to other accelerators?
high currents, like storage rings, because the energy is recovered,
high beam quality (low emittance, bunch length, and energy spread) like linacs, because each bunch traverses it only once,
tolerates beam disruption as each bunch is used only once before it’s discarded.

## Slide 8: ReLiC: Recycling Linear e+ e- Collider
A proposed luminosity upgrade of linear Collider: targeted Luminosity > 1036 cm-2 s-1 polarized beam collision
C-o-M energy: large range from 45 GeV to 700 GeV.
It extend ideas of recycling not only the beam energies after collision, but also the collided particles:
Conventional standing wave (SW), single-axis linacs, used to accelerate & decelerate e- & e+ beams.
Linacs are segmented into sections, divided by separators  separation between accelerated and decelerated beams (accelerated beams propagate on axis & deflection of decelerated beams).
2 interaction regions with 2 detectors  cumulated luminosity
Recirculation of particles allow increasing average current  Luminosity enhancement.
Damping rings used to restore emittance and energy spread of used beam before reuse.
Electron and positron sources to compensate losses by synchrotron radiation in the damping ring & IR,
More in V. Litvinenko’s talk tomorrow

## Slide 9: ReLiC: Recycling Linear e+ e- Collider
Critical issue:
Synchrotron radiation and energy spread growth in IR (trajectory bend & beam aligning to prepare energy recovery.
Efficient particle recovery: large energy acceptance damping ring  losses by SR in separator & IR optics, Beamstrahlung during collision…
Synergy with other concepts and existing facilities:
R&D on high-Q and high Tc SCRF cavities, microphonics suppression systems (FE-FRT), HOM dampers (BLA and HOM couplers).
Development of efficient cryogenic systems
Common technologies with low emittance light sources, high current e+ e- colliders and damping ring lattices with large energy acceptance.
Specific need:
High rep-rate and accurate kickers

## Slide 10: ERLC: A re-imagining of the ILC as an ERL
In each side of the IR, 2 parallel SC linacs, one for acceleration and the other for deceleration, connected one to the other with twin-axis cavities to exchange recovered beam power.
To reduce the energy spread arising from beam collisions, damping is ensured by wigglers at a return energy of about 5 GeV.
Duration of cycle is of several second (partial CW RF), imposed by the cryogenic consumption.
The concept was extended recently to an ERLC e- e- (Cf. V. Telnov talk tomorrow)
More in V. Telnov’s talk tomorrow

## Slide 11: ERLC: A re-imagining of the ILC as an ERL
Critical issues and Synergy with other concepts and existing facilities :
Mitigation of the RF Losses in the cavities and HOM to limit the cryogenic consumption.
 R&D on high-Q and high Tc SCRF cavities (Nb3SN)
 R&D on HOM dampers (BLA and HOM couplers).
 Development of efficient cryogenic systems
Specific need:
Development of Traveling Wave (TW) cavities (HELEN type), combined with the development of twin axis cavities

## Slide 12: The Ghost Collider:
A new ERL-based concept of an e+ e- linear collider, 550 GeV center-of-mass, initially inspired by ERLC design, then evolved thanks to the properties of “ghost bunches”.
More in A. Hutton’s talk tomorrow
Linacs are the same length as the ILC ones, with partial CW RF (2s on- 4s off), or later full CW RF @ 4.5K.
Shape of arcs was optimised, reducing synchrotron radiation by 35.8%.

## Slide 13: The Ghost Collider:
Ghost bunches are electrically neutral: equal numbers of e- and e+ traveling together in the same Linac buckets  No electromagnetic interactions with the linac environment:
  No excitation of High Order Modes (HOM)
  No multi-bunch Beam Breackup (MBBU)
Energy transferred between e- and e+ in the same bunch, decelerating one and accelerating the other  No need to couple linacs in the same side to transfer the power (no twin-cavity needed)
No electromagnetic interactions between ghost bunches travelling in opposite direction  Single bidirectional linac on either side of the IR
No electromagnetic interaction in IP as bunches are neutral  Possible to have several IPs in the IR, each of them with the design luminosity (1.6 1034 cm-2 s-1).
IP
Arc
Arc
SRF Linac
SRF Linac
Chicanes

## Slide 14: LHeC:

## Slide 15: LHeC:
HL-LHC – 7 TeV
1/3 LHC circumference
Beam Energy [GeV]
Luminosity [1034cm-2s-1]
Normalized emittance gex,y [mm]
Beta Function b*x,y [m]
rms Beam size s*x,y [mm]
Beam Current @ IP [mA]
Bunch Spacing @ IP [ns]
Bunch Population [1011]
Bunch charge [nC]
=1.18 TeV
LHeC | 
p | e-
7000 | 50
2.3 | 
2.5 | 20
0.07 | 0.1
4 | 4
1100 | 50
25 | 25
2.2 | 0.078
35 | 1.24
2.5 GW beam power
2.5 GW beam power
HL-LHC proton beam parameters
Very low beta functions at the IP!
50 mA e- current

## Slide 16: LHeC:
=1.18 TeV
 89 MeV- 20 mA
 250 MeV- 20 mA
LHeC configuration and parameters:
Multi-turn ERL (3 pass up, 3 pass down)
Top energy: 50 GeV, ~ 9 GeV /Linac
1.25 nc bunch charge @ 40 MHz  50 mA average current
802 MHz SRF system, targeted Q0= 3. 1010
Beam damped at injection energy (7 MeV)
RF systems (at twice the LINAC frequency) to compensate for the synchrotron radiation loss in the arcs
PERLE configuration and main parameters:
Multi-turn ERL (3 pass up, 3 pass down)
Top energy: 250 MeV, ~ 82 MeV /Linac
500 pc bunch charge @ 40 MHz  20 mA
802 MHz SRF system, targeted Q0= 3. 1010
Beam damped at injection energy (7 MeV)

## Slide 17
Thank you for your attention!

## Slide 18: LHeC as a bridge:
In standalone mode (ep/eA only), LHeC may be a bridge between major colliders at CERN: between the end of HL-LHC (2041) and the next flagship CERN collider.

## Slide 19: LHeC as a bridge:
In standalone mode (ep/eA only), LHeC may be a bridge between major colliders at CERN: between the end of HL-LHC (2041) and the next flagship CERN collider.

## Slide 20: ERL - The global landscape
Technology Limited
Funding Limited
ERLs were recognized as one of the five main axis of accelerators R&D in support of the ESPP:
  High-field magnets
  High-gradient RF structures & systems
  High-gradient plasma laser accelerators
  Bright muon beams and muon colliders
  Energy Recovery Linacs
Two projects: PERLE & bERLinPro were recognized as "essential pillars of the ERL development," with milestones to be achieved by the next ESPP in 2026.
ESPP R&D Accelerator Roadmap: https://arxiv.org/ftp/arxiv/papers/2201/2201.07895.pdf

## Slide 21: Further development toward improving ERL efficiency
The SRF traveling wave (TW) Nb structure in a resonant ring configuration are very promising in term of high achievable gradient and lower cryogenic losses compared to Standing Wave structure (factor of 2 higher 𝑅/𝑄 ).
In addition, the TW structure provides high stability of the field distribution along the structure with respect to geometrical perturbations. This allows for much longer accelerating structures, limited by the manufacturing technology only.
In the future, This could be a serious alternative for large-scale facility in general, and ERL-based one in particular, as it offer the compactness (high gradient) and the efficiency (low cryogenic loss).
For the time being we are at the stage of proof-of-principle experimental demonstrator with few cells.
Traveling wave (TW) bulk Nb structure: