## Slide 1
Status of the CLIC injector complex and Positron Source
Steffen Doebert on behalf of the CLIC collaboration
New injectors layout from the CLIC Readiness Report
Beam dynamics simulations (Yongke Zhao)
Positron Source Beam Loading studies (Nafiseh Mesbah)
AMD prototyping
Conclusion
LCWS , Valencia, October 2025

## Slide 2
CLIC Readiness Report
https://edms.cern.ch/ui/file/3285253/1/2025_CLIC_Readiness_Report_V2025may26.pdf
Latest CLIC documentation as Input for the European Strategy Update 2025
Very Interesting Read with lots of updates for the CLIC machine, in particular a new injector layout
Being published in: “The European Physics Journal Special Topics”

## Slide 3
CLIC Readiness Report New injector layout and configuration
New positron production energy: 2.86 GeV
Separate positron capture linac up to 2.86 GeV
Folded layout to save space
New optimized accelerating structure
Used lessons learned from the FCCee injector optimization
Results in power and cost savings

## Slide 4
All situated on the CERN Prevesin site

## Slide 5: CLIC positron production
Based on our latest e+ source simulation (CLIC-Note-1200), it is possible to reduce the e- beam energy from 5 GeV to ~2.3 GeV (assuming 1 nC max.)

## Slide 6: Positron Target Scheme, single amorphous target
Old baseline
Hybrid target option (CDR version)
Single target option
Hybrid target distance scan
Single target thickness scans
New baseline
Optimised target thickness vs beam energy
Positron yield improved by a factor of 1.65, deposited power in target reduced by a factor of 2.1, compared with the old optimization report published in 2019
Optimized thickness: 18 mm
Reoptimized in an old report published in 2019

## Slide 7: Revised beam dynamics design
  PDR accepted e+ yield ~ 1.1, Electron bunch charge ~ 1.0 nC, PEDD ~ 31J/g
  Spot size on target 2.5 mm, target thickness 16.5 mm
  Revised solenoid field along capture linac
  Revised beam dynamics in the linac up to 2.86 GeV
AMD exit Pre-Injector Linac exit Injector Linac exit

## Slide 8: Study of Imperfections
100 randomly misaligned machines simulated
Average positron yield reduced by 6%. Emittance also increased by 6%. Results are acceptable
Beam-based alignment corrections are not very necessary
Normalized emittance of all machines
Positron yield of all machines
Misalignments & beam jitters (RMS)

## Slide 9: Alternative options: uniform beam
Primary e- beam with uniform profile (transverse distribution)
Optimization results (e.g. DBA @ 380 GeV)
Transverse positions
Transverse momentums
Horizontal position
Significant improvement in yield (30%)
Uniform beam production is very challenging (to be designed)

## Slide 10: Alternative options: SC AMD, tapered target
Using a SC solenoid as AMD (similar to FCC-ee study)
Target can then be tapered to increase yield (originally conceived by Nicolas Vallis for FCC-ee study)
Optimization results of using analytic SC solenoid field
  The optimized field is the same as the FCC-ee HTS solenoid field (designed by PSI)
Schematic layout based on a SC AMD
Schematic layout for tapered target
On-axis Bz field comparison
FC: FC based AMD. New baseline
HTS: FCC-ee HTS based AMD
HTS-TT: HTS + Tapered target
HTS-TT-UB: HTS + Tapered target + Uniform beam
Results (DBA @ 380 GeV)
Significant improvement in yield (25%) using SC AMD, though much lower than FCC-ee (~50%)
Also significant improvements in other challenging options

## Slide 11: New injector linacs design
See as well dedicated presentation by Adnan Kurtulus in this workshop
Positron Capture Linac
Electron and Booster Linac

## Slide 12
Beam loading in the positron capture Linac
Nafiseh Mesbah
Simulated with RF-Track
Example of beam loading effects in the first structure using gaussian beams

## Slide 13
Beam loading in the positron capture Linac
Nafiseh Mesbah
Beam loading in the full capture linac with distribution tails cut.
Shown is the last bunch of the train

## Slide 14
Beam loading in the positron capture Linac
Nafiseh Mesbah
Beam loading in the full capture linac without distribution tails cut.
Shown is the last bunch of the train

## Slide 15
Beam loading in the positron capture Linac
Nafiseh Mesbah
Results after phase optimization to minimize beam loading effects.
Still many aspects to be understood but it looks with a phase optimization one can reach an acceptable result.

## Slide 16: Zoo of new designs for the CLIC e+ source
From linear to non-linear profile for the FC aperture:
Linear
Concave downward (1)
Concave upward
Concave downward + linear (3)
Concave downward (2)
Hugues Bajas

## Slide 17: Design optimization for the CLIC e+ source
SLAC design @ 25 kHz & 13 kA
Vs.
linear modified design
with large aperture
Vs.
Non-linear design (1) Concave downward
Vs.
Non-linear design (3) Concave downward + linear
Vs.
Non-linear design (2) Concave downward
Adapting the non-linear shape (green vs. yellow) preserves the yield (53% higher).
The voltages get significantly lower.
The detrimental forces directed along the coil axis Z lowers too.
Hugues Bajas

## Slide 18: Manufacturing choices
“Classic” Machining with
Electric Discharge Machining (EDM)
Better precision and surface quality
“Innovative” Machining with 3D printing (at CERN with Titanium and Steel)
Huge freedom in design (include cooling pipes)

## Slide 19: 3D-printing

## Slide 20
Possible Prototype testing within KEK test stand
Flexible holder for several prototypes

## Slide 21: Manufacturing with EDM
These are challenging pieces to machine, needs huge effort.
Finally, we manged to manufacture two prototypes at CERN

## Slide 22: 3D-printing results in Steel and Titanium
TI
SS
Not clear yet if this will be successful but would open very interesting options. Quite massive object for 3D printing

## Slide 23
Conclusions
Revisited and updated the design of the whole CLIC injector chain for EPPSU exercise Probably most consistent design for CLIC until now Performance improvements, cost and power savings New positron production design, 2.86 GeV drive beam, amorphous target, new linac structures
Still studying beam loading effects on the CLIC bunch train. Great evolution of the simulation tools but still a lot of open questions.
Successful manufacturing of adiabatic damping devices with different manufacturing techniques. High power testing needed to advance further.
Waiting for EPPSU outcome to define future directions