## Slide 1
COLD Cool copper Operation Linac Demonstrator and preliminary studies for a 6GeV injector Linac at ESRF
A. D’Elia on behalf of the COLD project team:
S. Liuzzo, P.Borowiec, V.Serrière, M.Dubrulle, M.Morati, S.White, F. Ewald, N.Benoist, K.Scheidt, B.Roche, C.Benabderrahmane, G. Le Bec, R.Bourtenbourg, J.-L. Pons, D. Martin, B. Pelissier, L.Eybert, T.Brochard, C.Maccarrone, J.-L. Revol, B.Joly, Y.Gouez, H. Pedroso Marques, P.Colomp, A.Dely, F.Falaise, David Frichet, Q.Qin
International collaborators
E.Nanni, A.Dhar, W.-H. Tan, G.Aymar (SLAC),
A.Latina (CERN),
D.Alesini, F.Cardelli, A.Giribono, C.Vaccarezza, G.Silvi (LNF),
M.Andorf, J.Maxson (Cornell),
P.Craievich, R.Zennaro (PSI)
LCWS2025, Valencia, Spain, 20-24 October 2025

## Slide 2: A NEW 6GeV Linac
ESRF is presently considering a complete upgrade of our injectors with a full energy linac: limited space available, high gradient technologies could be a solution
Enable ultra-low emittance / low aperture / low gaps SR lattice design by relaxing constraint on DA.
Complete renewal of obsolete injectors providing low emittance injected beams (<1nmrad, >40 times smaller than the present injectors, <1mm bunch length >10 times shorter bunch, 0.6mA/bunch)
Demonstrate state-of-the-art compact technology for users facilities injectors
Enable transparent on-axis off-phase* accumulation with ultra short injected beam (with ultra-fast kicker).
Enable new science making use of the linac electron beam (short pulse e-, FEL)
Booster beam
Linac beam
x
t
x
stable space
standard off-axis, on-energy
on-axis,
off-phase
stored beam
t
2ns, 2mrad kicker
60nm x 17mm
1nm x 1mm
*M.Aiba: https://journals.aps.org/prab/abstract/10.1103/PhysRevSTAB.18.020701

## Slide 3: Inj. Eff. in SR with 6GeV linac beam properties
Normal conditions beam at -8.mm
A. Sauret, PhD student, Beam Dynamics group
Bunch length = 2mm
1/1 nm.rad
Peak I.E. = 99.9%
Bunch length = 20mm
60/30 nm.rad
Peak I.E. = 82%
Booster (2025)
6GeV LINAC
Bunch length = 20mm
27/54 nm.rad
Peak I.E. = 92%
Booster (upgrade)

## Slide 4
Injectors
upgrade
SR Injection section
improvement
Booster
refurbishment
Linac
refurbishment
NEW
Linac
Non-linear injector kicker
Transparent injections
Maintain injection efficiency
Lower natural emittance
Higher injection efficiency in SR
Higher extraction efficiency
More reliability
Modernization
Higher energy
Advanced
design
✓
Procurement
✓
Advanced
✓
Short term
Long-term
Replace existing injectors with a full energy injector linac
Higher injection efficiency, lower injection perturbation, enable/facilitate future SR upgrades
6GeV + margin
> 600 pC (single bunch)
< 1 nm.rad at SR injection
< 0.1 % energy spread
< 1 mm bunch length
> 4 Hz repetition rate
Bunch spacing 2.8ns (in the SR)
Fits on site (maximum 180m)
As low energy consumption as possible
User facility grade :
Reliability
Reproducibility (turn on 1 month later and it works as before)
Maintainability easy to repair or operate with failing component for long term
FEL option to be studied
3 M€
0.5 M€
1.5 M€
COLD
started
✓
5 M€

## Slide 5: 6GeV full energy LINAC: better beam, less consumption, same cost
Fits on site
X ”pushed” design
X High cost
V BEST SOLUTION
Lowest consumption
x25 = 100Hz 6GeV FEL power
77
62
Cost estimates compatible with Compact Light cost estimates.

## Slide 6
E.Nanni, SLAC, IPAC, Venice, 2023
https://arxiv.org/abs/2203.09076

## Slide 7: C0.5: Cband cold 35MW
Less acc. structures
Less power overall
Less magnets
Less energy spread (0.06%)
Less building
Shorter (100m)
Needs LN2 cooling (77K)
Starting conditions
2mm mrad
0.5ps
100MeV

## Slide 8: Error Studies
50 um alignment:
RF
BPM
Quadrupoles
1 deg random phase error among structures

## Slide 9: Errors sensitivity: quadrupoles
Error sensitivities are very forgiving. ~1% emittance growth for 1 micrometer random errors (vibrations)
Plot style and analysis inspired from Wei-Hou Tan et al., Emittance Preservation in the C3 Main Linear Accelerator, SLAC, submitted for publication
Since emittance is not critical, we must check also corresponding beam position jitter amplitude that could harm later transport chain and finally injection efficiency.
15 nanometers for C3 collider

## Slide 10: Space available
Present linac 19.5m
Empty tunnel space 40m
60m long tunnel
✓
✓
Safety
~0.5GeV C3 demonstrator could fit in the empty tunnel and allows independent EBS operation
The empty tunnel space will be used for conditioning of RF structures (S-Band, C-band, …), test of diagnostics, training of personnel with high-power, pulsed RF, UHV, laser technology…

## Slide 11
COLD
A demonstrator to prove
high gradient cryogenic accelerating structures
for users facility grade operation
at low repetition rate.
The pre-injector of a new 6GeV linac.
C2 cold copper
Operation
Linac
Demonstrator

## Slide 12: INFN-LNF SPARC (or CLEAR) photo-GUN:
SLAC distributed coupling standing wave cryogenic accelerating strucutres and cryomodule
PSI: Pulse compression
high charge,
small emittance, short pulse length
high gradient (135MV/m)
Low breakdown rates at 77K
Enabling technologies available from the international collaborators
CERN: simulation tools (RF-Track)
CORNELL: FEL options
High quality factor C-band RF pulse compressors

## Slide 13: Can we reduce the number of klystron?
Freq. (GHz) | 5.712
Pin (MW) | 25
Pulse length (us) | 4
BOC | 
Beta | 9.4
Q0 | 220000
Acc. Structure | 
Beta | 2
Q0 | 22500
Rsh (Mohm/m) | 300
(PSI-BOC)
No Power reduction
No Power reduction
-30% in power applied at the output of the BOC
No Power reduction
30% of power reduction at the output of the BOC to take into account WG losses and some klystron power margin.
A 50MW klystron, 4us pulse length with PSI-BOC could feed 2 cryomodules (4 x C3 structures) to get 75/80 MV/m
Thus reducing the # of RF-units needed. ~50 Meuro instead of 64
42MW/3ms exists, 50MW/4ms is possible according to CANON considering our rep. rate of 4Hz

## Slide 14: Initial part of the linac, space charge dominated (up to 150MeV) = COLD setup
5.5 mm.mrad , 1.6 ps
desired: ~5mm.mrad, 0.5ps
700pC
SPARC 3GHz gun
Cu cathode
120 MV/m
sr = 0.6 mm (uniform)
st = 200 fs (gaussian)
Bz = 0.29 T
Ez C band = 135.0MV/m
~1 m drift for diagnostics
Simulated particle emission
Space charge
gun
Acc. struct.
in cryomodule
Diag. section and beam dump
Diag. section

## Slide 15: Layout for High power RF tests, dark currents measurement, diagnostics/dump tests
2027
Not to scale
50 cm
shielding
Accelerating structures
Quadrupole
Vaccum valve
Faraday cup
shielding
Faraday cup
BLM
Neutron monitor
bellow
bellow
328 cm
Quadrupole
Quadrupole
1x 50MW C-band RF-unit
50MW
gun
5.8m RI section
shielding
SCREEN
For emittance with quadrupole scan
RF deflector
https://doi.org/10.1016/j.nima.2006.07.050
Dipole
Faraday cup
BPM
shielding
SCREEN
Faraday cup
BPM
stripline
For energy
HV corrector
BLM
Neutron monitor
1x 35MW S-band RF-unit
35MW
buncher
Profit of the installation to test spare acc. section with beam.
Not to scale

## Slide 16: Electron Beam line Layout COLD Phase 1: 150MeV (170MeV authorization)
35MW
stripline
A.Cianchi: https://jacow.org/e08/papers/MOPC068.pdf
L.Badano: https://jacow.org/d07/papers/TUPC11.pdf
GUN
SOLENOID
on movers
HV corrector
SCREEN
From Compact Light CDR
destructive
sparc-mm-06/001
Current transformer
BPM
Vaccum valve
laser optics table
Laser input
Neutron monitor
shielding
SCREEN
For emittance with quadrupole scan
RF deflector
https://doi.org/10.1016/j.nima.2006.07.050
Dipole
Faraday cup
BPM
shielding
SCREEN
Faraday cup
BPM
stripline
For energy
HV corrector
BLM
Neutron monitor
Acc. structures
3xQuadrupole
on movers
BPM
stripline
Vaccum valve
Neutron monitor
bellow
GUN SECTION
DIAGNOSTICS/DUMP SECTION
bellow
PC
1x 50MW C-band RF-unit
2029
~3.9m
Not to scale
25MW
1x “6GeV linac module”, prototype

## Slide 17: Shorter 6GeV linac unit 300MeV module
BPM inside quad
Acc. structures
Quadrupole
on movers
stripline
Compact Vaccum valve
bellow
bellow
328cm
7.8m
BPM inside quad
Acc. structures
Quadrupole
on movers
stripline
Compact Vaccum valve
Neutron monitor
bellow
bellow
278cm
Acc. structures
bellow
278cm
Screen
5.93 m
BPM inside quad
Acc. structures
Quadrupole
on movers
stripline
screen
Neutron monitor
bellow
bellow
PC
50MW
PC
50MW
4mm.mrad, ~400pmrad@6GeV
0.19% energy spread
0.5mm bunch length
6.444 GeV in 170m, 21 x 7.8m modules
5.6mm.mrad, ~500pmrad@6GeV
0.18% energy spread
0.5mm bunch length
6.159 GeV in 131m, 21 x 5.93m modules
Fits on ESRF site
Ideal 5.70 m

## Slide 18: Electron Beam line Layout COLD Phase 2: 300 MeV (325MEV authorization)
stripline
A.Cianchi: https://jacow.org/e08/papers/MOPC068.pdf
L.Badano: https://jacow.org/d07/papers/TUPC11.pdf
1x “6GeV linac module”, prototype
GUN
SOLENOID
on movers
HV corrector
SCREEN
From Compact Light CDR
destructive
sparc-mm-06/001
Current transformer
BPM
Vaccum valve
laser optics table
Laser input
Neutron monitor
shielding
SCREEN
For emittance with quadrupole scan
RF deflector
https://doi.org/10.1016/j.nima.2006.07.050
Dipole
Faraday cup
BPM
shielding
SCREEN
Faraday cup
BPM
stripline
For energy
HV corrector
Neutron monitor
Acc. structures
3xQuadrupole
on movers
BPM
stripline
Vaccum valve
Neutron monitor
bellow
1x “6GeV linac module”, the #1
GUN SECTION
DIAGNOSTICS/DUMP SECTION
BPM inside quad
Acc. structures
Quadrupole
on movers
stripline
Compact Vaccum valve
Neutron monitor
bellow
bellow
bellow
PC
1x 50MW C-band RF-unit
Optimized length
Screen or valve alternating
2030
~3.9m
~3.1m
SLAC
ESRF
Not to scale
50MW
35MW

## Slide 19: Installation in the tunnel
2025
2026
2027
2029
2030
2031
(option) Proposed to install an undulator  WP12
2 cryomodules (1 from SLAC and 1 ESRF)
Beam to ESRF booster and old linac as spare
High power RF tests + beam in section0
Beam in C3 acc. structures.
Phase 1
Phase 2
6GeV Linac construction during shutdowns and commissioning during USM
Phase 3
2032-35
2 month shutdown to install new Transfer line linac to SR and commission new injection
2035
Take decision to continue or not toward 6GeV linac
2030
Mod
S_4
135 MeV

## Slide 20: Planning
A planning (12 WPs, ~150 tasks/subtasks) including resources and following an almost flat financial profile is set up with the available tools (excel mainly). A more advanced version will be set up with Microsoft Planner
S-band RF unit
C-band RF unit,
instrumentation
Diagnostics, waveguides, laser, acc.structures
Photogun,
Pulse compressor
WP-01 RF
WP-02 Diagnostics and Laser
WP-03 Vacuum
WP-04 Mechanical Engineering
WP-05 infrastructure
WP-06 Operation
WP-07 Controls
WP-08 Alignment
WP-09 Safety
WP-10 magnets and power supplies
WP-11 beam dynamics
WP-12 Photons
Financial profile and budget codes are set up
High power RF measurements
Beam

## Slide 21: RF
S-Band RF-unit CFT performed. Provider selected.
COLD photo-gun RF unit.
Fully compatible (identical) to the new RF-Units purchased for the present linac refurbishment.
In case COLD project is delayed, this equipment can be used for USM operation.
First component of COLD project purchased in 2025

## Slide 22: COLD project risks
 | low | moderate | high | 6GeV show stopper | Impact USM
Lack of Human resources |  |  |  |  | 
Collaboration contracts / Amendments not established in time |  |  |  |  | 
Gradient not reached |  |  |  |  | 
Low reliability |  |  |  |  | 
Low repeatability |  |  |  |  | 
Low maintainability |  |  |  |  | 
Lack of financial resources |  |  |  |  | 
Pulse compression not reached |  |  |  |  | 
Module > 5.9m |  |  |  |  | 
Current not reached |  |  |  |  | 

## Slide 23: Conclusions
To upgrade the ESRF injectors a full energy 6GeV linac is considered.
The shortest, cheapest and less consuming solution is a cryo C-band distrib. coupling acc. structure
High gradient technology leads to smaller footprint injector, thus reducing costs and fitting on site.
The new injector will consume likely a factor 2 less than the present one.
The beam properties are being studied in presence of errors. Further studies are being pursued.
Smaller iris apertures (higher gradients) seem to be acceptable.
50 micrometer static alignment errors can be corrected easily.
Up to 1 micrometer amplitude vibrations are acceptable.
All components exist (no R&D needed). COLD project started in April 2025 will prove the technology readiness and build the competences needed.
100m
~56M€
50% of present
77K

## Slide 24: Many thanks for your attention
A.D’Elia: on behalf of the COLD project team:
S. Liuzzo, P.Borowiec, V.Serriere, M.Dubrulle, M.Morati, S.White, F. Ewald, N.Benoist, K.Scheidt, B.Roche, C.Benabderrahmane, G. Le Bec, R.Bourtenbourg, J.-L. Pons, D. Martin, B. Pelissier, L.Eybert, T.Brochard, C.Maccarrone, J.-L. Revol, B.Joly, Y.Gouez, H. Pedroso Marques, P.Colomp, A.Dely, F.Falaise, David Frichet, Q.Qin
International collaborators
E.Nanni, A.Dhar, W.-H. Tan, G.Aymar (SLAC),
A.Latina (CERN),
D.Alesini, F.Cardelli, A.Giribono, C.Vaccarezza, G.Silvi (INFN-LNF),
M.Andorf, J.Maxson (Cornell),
P.Craievich, R.Zennaro (PSI)
6GeV Linac injector
Thank you for your attention!