## Slide 1
Recent Progress in Dielectric Laser Acceleration
Manuel Konrad, Stefanie Kraus, Julian Litzel, Leon Brückner, Zhexin Zhao, Julian Freier, Roy Shiloh*, Tomas Chlouba**, Peter Hommelhoff***
Friedrich-Alexander-Universität Erlangen-Nürnberg (FAU), Erlangen, Germany
* Now with Hebrew University, Jerusalem, Israel
** Now with AMOLF, Amsterdan, Netherlands
*** Now with Ludwig-Maximilian University München (LMU) and FAU

## Slide 2: Why dielectric-based laser accelerators?
Fermilab
Dielectric materials and optical frequencies
Higher damage threshold than metallic cavities
Higher gradients and smaller, minituarized structures
Much stricter requirements on beam properties
Lower current
per channel
f=150 THz (λ=2 μm)
τ=6.6 fs
RR ~ kHz-MHz
>3 GV/m fields
Gradient >1 GeV/m
Physical aperture: ~200 nm
Emittance <100 pm rad (norm)
fA-pA
(in single channel, many are possible soon)
f=3 GHz
τ=333 ps
RR ~ Hz-kHz
<200 MV/m
25-50 MeV/m
~1cm
1 μm ~ 1 mm rad
nA-μA and larger
DLA
RF
Multi-channel DLA:
Zhao et al., Photonics Research 8 10,
1586-1598 (2020)
Laser
Laser

## Slide 3: Operation principle
~620nm
TM-polarized
Depending on particles position:
Acceleration
Deceleration
Deflection
2
1
3
4
Proof of concept:
25 MeV/m: J. Breuer, P. Hommelhoff, PRL 111, 134803 (2013)
: 250MeV/m: Peralta, E. A., Soong, K., England, R. J., Colby, E. R., Wu, Z., Montazeri, B., ... & Byer, R. L. (2013). Nature, 503(7474), 91-94.
First spatial harmonic
1
2
3
4
2
3
4
1
Goal: generate a mode that allows momentum transfer from laser field to electrons
Use first order effect, so m=1 (efficient!)
Second order effects too already too inefficient
Synchronicity condition:
Acceleration
Deceleration
0

## Slide 4
Chen et al., Proposal (1989)
Shiloh, et al., Opt. Express 29, 14403-14411 (2021)
Leedle, et al. CLEO, pp. FM3M-7 (2018)
Leedle, et al. Opt. Lett. 40, 4344-4347 (2018)
Yousefi et al., Opt. Lett. 44, 1520-1523 (2019)
Fishman et al., Nature Comm 14, 3687 (2023)
Black et al., PRAB 23, 114001 (2020)
Bonded silica gratings
Silicon pillar structures
Peralta et al. Nature 503, 91–94 (2013)
Koyama, K., et al. IPAC (2014)
Wei et al., Appl. Optics 56(29) (2017)
Wie et al., Physics of Plasmas 24.7 (2017)
Cesar et al., NIMA 909, 252-256 (2018)
Cesar et al., Optics Expr., 26(22), (2018)
Crisp et al., arXiv:2310.12384 (2023)
Top illumination
2013
2021
2015

## Slide 5: Guiding of sub-relativistic electrons inside DLAs (in plane parallel to substrate)

## Slide 6
Force acting on electrons:
Guiding with Alternating Phase Focusing
(without acceleration)
e-
z
y
x
: Phase between laser and electron
z<0
Shiloh, R., Illmer, J., Chlouba, T., Yousefi, P., Schönenberger, N., Niedermayer, U., Mittelbach, A., & Hommelhoff, P. Nature 597, 498 (2021)
Niedermayer, U., Egenolf, T., Boine-Frankenheim, O., Hommelhoff P., Phys. Rev. Lett. 121, 214801 (2018)

## Slide 7
R. Shiloh, J. Illmer, T. Chlouba, P. Yousefi, N. Schönenberger, U. Niedermayer, A. Mittelbach, P. Hommelhoff, Nature 597, 498 (2021)
Overfocusing effect (>400 MV/m)
Different structure geometry with larger macrocells
Overfocusing
Alternating phase focusing effect: proof of principle
2.7 times larger electron current at optimal transport field strength (~700 MV/m)
Guiding
For Linacs: Lauber, S., Barth, W., Basten, M., Dziuba, F. D., List, J., Miski-Oglu, M., ... & Yaramyshev, S., EPJ Techniques & Instrumentation, 11(1), 5 (2024)

## Slide 8: Acceleration + Guiding (guiding in plane parallel to substrate)

## Slide 9: Coherent laser acceleration of electrons
T. Chlouba*, R. Shiloh*, S. Kraus*, L. Brückner*, J. Litzel, P. Hommelhoff, Nature, 622, 476 (2023)
Phase jumps + Tapering
=
Guiding + Acceleration
So far only guiding, now: acceleration
Reminder:
D: Defocusing
F: Focusing

## Slide 10
9
200
300
400
500
Previous generation accelerating structure
EPeak = 600MV/m - 700MV/m
Design gradient: 22.7MeV/m
2µm
1mm
e-
Laser
225nm
450nm
480nm
Top view
139 – 237nm

## Slide 11
10
200
300
400
500
Previous generation accelerating structure
1mm
e-
Laser
2µm
EPeak = 600MV/m - 700MV/m
Design gradient: 22.7MeV/m
225nm
450nm
480nm
Top view

## Slide 12: Experimental setup at FAU
Electron sources
XL30

## Slide 13
Maximum energy gain 12.3 keV
Total energy of 40.7 keV
43% energy gain
200m
300m
400m
T. Chlouba*, R. Shiloh*, S. Kraus*, L. Brückner*, J. Litzel, P. Hommelhoff, Nature, 622, 476 (2023)
500m
Similar results from Stanford/Darmstadt team:
Broaddus, Egenolf, …, Byer, Leedle, Solgaard, Phys. Rev. Lett. 132, 085001 (2024)
Laser on
Laser off
Simulation
4.5 keV
Simulation
Pillar distance
Energy gain (keV)
% of survived particles
Energy
1
0.5
0
6.6 keV
8.8 keV
11.9 keV

## Slide 14: DLA @ 10 µm
Advantage of longer wavelengths:
Higher damage threshold → Higher accelerating fields
Wider channel (factor 5 for 10 µm vs. 2 µm) → Larger acceptance / less strict requirements on input beam → Larger currents possible
Easier fabrication → Additive fabrication? → More possibilities for 3D structures
L. Brückner, et al., Opt. Express 32, 28348 (2024)
L. Brückner, dissertation

## Slide 15: Scalability of DLA - optimistic
Subrelativistic energies:
FAU (28.4keV 30.8keV) 200MV/m
FAU (28.4keV 40.7keV) 22MV/m
Stanford (86.5keV 96.3keV) 370MV/m
Stanford (96keV 128keV) 46MV/m
Relativistic energies: Highest peak gradient record: 1.8GV/m (8MeV at UCLA)
<50 keV: average gradient of 50 MeV/m
Up to 100 keV: average gradient of 100 MeV/m
Above: 1 GeV/m
Cesar, et al., Communications Physics, 1(1), 46, (2018)
Yousefi, Peyman, et al., Optics letters 44.6: 1520-1523 (2019)
Chlouba et al., Nature, 622, 476 (2023)
Leedle, Kenneth J., et al. Optics letters 40.18: 4344-4347 (2015).
Broaddus, P., et. al., PRL, 132(8), 085001 (2024).
Epeak = 600MV/m, 100fs pulse length, 167kHz rep. rate, 𝜔𝑥 = 2.5𝜇m
1MeV
Structure:
Length 1.8mm
Laser:
Pavg mW
1GeV
Structure:
Length 1m
Laser:
Pavg W
10GeV
Structure:
Length 10m
Laser:
Pavg kW
Challenges
Excitation of synchronous mode
Conservative design (50% of the crest)
Not fully optimized structure
  Try variable pillar sizes
  Inverse designed structures

## Slide 16: Other applications of DLA structures
At sub-relativistic energies, the phase-dependent energy spread can be used for temporal bunching

## Slide 17: Other applications of DLA structures
Inverse of DLA: Smith-Purcell-Effect
Emission of narrowband radiation in a highly tunable frequency range -> Narrowband: Bragg mirrors -> Tunable: Frequency depends on structure period and electron velocity
Can be put in electron beamline -> Useful for pump-probe experiments
ACS Photonics 2022, 9, 1143-1149

## Slide 18: Other applications of DLA structures
Efficient, quantum coherent coupling between photons and free electrons allows entanglement between them -> Allows extraction of photon statistics from electron spectra

## Slide 19
Partners:
iQCE collaboration
ACHIP collaboration
M. Chekhova, MPL
Y. Morimoto, RIKEN
I. Kaminer, Technion
O. Neufeld, Technion
J. Rosenzweig, UCLA
I. Franco, Rochester
F. Tani, Ph. Russell, MPL
Th. Fennel, Rostock
C. Lemell, J. Burgdörfer, TU Vienna
A. Leitensdorfer, Konstanz
FAU Applied Physics: H. Weber
M. Kling, LMU/MPQ
R. L. Byer + coll., Stanford / SLAC
M. StockmanϮ, Georgia State
G. G. Paulus, Jena
Fabian Bammes
Nils Bode
Leon Brückner
Yiqi Fang
Julian Freier
Jonas Heimerl
Celina Hüttner
Johannes Illmer
Patrick Käferlein
Manuel Konrad
Viacheslav Korolev
Stefanie Kraus
Daniel Lesko
Weizhe Li
Julian Litzel
Felix López Hoffmann
Matthias Meier
Stefan Meier
Selina Nöcker
Jonathan Pölloth
Tamara Pröbster
Martin Reh
Franz Schmidt-Kaler
Fabian Sochor
Frederic Voggel
Tobias Volk
Timo Wirth
Maria Würth
Zhexin Zhao
Recent alumni:
PhDs: T. Weitz (né Boolakee) Ph. Dienstbier C. Gerner C. Heide Ang Li M. Seidling T. Paschen A. Tafel N. Schönenberger R. Zimmermann (M. Sirotin)
Postdocs: T. Chlouba M. Knipfer F. Mooshammer Y. Morimoto R. Shiloh T. Shibuya
Master students: S. Hillmann M. Knauft B. Löhrl A. Michalak
I. Probst S. Wittigschlager

## Slide 20: Thank you for your attention!

## Slide 21: Summary
Preliminary!
T. Chlouba, R. Shiloh, S. Kraus, L. Brückner, J. Litzel, P. Hommelhoff, Nature, 622, 476 (2023)
2D APF
(guiding in plane)
2D APF +
Acceleration
3D APF
(full guiding)
Shiloh, R., et al., Nature 597, 498 (2021)
Long term goal:
3D APF + Acceleration -> Scalable accelerators

## Slide 22: Guiding in 3D? (including out of plane direction)

## Slide 23: Guiding in 3D - The concept
Problem: structures etched from silicon -> field roughly invariant perpendicular to substrate -> No field component in that direction
Possible Solution proposed by Uwe Niedermayer et al.: Stacked layers of different dielectrics -> Contrast of refractive index breaks invariance
Niedermayer, et al., Phys. Rev. Lett. 125, 164801 (2020)

## Slide 24: Guiding in 3D - The concept
For top-illumination:
  Field invariance is broken -> field nodes form along channel
  Transversal forces now in both directions
Niedermayer, et al., Phys. Rev. Lett. 125, 164801 (2020)
Shiloh, et al., Opt. Express 29, 14403-14411 (2021)
Another way to break invariance: Top illumination! -> Reflection from substrate breaks invariance -> Similar field profiles to stacked structure
Two questions arise:
Do we need the stacked structure or is top-illumination sufficient
If so, did we already have 3D confinement in previous measurements?

## Slide 25: Guiding in 3D – Material combinations
How does the material influence 3D APF? -> Nodes less pronounced for lower contrast
Only Silicon: Nodes forming as well -> due to top-illumination

## Slide 26: Guiding in 3D – First preliminary simulation results
All structures show guiding, but is it 3D APF? -> Need to find a way to distinguish between 2D and 3D guiding
Note: Pure silicon shows strongest guiding -> Structures not yet optimized
First measurements incoming!
Preliminary!
2D APF
Shiloh, R., et al., Nature 597, 498 (2021)
First simulation data: