## Slide 1: Damping Ring and Bunch Compressor design for the C3 collider
Matthew Andorf

## Slide 2: Acknowledgments
SLAC
Emilio Nanni
Marty Breidenbach
Caterina Vernieri
Wei-Hou Tan
Sophia Morton
Cornell
Nigel Lockyer
Jared Maxson
Adam Bartnik
David Sagan
Colwyn Gulliford

## Slide 3: Outline
Motivation for damping ring
Damping ring design concepts
Intrabeam scattering in damping ring + performance
Bunch compressor performance

## Slide 4: Motivation for Damping Rings
Spin Polarized Electron Production:
  GaAs photocathode operated in a DC electron gun
  Round beam, ~2-3 μm normalized emittance
Positron production:
  Tungsten target
  2-3 orders of magnitude larger beam emittance than electron beam
Damping Rings optimize beam luminosity!
  Can produce ~100 nm horizontal emittances
  Produce flat beams, ~1 nm vertical emittance
Beamstrahlung:
  Use of a flat beam reduces beam collision induced radiative losses

## Slide 5: Ring Layout
Most damping designs use a race-track layout:
  Arcs consist of periodic cells designed for low emittance
  Straight sections provide room for damping wigglers, RF cavities and injection/extraction lines
Periodic arc-cells
Periodic arc-cells
Damping wigglers, RF
injection/extraction lines/wigglers
From Booster Linac
(or pre-damping ring)
To Main Linac

## Slide 6: Synchrotron Radiation Damping
Synchrotron radiation damps particle motion in all three planes (horizontal, vertical and longitudinal)
Energy loss from radiation grows with particle’s energy  longitudinal damping
Damping in the transverse plane is the result photon emission (tangential to particle path) + RF energy restoration (longitudinal direction only)
SR damping is countered by quantunm excitation leading to a ‘natural’ or zero-charge beam emittance!

## Slide 7: Damping Ring Basic Considerations
Givens:
  Bunch structure (e.g. bunch spacing, number of bunches per train)
  Collider repetition rate
  Injected beam emittance
Choices:
  Number of stored bunch trains (Ntrain)—determines min. circumference
  Stored number of damping times(Nτ )—constrains value of damping time
  Lattice design, wiggler parameters
Consequences of those choices:
  Beam energy
  Extracted beam emittance

## Slide 8: Arc cell design
Optimal values at dipole center
Bend magnet
Theoretical Minimum Emittance (TME) cells:
  Produce lowest achievable emittance
  Twiss parameters chosen to minimize I5 integral while accounting propagation through dipole
  Does not produce dispersion free section…not a problem for damping rings!

## Slide 9: Arc Lattice design
Emittance scales as θ3.
Number of cells can be varied to achieve design emittance goal.
  Wiggler can reduce emittance further
  IBS will increase final achieved emittance
Some limitations to consider:
  The minimum cell length needs to be achievable from magnet/vacuum design considerations
  TME cells require strong focusing resulting in high chromaticity. Operating at optimum emittance may not be achievable.
  Higher number of cells will result in a tighter alignment requirement (vertical emittance)
  The cost and complexity of building the ring goes up with number of cells

## Slide 10: TME cell
Parameter | Value*
Bend angle (degree) | 3.6
Bend B field (T) | 0.55
Bend Length (m) | 0.7
Bend gradient (T/m) | 12.5
QF1 gradient (T/m) | -31.7
QF1 length (m) | 0.20
ξx/Qx (Normalized natural chromaticity) | -1.8
ξx/Qx (Normalized natural chromaticity) | -2.35
jx | 1.33
ε/εopt | 3.8
* @ 2.5 GeV

## Slide 11: Damping Wigglers
Damping Wigglers can be used to both lower the equilibrium emittance
  Damping rate is proportional to radiative losses around the ring
  I2 is increased due to extra bending (independent of ring circumference) directly lowering eq. emittance
  Faster damping allows reduction in design energy, indirectly lowering eq. emittance
  Wigglers are installed in dispersion free region
  Wiggler ‘self-dispersion’ modifies I5. Wiggler B-field can not be increased arbitrarily emittance growth

## Slide 12: Intrabeam Scattering
IBS: Multiple small angle scattering within beam results in emittance growth in all three planes
Theory simplifies at high energy (“CIMP”), allowing fast computation of IBS effect
  Rates depend only on lattice functions and beam parameters
  Implemented custom CIMP code in python
    Lattice functions extracted from TAO (BMAD)
    IBS rates computed from weighted sum of TME cell/Wiggler (FODO) section
Eq. emittance is a balance between SR damping, quantum excitation and IBS induced growth resulting in ODE system
Solved through combination of integrating ODE and numerical nonlinear solver

## Slide 13: Wiggler Optimization with IBS
Wiggler bend radius and length varied with the following fixed:
  Damping time 6.1 ms (5.5 damping times)
  Bunch charge: 1 nC
  Zero charge bunch length: 1 mm (RF voltage adjusted accordingly)
  100 TME cells, length scaled to fix ring circumference
  Wiggler period, 7.5 cm. Wiggler contained in FODO cell 5.3 m long

## Slide 14: Wiggler Optimization with IBS
Wiggler bend radius and length varied with the following fixed:
  Damping time 6.1 ms (5.5 damping times)
  Bunch charge: 1 nC
  Zero charge bunch length: 1 mm (RF voltage adjusted accordingly)
  100 TME cells, length scaled to fix ring circumference
  Wiggler period, 7.5 cm. Wiggler contained in FODO cell 5.3 m long

## Slide 15: Bunch compression
Short bunch length (100 um) required for main linac
Bunch compressor (BC) between DR and main linac
Trade-off between transverse emittances and longitudinal emittance in DR
Without further acceleration in BC longitudinal emittance is conserved
  Higher compressionhigher resulting energy spread (percent level)

## Slide 16: BACK UP SLIDES

## Slide 17: Bunch Compression
The longitudinal phase-space is uncorrelated leaving the damping ring
RF cavity imparts an energy “chirp” on to the beam correlating position and energy

## Slide 18: BMAD lattice design
Parameter | Value
Bunch Charge (nC) | 0.5
Initial/Final Energy(GeV)* | 4.6/3.9
RF frequency (GHz) | 2.85
L (m) | 1.57
Gradient (MV/m) | -9.17
Cells | 15
Total number of RF cavities | 80
Dipole Length | 2.0
Bend angle (Deg) | 4.58
Bend strength (T) | 0.51
Dipole separation (m) | 4
*non-zero phase chosen to compensate non-linear motion in chicane

## Slide 19: Single particle tracking
Input beam (from DR)
After compressor

## Slide 20: Coherent Synchrotron Radiation
A beam passing through a bend radiates broadband synchrotron radiation (UV—THz)
For wavelengths <<σz the radiation adds incoherently. Intensity scales as ~N
For wavelengths >>σz the radiation adds incoherently. Intensity scales as ~N2
A 1-D model of CSR in a single bend-magnet gives:
Sagan et al, 2009. http://dx.doi.org/10.1103/PhysRevSTAB.12.040703
Where:
For us, R/3=35 pm, while σz/N~0.32 pm (at the start of the chicane, 0.5 nC)

## Slide 21: CSR/Space charge
Particle tracking with CSR and space charge performed for each bunch charge done in IBS study
Work in progress: will extend to higher charge to find maximum achievable luminosity before limited by CSR

## Slide 22: Natural Equilibrium Emittance
SR damping is countered by quantum excitation leading to a ‘natural’ or zero-charge beam emittance
The emission of a photon in a dispersive region results in an increase in betatron motion.
fixed by ring geometry
Optimized by layout of quads/bend magnets
In vertical plane, ultimate emittance set by opening angle of radiation emission
Magnet misalignments and IBS will additionally grow emittance.

## Slide 23: Second order path-lengthening correction
Particle motion through a chicane has a non-linear path lengthening that is quadratic in energy:
We can leverage the (time-dependent) curvature in the RF field to introduce a z2δ on energy.
After a 90 degree phase-space rotation, these correlations cancel
Requires beam to be off the zero-crossing (R66<1) by a small amount

## Slide 24: Transfer matrices
RF cavity
Provides the Energy chirp
Adiabatic damping if <1 (acceleration)
Chicane
R56 provides energy dependent path-length
Total transfer
For an initially uncorrelated beam between energy and position (case for the beam leaving the damping ring):