## Slide 1: US R&D toward a Higgs Factory
J. Ritchie Patterson Cornell University
The US government shutdown prevented many US scientists from being here.

## Slide 2: U.S. Organizational update
Higgs Factory Coordination Consortium
Higgs Factory Circular Collider Organization
Near-term impact on R&D is modest, but in the longer term, research focused strictly on LC will be affected
DOE instruction: shift focus to the Future Circular Collider (FCC-ee)

## Slide 3: Outline
Detector R&D in the Americas
Accelerator R&D in the Americas
HFCC support
Projects receiving HFCC support
Pointer to LCWS talk T 12:20 TVT

## Slide 4: Tracking: Gaseous detectors
Hardware development
Next: Prototype (24 straws) and helium-isobutane gas mixture system U. Michigan
GEANT simulation of 5000 muon hits
HFCC support
Tracking Detectors and Software workshop at BNL, May 2025
Long US involvement in gaseous detectors
Recent activity: Straw Tubes
Recorded electron beam waveform
CERN test beam, Aug. 2025
Ar-CO2(70:30),1bar, 293K
25 um wire radius, 7.1 mm tube radius.
HV=2100V
Next: He-Isobutane
Particle ID via dN/dx (primary ionizations/cm)
Garfield simulations
Physics simulations
Test beam data
Goal: dN/dx in electronics

## Slide 5: Monolithic Active Pixel Sensors (MAPS)
Fermilab
Sensor design, simulations, vendor development, prototype tests
SLAC
NAPA chip targeting 7μm resolution, ~ns timing, ¼ MIP threshold, <10 mW/cm2
using CMOS process via CERN WP1.2 for SiD tracker and ECal
3rd prototype T 12:20 TVT
HFCC support
Lightweight support structures
Integrate services, power management, cooling, data flow, and multiplexing
Jung, HFCC First Thursday meeting, April 2025
Vallone, FCC Tracking Detectors Workshop, BNL 5/25
Proton beam test
~15 μm position res.
35 ps time res.
carbon fiber
A. Habib et al JINST 19 C04033 (2024)
ALICE MAPS vertex detector for HL-LHC
MAPS tracker
High granularity, lightweight, low power detector layers
Stitching for 1000 m2 system
HFCC support

## Slide 6: LGADs: ps timing
CMS Endcap Timing Layer LGAD detector 30-40 ps timestamp
Read out chip and module assembly FNAL
ePIC detector at Electron Ion Collider
AC-LGADs with 25 ps timing
Design of sensors, front-end ASIC and readout electronics BNL, UIC, LANL, ORNL, UCSC, Rice, FNAL, Purdue, OSU, NCKU, IJCLab,CEA Paris-Saclay, OMEGA
Activities sampler
Improving spatial resolution using charge sharing:  10 μm resolution achieved in laser tests. Next: test beam Brown, BNL, Northwestern, Zurich
Radiation damage and single event burnout BNL, Brown, U New Mexico, UCSC
Commercializable design SLAC, FNAL, LBNL T 12:04 TVT
Momentum Scale determination at LC Th 13:15 Soft
Pile up mitigation (HL-LHC)
Particle ID via Time of Flight Outer tracking layer

## Slide 7: Dual readout calorimetry
High-resolution hadronic calorimetry
figure courtesy B. Hirosky
Č and scint light
Scint only
EM and hadronic components fluctuate shower to shower, and they have different light collection effs
Use Č light timing to reveal the nuclear interactions
New: timing observed in test beam
arXiv:2408.15430v1 [physics.ins-det] Feng and Jin talks at CPAD 2025
HG-DREAM
RD52 collab.
Fiber HCal with Quartz (Č emitting) fibers ~30%/√E
New: Observed ~160 Č pe/GeV in BGO in test run at JLab, exceeding goal. Builds on prior test runs at DESY and CERN (2024).
CalVision:
Partnering with Europe’s MaxiCC collab.
HFCC support
SiPM readout
Hirosky, Cummings CPAD 2025
Cummings, 8th FCC Physics Workshop, Jan 2025
Crystal ECal providing high resolution for both EM and hadronic showers
Challenge is Č light yield

## Slide 8: Calorimetry with MAPS
Tungsten/MAPS sampling ECAL
40 GeV π0 → two 20 GeV γ’s
SiD ECal fine pixel MAPS
25μm x 100 μm
EPJ Web of Conferences 315, 03005 (2024)
W 10:00 CalPID
Detailed reconstruction of particles in jet for better particle flow
Exceeds LC energy resolution requirement with digital counts

## Slide 9: Smart detectors: AI and Microelectronics
ML-in-ASIC capabilities for “smart detectors”, e.g.
  Intelligent data handling and power management
  On-board calibration
  On-chip processing to reduce readout
    SmartPixels – ML embedded on ASIC
    eFPGA – integrate FPGA-like logic into an ASIC
  Dynamic readout granularity
Analog on-detector computing to reduce power load
ML for the Front-end (ML4FE) workshop, May 2025
See review Gouskos Th 16:15 plenary
Major US emphasis on AI:
new centers, new initiatives in the pipeline
Smart Pixels:
track parameters on a chip

## Slide 10: Software and Computing
Key4HEP software ecosystem
Analysis Tools and Generators
US Computing Resources
  User facilities
  Future resources for grid computing
See HFCC “First Thursday” meeting, Oct 2025
HFCC Priorities Key4HEP support/development LBNL
Simulation and Analysis Tools support Princeton
Software workshops, training events FNAL
HFCC support
L. Bauerdick, M. Hance
Connection: Optimizing detector layouts

## Slide 11: Outline
Detector R&D in the Americas
Accelerator R&D in the Americas

## Slide 12: Polarized Sources
Photocathodes for polarized electrons
Workhorse: GaAs activated to Neg. Electron Affinity (NEA) with Cs+O  short lifetime due to fragile NEA coating
Improved robustness: Sb based NEA layers, CsI surface treatment
Promising alternatives to GaAs: III-Nitrides (e.g. GaN and InAlGaN) W 12:20 Sources and growth methods W 12:00 Sources
J. Appl. Phys. 137, 224901 (2025)
Electron spin polarization (%)
GaN matches GaAs!
Appl. Phys. Lett. 125, 034107 (2024)
unstrained
Polarized positrons
Build on Ce+BAF effort: 1 μA with > 60% pol’n
See talks on the target W 12:40 Sources, target cooling W 13:00 Sources, and target and beam parameters W 11:20 Sources
US-Japan Collaboration
high power target
120 MeV polarized e–
e+ capture linac
bunch compression
spin rotator
SRF
Polarized e+
matching

## Slide 13: Beam Dynamics & MDI
Detailed simulations of beam-beam interactions using Warp-X
Beamstrahlung at 10 TeV Colliders T 10:20 AAT
Physics impact of beam configurations at 10 TeV T 10:40 AAT
Warp-X vs Guinea Pig
Beam beam simulations at LBNL, SLAC, CEA
J.Instr. 18.06 (2023): T06001
magnetic field streamlines
electron density
positron
density
10 TeV
Direct-wind superconducting magnets for the IP T 10:15 MDI
Improved Luminosity detectors W 10:40 CalPID
Laser collimation of e beams and intensity control at FACET-II W 12:00 DRBD

## Slide 14: Superconducting RF cavities
ILC 1.3 GHz bulk Nb SRF cavities
  TDR performance specs:
  Q0=1x1010, Eacc = 31.5 MV/m
  Impressive progress worldwide since TDR: Impurity infusion, low and mid temp baking, cold electropolishing
  Now feasible:
  Q0=2x1010, Eacc = 31.5 MV/m
  If this can be done at scale, allows 5 Hz  10 Hz rep rate
Cavity shape+High RRR Nb
Nitrogen doping!
High pressure water rinse
EP+low-temperature baking
75/120 C bake/N infusion
Plot: A Grasselino and K. McGee
  High gradient, high Q at JLAB T 12:00 SRF and at FNAL T 12:30 SRF
  Identifying electron emitters T 12:15 SRF
  Can we use materials expertise to make further progress?
  What about traveling wave cavities?
Eacc (MV/m)
U.S. groups

## Slide 15: Alternative superconductors
Nb3Sn
Higher vortex entry field than Nb
 Higher Eacc 100 MV/m max rather than 55 MV/m
Higher Tc than Nb (18K vs 9K)
 Achieves good RBCS at 4K rather than 2K
3.2x more efficient heat extraction  smaller cryoload
Growth is challenging
Tc and vortex entry field sensitive to Nb:Sn ratio
Low thermal conductivity: 1/1000 of Nb
Exciting new result: Eacc=100 MV/m in a small sample using μs pulses (SRF ‘25)
2 μm
Phys. Rev. B 103, 024516 (2021)
Can we use high temperature superconductors for SRF? See talk T 12:45 SRF
REBCO tape

## Slide 16: Update on the Cool Copper Collider
LCWS 2025
LC Vision, evaluated as a standalone and LCF upgrade
250 GeV in 8 km with 70 MeV/m gradient
550 GeV in 8 km with 120 MeV/m gradient
2 TeV in 20 km with 155 MeV/m gradient 230 MW site power
C3 - 8 km Footprint for 250/550 GeV
Recent Updates:
Improved site layout; new beam format 150  110 MW site power, same lumi W 3:45 PL
Optimizing damping rings and bunch compressors W 11:45 DRBD
Beam dynamics/emittance preservation W 11:20 DRBD
Beam-beam interactions Tu 10:35 MDI

## Slide 17: Towards a Cold Copper Demonstration
Highest priority: Demo of main linac technology and specifications
Building main linac raft (~2.5), 2X structures, 1X quad, alignment and positioning W 9:20 NCRF
Planned test with beam at ESRF W 11:30 NCRF, including auxiliary systems LLRF W 9:00 NCRF, alignment W 9:40 NCRF
Leveraging synergies with other applications
  injectors for storage rings
  injectors for collider concepts (FCC-ee)
  e-beam driven positron linac for ILC
  positron linac for HALHF
Quarter Cryomodule

## Slide 18: Toward Multi-TeV
Ghost collider – new ERL-based concept 550 GeV center-of-mass linear collider with four interaction regions, each with the design luminosity Th 10:00 AAT
ReLiC – ERL-based e+e- collider with c.m. energy from 100 GeV to 3 TeV and luminosity between 1036 to 1037 cm–2 s–1 Th 10:20 AAT
CLIC-like Structure wakefield acceleration at Argonne T 10:00 AAT and Short pulse RF for high gradients (~300 MV/m) Th 12:30 AAT
Phys. Rev. Lett. 133, 255001 (2024)
LBNL, UC Berkeley, U Maryland
Channel-guided laser plasma WFA
Laser-driven PWFA T 9:40 AAT
Compact positron source for PWFA studies at SLAC W 11:40 Sources

## Slide 19: The 10 TeV Wakefield Collider Design Study
https://indico.slac.stanford.edu/event/9402/
Laser-Plasma Collider
JINST 2023
The Design Study aims to produce a unified, self-consistent concept for a 10 TeV parton-center-of-mass (pCM) collider based on wakefield accelerator (WFA) technology.
The study is Initiated by the 2023 US P5 Report, but it is a global undertaking.
We will collaborate with on-going design efforts, including ALEGRO, HALHF, ALIVE, and XCC and contribute to the LC Vision program.
This is an HEP-wide community effort. The study involves theorists, experimentalists and Linear Collider experts.
Join the Study!
Overview T 9:00 AAT