## Slide 1: Overview of Wakefield Acceleration Recent Progress and R&D Challenges
M. Turner
1

## Slide 2: Outline
Introduction to Wakefield Acceleration
Recent Experimental Progress
  Laser and Beam Driven Plasma Wakefield Acceleration
Linear Collider Design Studies
  R&D Challenges
  Design Studies
Towards Applications
  Recent Technology R&D Progress
Summary & Conclusion
22.10.2025
M. Turner, LCWS 2025
1 / 16

## Slide 3: High-Gradient Wakefield Acceleration
Includes all concepts that can achieve an acceleration gradient > 1 GeV/m
  High gradients → Compact accelerators → Potentially lower cost & environmental footprint
Wakefields in Dielectric Structures
Laser Driven
Beam Driven
Accelerating gradient on the order of 1 GeV/m
22.10.2025
M. Turner, LCWS 2025
2 / 16
Notes: 3

## Slide 4: High-Gradient Wakefield Acceleration
Includes all concepts that can achieve an acceleration gradient > 1 GeV/m
  High gradients → Compact accelerators → Potentially lower cost & environmental footprint
Wakefields in Dielectric Structures
Laser Driven
Beam Driven
Wakefields in Plasma
Laser Driven
Beam Driven
Session on Advanced Accelerator Technologies
Presentation by X. Lu: Progress and challenges in RF structures for short-pulse SWFA  Thursday 12h30
Session on Advanced Accelerator Technologies
Presentation by M. Konrad: Recent Progress in Dielectric Laser Acceleration  Wednesday 12h30
22.10.2025
M. Turner, LCWS 2025
2 / 16
Accelerating gradient 1-100 GeV/m
Notes: 4

## Slide 5
To be a Candidate for a Linear Collider, Wakefield Acceleration Must Offer a Path To…
High
Energy
High
Efficiency
High
Luminosity
22.10.2025
M. Turner, LCWS 2025
3 / 16

## Slide 6: Outline
Introduction to Wakefield Acceleration
Recent Experimental Progress
  Laser and Beam Driven Plasma Wakefield Acceleration
Linear Collider Design Studies
  R&D Challenges
  Design Studies
Towards Applications
  Recent Technology R&D Progress
Summary & Conclusion
22.10.2025
M. Turner, LCWS 2025

## Slide 7: Outline
Introduction to Wakefield Acceleration
Recent Experimental Progress
  Laser and Beam Driven Plasma Wakefield Acceleration
Linear Collider Design Studies
  R&D Challenges
  Design Studies
Towards Applications
  Recent Technology R&D Progress
Summary & Conclusion
22.10.2025
M. Turner, LCWS 2025

## Slide 8: Recent Progress in Experiments Highlights from Single Stage Experiments  Laser-Driven
Energy
Beam Quality
Efficiency
Winkler, P. et al. Active energy compression of a laser-plasma electron beam. Nature 640, 907–910 (2025).
Energy spread and jitter below permille level by employing active stabilization
 Laser to electron conversion efficiency of at least ∼30%
 Multi-GeV energy gain
E. Rockafellow et a;., High charge laser acceleration of electrons to 10 GeV
NIM A, Volume 1077, August 2025, 170586
Matched Guiding and Controlled Injection in Dark-Current-Free, 10-GeV-Class, Channel-Guided Laser-Plasma Accelerators
A. Picksley et al., Phys. Rev. Lett. 133, 255001 (2024)
 ~10 GeV energy gain over 10 cm
 Multiple acceleration regimes that may be difficult to control
 ~9.2 GeV energy gain over 30 cm
 Laser-created ‘free-standing’ plasma channels that can be recreated at the repetition rate of the laser
 Multiple independent results
C. Aniculaesei et al., The acceleration of a high-charge electron bunch to 10 GeV in a 10-cm nanoparticle-assisted wakefield accelerator. Matter Radiat. Extremes 2024; 9 (1): 014001
22.10.2025
M. Turner, LCWS 2025
4 / 16
Notes: Add logos, add also desy result,
8

## Slide 9: Recent Progress in Experiments Highlights from Single Stage Experiments  Beam-Driven
Energy
Beam Quality
Efficiency
 Emittance preservation at micron level for 40 MeV energy gain (on top of 1 GeV)
 ~60% driver depletion
C Zhang et al 2024 Plasma Phys. Control. Fusion 66 025013
 42% local energy transfer efficiency
C. A. Lindstrøm et al., Phys. Rev. Lett. 126, 014801 (2021)
Lindstrøm, C.A. et al. Emittance preservation in a plasma-wakefield accelerator. Nat Commun 15, 6097 (2024)
Session on Advanced Accelerator Technologies
Presentation by J. Wood: Progress in Experimental Plasma Wakefield Acceleration at FLASHForward, DESY  Thursday 11h50
I. Blumenfeld et al., Nature 445, 741 (2007):
 42 GeV energy gain in 85 cm
22.10.2025
M. Turner, LCWS 2025
4 / 16
Notes: Add logos, add also desy result,
9

## Slide 10
For Now In Experiments:
Choose 1, Maybe 2 (at the same time)
Energy
Efficiency
Quality
Large final energy gain
Small emittance and energy spread, high charge
Minimal power/energy consumption
22.10.2025
M. Turner, LCWS 2025
5 / 16

## Slide 11
Our Community Is Working Towards Delivering Beams With…
Energy
Efficiency
Quality
GeV, TeV
High beam charge and quality
Low power consumption
 Exact needs/tolerances depend on the application
&
&
22.10.2025
M. Turner, LCWS 2025
5 / 16

## Slide 12: Outline
Introduction to Wakefield Acceleration
Recent Experimental Progress
  Laser and Beam Driven Plasma Wakefield Acceleration
Linear Collider Design Studies
  R&D Challenges
  Design Studies
Towards Applications
  Recent Technology R&D Progress
Summary & Conclusion
22.10.2025
M. Turner, LCWS 2025

## Slide 13: Outline
Introduction to Wakefield Acceleration
Recent Experimental Progress
  Laser and Beam Driven Plasma Wakefield Acceleration
Linear Collider Design Studies
  R&D Challenges
  Design Studies
Towards Applications
  Recent Technology R&D Progress
Summary & Conclusion
22.10.2025
M. Turner, LCWS 2025

## Slide 14: Wakefield Acceleration Comes with Unique Challenges
Including:
1) Positron Acceleration in Plasma
  Acceleration in the non-linear regime is not symmetric for positive and negative charges
Images from: https://indico.cern.ch/event/1193719/contributions/5274924/attachments/2617597/4524780/SDiederichs_ALEGRO_2023_Positrons.pdf
+
+
+
+
+
+
+
+
+
+
22.10.2025
M. Turner, LCWS 2025
6 / 16

## Slide 15: Wakefield Acceleration Comes with Unique Challenges
Including:
1) Positron Acceleration in Plasma
  Acceleration in the non-linear regime is not symmetric for positive and negative charges
Images from: https://indico.cern.ch/event/1193719/contributions/5274924/attachments/2617597/4524780/SDiederichs_ALEGRO_2023_Positrons.pdf
Session on Advanced Accelerator Technologies
Presentation by S. Zhou: Advances in plasma-based positron acceleration  Thursday 13h10
Positron acceleration: TRL 1!
+
+
+
+
+
+
+
+
+
+
22.10.2025
M. Turner, LCWS 2025
6 / 16
Wakefields in Dielectric Structures

## Slide 16: Wakefield Acceleration Comes with Unique Challenges
Including:
1) Positron Acceleration in Plasma
  Acceleration in the non-linear regime is not symmetric for positive and negative charges
2) Staging
Driver 1
Witness
Plasma 1
One stage may be sufficient…
22.10.2025
M. Turner, LCWS 2025
6 / 16

## Slide 17: Wakefield Acceleration Comes with Unique Challenges
Including:
1) Positron Acceleration in Plasma
  Acceleration in the non-linear regime is not symmetric for positive and negative charges
2) Staging
  Tight tolerances, matching
  Must be compact
Driver 1
Witness
Driver 2
Plasma 1
Plasma 2
Refocus
Witness
Unit cell
Concepts exist.
No experimental demonstration with high charge transfer yet!
22.10.2025
M. Turner, LCWS 2025
6 / 16

## Slide 18: Wakefield Acceleration Comes with Unique Challenges
Including:
1) Positron Acceleration in Plasma
  Acceleration in the non-linear regime is not symmetric for positive and negative charges
2) Staging
  Tight tolerances, matching
  Must be compact
…
ESPP Input #154: European Accelerator R&D Platform Review for the Laboratory Directors Group (link)
22.10.2025
M. Turner, LCWS 2025
6 / 16

## Slide 19: Outline
Introduction to Wakefield Acceleration
Recent Experimental Progress
  Laser and Beam Driven Plasma Wakefield Acceleration
Linear Collider Design Studies
  R&D Challenges
  Design Studies
Towards Applications
  Recent Technology R&D Progress
Summary & Conclusion
22.10.2025
M. Turner, LCWS 2025

## Slide 20: Strategy 1: Avoid Positron Acceleration
Positron acceleration: TRL 1!
22.10.2025
M. Turner, LCWS 2025

## Slide 21: Collider Design Studies
HALHF Hybrid, Asymmetric, Linear Higgs Factory
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities (C3 technology)
To make most effective use of space  collision of polarised 375 GeV e- with 42 GeV e+
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration in plasma
+ compact footprint, ~5 km
Since 2023
    Asymmetric collisions: 375 GeV polarized e- with 41.7 GeV polarized e+ (boost: γ=1.67), Center-of-mass energy: 250 GeV.
       upgrades 380, 550 GeV center-of-mass energy discussed
Estimated luminosity: 1.2x1034 cm-2s-1  two IPs
Estimated total power usage: 106 MW
Estimated cost: 3.8 BCHF (2024 Swiss francs)
Estimated R&D time (technically limited): 10-15 years
Foster et al., Phys. Open 23, 100261 (2025)
22.10.2025
M. Turner, LCWS 2025
7 / 16

## Slide 22: Collider Design Studies - Challenges
HALHF Hybrid, Asymmetric, Linear Higgs Factory
e- acceleration in e- beam–driven plasma wakefields
e+ acceleration in radiofrequency cavities
To make most effective use of space  collision of 375 GeV e- with 42 GeV e+
Advantages:
+ most advanced wakefield collider concept  avoids e+ acceleration
+ compact footprint, ~5 km
Since 2023
Challenges:
High repetition rate plasma operation and cooling, Staging, Production and acceleration of polarized beams, BDS design,…
10-15 years of R&D
ESPP Input #57: HALHF: a hybrid, asymmetric, linear Higgs factory using plasma- and RF-based acceleration (link)
Next:
Presentation by B. Foster: Hybrid collider concepts
Session on Advanced Accelerator Technologies
Presentation by R. D’Arcy: HALHF: Recent updates, R&D, tools, insights, and plans  Thursday 9h00
Presentation by B. Chen: ABEL, A start-to-end simulation framework for plasma-based and conventional linear colliders  Thursday 9h20
Session on Damping rings, Beam dynamics, Beam delivery systems
Presentation by R. Garcia: Towards a Beam Delivery System for the HALHF Project  Thursday 12h30
22.10.2025
M. Turner, LCWS 2025
7 / 16

## Slide 23: Strategy 2: Avoid Staging
Driver 1
Witness
Driver 2
Plasma 1
Plasma 2
Refocus
Witness
Unit cell
Interstage: conventional magnetic optics and/or plasma lenses
22.10.2025
M. Turner, LCWS 2025

## Slide 24: Collider Design Studies
ALiVE
A Linear accelerator for Very high Energies
e- and e+ acceleration in single stage p+ beam-driven plasma wakefields
  Enabled by the energetic and short p+ drivers
  p+ drivers: high-rep.-rate 500 GeV synchrotron
Advantages:
+ avoids staging
+ compact footprint
+ scaling to higher energies (10 TeV)
Since 2024
Preliminary investigation of a Higgs factory based on proton-driven plasma wakefield acceleration J. Farmer et al., 2024 New J. Phys. 26 113011
Collider Parameters:
Centre-of-mass energy (CoM): 250 GeV Estimated luminosity: 1.7x1034 cm-2s-1
Footprint: ~4 x 2 km.
7 km circumference
high rep. rate: 14.4 kHz
500 GeV p+ synchrotron
Upgrade to ~7 TeV for 10 TeV collisions
22.10.2025
M. Turner, LCWS 2025
8 / 16

## Slide 25: Collider Design Studies - Challenges
ALiVE
A Linear accelerator for Very high Energies
e- and e+ acceleration in single stage p+ beam-driven plasma wakefields
  Enabled by the energetic and short p+ drivers
  p+ drivers: high-rep.-rate 500 GeV synchrotron
Advantages:
+ avoids staging
+ compact footprint
+ scaling to higher energies (10 TeV)
Since 2024
Preliminary investigation of a Higgs factory based on proton-driven plasma wakefield acceleration J. Farmer et al., 2024 New J. Phys. 26 113011
Collider Parameters:
Centre-of-mass energy (CoM): 250 GeV Estimated luminosity: 1.7x1034 cm-2s-1
Footprint: ~4 x 2 km.
Challenges:
High power synchrotron, Proton Bunch Compression, Plasma Source Development, Positron Acceleration, Energy Transfer Efficiency, Beam Quality Preservation,…
ESPP Input #210: Proton-Driven Plasma Wakefield Acceleration for Future HEP Colliders (link)
Session on Advanced Accelerator Technologies
Presentation by J. Farmer: ALiVE: Proton-driven plasma wakefield acceleration for collider applications  Thursday 9h40
22.10.2025
M. Turner, LCWS 2025
8 / 16

## Slide 26: To Achieve This…
Repetition rate
and
Charge per bunch
and
Emittance
Staging
or
Energetic drivers
Wall-plug to Drivers
x
Driver to Wake
x
Wake to Witness

## Slide 27: Preliminary Plasma Collider Parameters
HALHF:
e-: 48 stages x 7.8 GeV = 375 GeV
e+: RF Linac 40 MV/m x 1.05 km= 42 GeV
ALIVE:
e-: 1 x 125 GeV
e+: 1 x 125 GeV
HALHF:
Avg. rep. rate: 16 kHz
Charge per bunch: 1.6 nC (e-) / 4.8 nC (e+)
Emittance (H/V): (90/0.32) mm mrad (e-) / (10/0.035) mm mrad (e+)
Luminosity: 1.2x1034 cm-2s-1 *  two IPs
* (0.76x1034 cm-2s-1 ) in top 1%
ALIVE:
Avg. rep. rate: 7.2 kHz
Charge per bunch: 3.2 nC (e-) / 3.2 nC (e+)
Emittance (H/V): (0.1/0.1) µm mrad (e-) / (0.4/0.4) µm mrad (e+)
Luminosity: 7x1034 cm-2s-1 **
** (0.25x1034 cm-2s-1 ) in top 1%
HALHF (PWFA Linac):
Wallplug-to-driver: 55%
Driver-to-wake efficiency: 80 %
Wake-to-beam efficiency: 50 %
Driver-to-beam efficiency: 40%
Wallplug-to-witness efficiency: 22%
ALIVE:
Wallplug-to-driver: 46 % (assumed)
Driver-to-wake efficiency: 12 % *
Wake-to-beam efficiency: 50 %
Driver-to-beam efficiency: 6 %
Wallplug-to-witness efficiency: 3 %
Luminosity
Energy
Efficiency
* there are avenues to improve
22.10.2025
M. Turner, LCWS 2025
9 / 16

## Slide 28: Strategy 3: Aim Longer Term
First user facilities
Low-Energy
Injector
Particle physics applications
Higgs factories
10+ TeV
collider
O (~GeV)
O (~10s GeV)
250 GeV
10 TeV
 Exploratory studies
~5 years
HALHF
ALiVE
10 TeV Design Study
~10 years
Collider building block
And very high energies: 10+ TeV
22.10.2025
M. Turner, LCWS 2025

## Slide 29: Collider Design Studies
10 TeV Design Initiative for a 10 TeV pCM Wakefield Collider
Technology candidates:
Laser-Driven Plasma Wakefields
Beam-Driven Plasma Wakefields
Structure Wakefields
Collider type:
e+e-
e-e-
γγ
Goals include delivery of:
+ end-to-end design study report in 2028
+ roadmaps and resource estimates
Since 2025
The Design Study aims to produce a unified, self-consistent concept for a 10 TeV parton-center-of-mass (pCM) collider based on wakefield accelerator (WFA) technology.
Assume for now that is an upgrade to another linear collider facility.
Chosen design constraints:
Ez,avg > 500 MeV/m
ℒ/Ptot > 1032 cm-2s-1 MW-1
22.10.2025
M. Turner, LCWS 2025
10 / 16

## Slide 30: Collider Design Studies
10 TeV Design Initiative for a 10 TeV pCM Wakefield Collider
Technology candidates:
Laser-Driven Plasma Wakefields
Beam-Driven Plasma Wakefields
Structure Wakefields
Collider type:
e+e-
e-e-
γγ
Goals include delivery of:
+ end-to-end design study report in 2028
+ roadmaps and resource estimates
Since 2025
Chosen design constraints:
Ez,avg > 500 MeV/m
ℒ/Ptot > 1032 cm-2s-1 MW-1
ESPP Input #98: Design Initiative for a 10 TeV pCM Wakefield Collider (link)
Session on Advanced Accelerator Technologies
Presentation by J. Osterhoff : The 10-TeV Wakefield Accelerator Collider Design Study  Tuesday 9h00
Presentation by C. Schroeder: Design considerations for a laser plasma accelerator based linear collider  Tuesday 9h40
Presentation by L. Verra: Beam-Driven Plasma Wakefield Accelerator for a 10 TeV Wakefield Collider  Tuesday 9h20
Poster by L. Verra: Beam-Driven Plasma Wakefield Accelerator for a 10 TeV Wakefield Collider  Tuesday 9h20
Presentation by P. Piot: Concept for an Energy-Frontier Collider based on Structure Wakefield Acceleration  Tuesday 10h00
Broad participation: detector physicists, particle physicists, etc…
https://indico.slac.stanford.edu/category/138/
209 Endorsers!
22.10.2025
M. Turner, LCWS 2025
10 / 16

## Slide 31: Outline
Introduction to Wakefield Acceleration
Recent Experimental Progress
  Laser and Beam Driven Plasma Wakefield Acceleration
Linear Collider Design Studies
  R&D Challenges
  Design Studies
Towards Applications
  Recent Technology R&D Progress
Summary & Conclusion
22.10.2025
M. Turner, LCWS 2025

## Slide 32: Progress on the Technology R&D Highlights
Efficient Laser Drivers
Plasma Sources
Development of scalable plasma sources at CERN
10 m long Discharge Plasma
1 m long Helicon Plasma
KALDERA  based on Ti:Sa technology, started commissioning
kBELLA  efficient coherent combination of fiber lasers 10’s mJ at kHz, 100+ mJ in progress scheduled for next year
Development of Joule-class kHz laser systems:
Multiple technologies being investigated, e.g. Ti:Sa, fiber lasers, TmYLF, Tm-doped ceramics
2x107 discharges
10-150 Hz operation
ceramic
low voltage solid-state discharge system
 MHz repetition rate
22.10.2025
LPA Guiding channels
Multiple open source codes available to simulate collider quality beams
S. Diederichs et al., Comput. Phys. Comm. 276 108421 (2022) Open-source: https://github.com/Hi-PACE/hipace
HiPACE++
Numerical convergence: few hrs on few GPU’s
Simulation Tools
E.g. using..
M. Turner, LCWS 2025
11 / 16
Notes: Add logos, add also desy result,
32

## Slide 33: + Recent Progress in Experiments
Energy
Beam Quality
Efficiency
Matched Guiding and Controlled Injection in Dark-Current-Free, 10-GeV-Class, Channel-Guided Laser-Plasma Accelerators
A. Picksley et al., Phys. Rev. Lett. 133, 255001 (2024)
 ~10 GeV energy gain over 10 cm
 Multiple acceleration regimes that may be difficult to control
 ~9.2 GeV energy gain over 30 cm
 Laser-created ‘free-standing’ plasma channels that can be recreated at the repetition rate of the laser
 Multiple independent results
C. Aniculaesei et al., The acceleration of a high-charge electron bunch to 10 GeV in a 10-cm nanoparticle-assisted wakefield accelerator. Matter Radiat. Extremes 2024; 9 (1): 014001
Winkler, P. et al. Active energy compression of a laser-plasma electron beam. Nature 640, 907–910 (2025).
Energy spread below the permille level
Employing active stabilization
Lindstrøm, C.A., Beinortaitė, J., Björklund Svensson, J. et al. Emittance preservation in a plasma-wakefield accelerator. Nat Commun 15, 6097 (2024)
 Emittance preservation at micron level for 40 MeV energy gain (on top of 1 GeV)
 ~60% driver depletion
C Zhang et al 2024 Plasma Phys. Control. Fusion 66 025013
 Laser to electron conversion efficiency of at least ∼30%
 Multi-GeV energy gain
E. Rockafellow et a;., High charge laser acceleration of electrons to 10 GeV
NIM A, Volume 1077, August 2025, 170586
 42% local energy transfer efficiency
C. A. Lindstrøm et al., Phys. Rev. Lett. 126, 014801 (2021)
 Towards delivering beams for first applications
Application will be used to mature wakefield acceleration technology
22.10.2025
M. Turner, LCWS 2025
12 / 16
Notes: Add logos, add also desy result,
33

## Slide 34: Summary of Applications Laser-Driven
Laser-Driven Plasma Wakefield Injector for PETRA IV injector complex :
  Final Goal: 6 GeV injector, to decrease the spatial footprint and power requirements
PIP4 CDR A. Martinez de la Ossa et al. doi:10.3204/PUBDB-2024-06078
22.10.2025
M. Turner, LCWS 2025
13 / 16
Notes: Add logos of labs
34

## Slide 35: Summary of Progress on Applications Beam-Driven
Laser-Driven Plasma Wakefield Injector for PETRA IV injector complex :
  Final Goal: 6 GeV injector, to decrease the spatial footprint and power requirements
(Proton-driven plasma wakefield experiment at CERN) Run 2c and d approved  First fixed-target applications after LS4
 CEPC Injector
PIP4 CDR A. Martinez de la Ossa et al. doi:10.3204/PUBDB-2024-06078
Session on Advanced Accelerator Technologies
Presentation by W.Lu: Research platforms on plasma wakefield accelerator and future plans towards colliders in IHEP/SARI/BAQIS/THU Thursday 12h10
22.10.2025
M. Turner, LCWS 2025
13 / 16
Notes: Add logos of labs
35

## Slide 36: Summary of Progress on Applications Laser and Beam-Driven
Laser-Driven Plasma Wakefield Injector for PETRA IV injector complex :
  Final Goal: 6 GeV injector, to decrease the spatial footprint and power requirements
(Proton-driven plasma wakefield experiment at CERN) Run 2c and d approved  First fixed-target applications after LS4
 CEPC Injector
(Particle accelerator research infrastructure based on novel plasma acceleration)
 FEL user facility by 2031
  FEL lasing achieved by 4 groups!
    Enabled by improved beam-quality and stability
PIP4 CDR A. Martinez de la Ossa et al. doi:10.3204/PUBDB-2024-06078
Plenary Session
Presentation by S. Barber: Applications: Near term applications of advanced accelerator technologies: compact free electron lasers Thursday 18h00
Session on Advanced Accelerator Technologies
Presentation by M. Ferrario: The EuPRAXIA project: a plasma-based accelerator user facility for the next decade Thursday 11h30
22.10.2025
M. Turner, LCWS 2025
13 / 16
Notes: Add logos of labs
36

## Slide 37: Outline
Introduction to Wakefield Acceleration
Recent Experimental Progress
  Laser and Beam Driven Plasma Wakefield Acceleration
Linear Collider Design Studies
  R&D Challenges
  Design Studies
Towards Applications
  Recent Technology R&D Progress
Summary & Conclusion
22.10.2025
M. Turner, LCWS 2025

## Slide 38: The Wakefield Accelerator Community Supports a Linear Collider….
Because the key strength of wakefield accelerator lies in the high accelerating gradients
Wakefield acceleration could allow for exciting future energy upgrades and reuse of tunnel infrastructure
  Win-win situation  Proposed by LCV for ESPP
ESPP Input #140: A Linear Collider Vision for the Future of Particle Physics (link)
22.10.2025
M. Turner, LCWS 2025
14 / 16
16 dedicated talks @ LCWS!

## Slide 39: ALEGRO
ALEGRO: Advanced LinEar collider study GROup : An international study group to promote Advanced and Novel Accelerators for High Energy Physics applications.
  Foster and trigger advanced linear collider related activities
  Provide a framework to amplify international coordination, broaden the community, involving accelerator laboratories/institutes
  Identify topics requiring intensive R&D and needed facilities
 Driven by the ICFA-Advanced and Novel Accelerators (ANA) Panel
Main activities:
Organize workshops dedicated to applications of ANAs to particle and high-energy physics.
ESPP Input #159: Contribution of ALEGRO to the Update of the European Strategy on Particle Physics (link)
22.10.2025
M. Turner, LCWS 2025
15 / 16

## Slide 40: Summary & Conclusions
Wakefield accelerators are exciting because of their high acceleration gradients
  > 1 GeV/m
Plasma-based accelerators are approaching the performance levels required for applications
  First applications are expected to come online within the next 5-10 years
Significant progress has been made on collider concepts, including the development of concrete parameter sets
  There are remaining challenges that will require R&D
  Exciting opportunity for an energy upgrade of another linear collider facility
22.10.2025
M. Turner, LCWS 2025
16 / 16

## Slide 41: Thank you!

## Slide 42
Accelerating for e-
Decelerating for e-
Focusing for e-
Defocusing for e-
Drive
bunch
e-
Periodicity: λpe

## Slide 43: Collider-Quality Beams can Now be Simulated with Open-Source Codes
3D quasistatic
Ion motion, ionisation, spin tracking included
Mesh refinement makes simulations in 3D (very) affordable.
S. Diederichs et al., Comput. Phys. Comm. 276 108421 (2022) Open-source: https://github.com/Hi-PACE/hipace
3D full-PIC
modelling of 50 multi-GeV stages
  idealized transport
  low witness bunch charge
J-L Vay et al., WarpX MS FY23.1 and FY23.2 (2023);
256 GPUs for 8h on Perlmutter (NERSC)
Open source https://github.com/Angel/FP/Wake-T moving soon to https://github.com/Wake-T/Wake-T
Ferran Pousa et al., in preparation
WakeT
HiPACE++
WarpX
2D cylindrical, quasistatic
adaptive grid method  fully converged simulations of beams with nm-scale emittance including ion motion, on a laptop
Numerical convergence: 7min on a CPU core
Numerical convergence: few hrs on few GPU’s
Fedeli L, Huebl A, et al. SC22: 2022. DOI:10.1109/SC41404.2022.00008
+ collaborators
Notes: Add logos, add also desy result,
43

## Slide 44: Roadmap based on LDG report findings
LDG
Defined in 2023
Recommendation #1 (link):
Ensure the timely completion of HALHF pre-CDR study and plan for an independent review
Notes: Make this in paralle
44

## Slide 45: Plasma Wakefield Linac
Driver 1
Witness
Driver 2
Plasma 1
Plasma 2
Refocus
Witness
Driver
Plasma
Witness
Driver
Witness
If the single stage energy gain is not sufficient
 Staging until the desired energy is reached
Unit cell
Interstage: conventional magnetic optics and/or plasma lenses
from (link)
Driver loses energy
Witness gains energy
  Energy gain per stage depends on the drive, witness and plasma parameters
One plasma stage may be sufficient
Notes: If we look more closely at a plasma wakefield acceleration stage, we have the driver, which excites a plasma wakefield, and the witness which gains energy from the wakefields. When the driver is a laser pulse, one sometimes adds a guiding channel
45

## Slide 46: FEL Lasing Achieved by Four Groups  Enabled by Improved Beam-Quality and Stability
Wang, et al. Free-electron lasing at 27 nanometres based on a laser wakefield accelerator. Nature 595, 516–520 (2021).
188 MeV, ~6.3% energy spread, ~100 pC
Labat, M., et al. Seeded free-electron laser driven by a compact laser plasma accelerator. Nat. Photon. 17, 150–156 (2023).
Pompili, R., et al. Free-electron lasing with compact beam-driven plasma wakefield accelerator. Nature 605, 659–662 (2022).
Seeded free-electron laser
SASE gain >1000, some gain on >90% events
~100 MeV, 2% energy spread, ~90 pC
S. K. Barber et al., Greater than 1000-fold gain in a free-electron laser driven by a laser plasma
accelerator with high reliability, under review
Beam-driven
5.8 MeV energy gain, 0.3% energy spread, 20 pC
Lasing at 27 nm
490 MeV, ~0.5% energy spread, 30 pC
Notes: Add logos of labs
46

## Slide 47: Progress Towards First Applications
Run 2c and d approved
Separate Self-Modulation from acceleration to accelerate bunches with quality at few GeV energies
Experiments starting in 2029
First applications after LS4
Proton-driven plasma wakefield experiment at CERN
Toward a demonstrator facility for multistage plasma acceleration
Developing:
nonlinear plasma lenses
self-correction mechanisms
 multistage demonstrator facility e.g., with 50 GeV for strong-field QED, to be implemented in a major accelerator lab.
Particle accelerator research infrastructure based on novel plasma acceleration
C. A. Lindstrøm et al., Proceedings of IPAC 2025
ESPP Input #172: AWAKE - Input to the European Strategy for Particle Physics Update on behalf of the AWAKE Collaboration (link)
AWAKE is the first to go
into LS3!
High repetition rate plasma sources
Technology R&D and critical experimental facilities
LPA demonstrator stages (low average power, near collider emittances)
PWFA staging (including low-energy design at EuPRAXIA@SPARC_LAB)
Positron beam test capabilities
FEL user facility starting in 2029