## Slide 1
A Flight Simulator to perform BBA at ATF
P. Korysko*, A. Latina, Wiktoria Malek
LCWS2025
October 23, 2025
*pierre.korysko@cern.ch

## Slide 2
Outline
2
P. Korysko - LCWS2025 - Oct. 23, 2025
The Accelerator Test Facility (ATF)
New Python ATF Flight Simulator
DFS Results in the ATF LINAC and the ATF2 Beamline
WFS Results in the ATF2 Beamline
Conclusions

## Slide 3
The Accelerator Test Facility (ATF)

## Slide 4
The Accelerator Test Facility (ATF)
4
P. Korysko - LCWS2025 - Oct. 23, 2025

## Slide 5
The Accelerator Test Facility 2 (ATF2)
5
P. Korysko - LCWS2025 - Oct. 23, 2025
ATF2 is a test facility to study the feasibility of the Final Focus System [1] that is envisaged in the future linear colliders ILC an CLIC. The primary project goal is to establish the hardware and beam handling technologies pertaining to transverse focussing of the electron beams to 37 nm. All the parameters can be found in the ATF2 design proposal report [2].

## Slide 6
Extensive Simulations done in ATF2
6
P. Korysko - LCWS2025 - Oct. 23, 2025
Simulated errors:
Static errors: - Misalignment of quadrupoles, sextupoles and BPMs of 100 um RMS. - Strength error of quadrupoles and sextupoles of 0.1% RMS. - Roll error for quadrupoles and sextupoles of 200 urad RMS.
Dynamic errors: - Incoming pos./ang. jitter of [0.1σy/y’ - 1.0σy/y’] Simulation procedure:
- Tracking 200 bunches per machine from the ATF extraction line to the IP.
- 100 machines with the previously cited static imperfections.
- Apply the cited corrections and the knobs on the distribution at the IP.
Corrections applied:
- One-to-one - Dispersion Free Steering - Wakefield Free Steering - Knobs (Y, YP D XP XP.*XP XP.*YP XP.*D)
First order*
Second order**
*First order knobs correction by changing the position of final focus sextupoles.
**Second order knobs correction by changing the strength of the final focus sextupoles.
Figure: Positions of the sextupole knobs in the Accelerator Test Facility 2 (ATF2) [5].

## Slide 7
Comparison Simulations/Measurements
7
P. Korysko - LCWS2025 - Oct. 23, 2025
Simulations: Static errors:
- Misalignement of quadrupoles, sextupoles and BPMs of 100 um RMS.
- Strength error of quadrupoles and sextupoles of 0.1% RMS.
- Roll error for quadrupoles and sextupoles of 200 urad RMS.
Dynamic errors:
- Incoming pos. & ang. jitter of 1.0σy and 1.0σy’ respectively.

## Slide 8
One-to-One, Dispersion Free Steering (DFS) and Wakefield Free Steering (WFS)

## Slide 9
One-to-One, DFS and WFS
9
P. Korysko - LCWS2025 - Oct. 23, 2025
The One-to-One correction consists of minimizing the transverse position of the beam, with respect to the beam pipe centre measured at BPMs (inside quadrupoles in this case), using steering magnets [3].
One-to-One
Dispersion Free Steering
The DFS correction consists of minimizing the dispersion effect. In practice, it reduces the orbit difference between two beams with different energies [4].
Wakefield Free Steering
The WFS correction consists of minimizing the orbit difference introduced by wakefields. In practice, it reduces the orbit difference between two beams with different charges [5].

## Slide 10
The ATF Flight Simulator

## Slide 11
P. Korysko - ATF2 Weekly Meeting - June 20, 2025
A first version of the ATF Flight Simulator has been written and tested at ATF2 (called SysID for System Identification).
4 available interfaces for now: - ATF Damping Ring - ATF Extraction Line - ATF LINAC - RF-Track Simulations
The ATF Flight Simulator
11

## Slide 12
P. Korysko - ATF2 Weekly Meeting - June 20, 2025
A tool dedicated to compute Response Matrices
List of correctors to use.
List of BPMs to use.
12

## Slide 13
Response Matrices measured in ATF
13
P. Korysko - LCWS2025 - Oct. 23, 2025
LINAC Damping Ring ATF2 Beamline

## Slide 14
A tool dedicated to corrections
14
P. Korysko - LCWS2025 - Oct. 23, 2025
List of correctors to use.
List of BPMs to use.
Orbit weight Dispersion weight Wakefield weight Nb. of iteration etc

## Slide 15
One-to-One correction in ATF
15
P. Korysko - LCWS2025 - Oct. 23, 2025
LINAC Damping Ring ATF2 Beamline

## Slide 16
DFS in the ATF LINAC
To change the beam energy in the LINAC, the Phase of the Klystron #1 is increased by 5 degrees:
16
P. Korysko - LCWS2025 - Oct. 23, 2025
Response Matrix for DFS in the ATF LINAC with R0 (nominal energy) and R1 (lower energy)
R1 – R0

## Slide 17
DFS in the ATF2 Beamline
To change the beam energy in the ATF2 beamline, the DR Delta-F is decreased by 2 kHz:
17
P. Korysko - LCWS2025 - Oct. 23, 2025
Response Matrix for DFS in the ATF2 Beamline with R0 (nominal energy) and R1 (lower energy)
R1 – R0

## Slide 18
WFS in the ATF2 Beamline
18
P. Korysko - LCWS2025 - Oct. 23, 2025
To change the beam charge in the LINAC/ATF2 beamline, the Laser amplitude is decreased by 20%:
Response Matrix for WFS in the ATF2 Beamline with R0 (nominal charge) and R1 (lower charge)
R1 – R0

## Slide 19
DFS and WFS Impact
19
P. Korysko - LCWS2025 - Oct. 23, 2025

## Slide 20
RF-Track Simulations Interface
20
P. Korysko - LCWS2025 - Oct. 23, 2025
List of correctors to use.
List of BPMs to use.
Maximum transverse orbit excursion
Path to file
https://gitlab.cern.ch/rf-track
RF-Track is a tracking code developed at CERN for the design and optimisation of particle accelerators, offering outstanding flexibility and rapid simulation speed.

## Slide 21
RF-Track Simulations Interface
21
P. Korysko - LCWS2025 - Oct. 23, 2025
Simulation of the excitation of ATF2 beamline correctors with RF-Track:
https://gitlab.cern.ch/rf-track

## Slide 22
Conclusions
22
P. Korysko - LCWS2025 - Oct. 23, 2025
A new Python Flight Simulator has been developed and tested at ATF.
Dedicated tools for Response Matrix calculations and One-to-One correction were implemented in the Flight Simulator and give good results.
Other BBA corrections (DFS and WFS) were tested and give promising results. They will soon be implemented in the Flight Simulator.
A new RF-Track interface has been implemented and tested to simulate, compare and optimise the results directly on the control room computers.

## Slide 23
Thank you

## Slide 24
References
24
P. Korysko - LCWS2025 - Oct. 23, 2025
[1] P. Raimondi, “Novel Final Focus Design for Future Linear Colliders”, PRL 86, 3779.
[2] “ATF2 Proposal”, SLAC-R-771.
[3] M. G. Minty et al., “Correction to: Measurement and Control of Charged Particle Beams”, DOI.
[4] T.O. Raubenheimer et al. “A dispersion-free trajectory correction technique for linear colliders”, NIMA, A302 (1991) 191-208.
[5] T.O. Raubenheimer, “A new technique of correcting emittance dilutions in linear colliders”, NIMA, A306 (1991) 61-64.