## Slide 1: ATF contribution to ITN
Hiroshi Sakai (KEK)
This presentation is based on LCWS2025 presentation of
  Steinar Stepnes, “A linear collider @ CERN“
  Shin Michizono, “ILC Technology Network (ITN)”
https://agenda.linearcollider.org/event/10594/timetable/#20251020
Contents
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
  Worldwide ITN status
Others
Summary

## Slide 2
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
  Worldwide ITN status
Others
Summary

## Slide 3: ILC and the Accelerator Technology
Parameters | Value
Beam Energy | 125 + 125 GeV
Luminosity | 1.35 / 2.7 x 1034 cm2/s
Beam rep. rate | 5 Hz
Pulse duration | 0.73 / 0.961 ms
# bunch / pulse | 1312 / 2625
Beam Current | 5.8 / 8.8 mA
Beam size (y) at FF | 7.7 nm
SRF Field gradient | < 31.5 > MV/m (+/-20%) Q0 = 1x1010
#SRF 9-cell cavities (CM) | ~ 8,000 (~ 900)
AC-plug Power | 111 / 138 MW
SRF
Nano-Beam
e- Source
e+ Main Liinac
e+ Source
e- Main Linac
Detectors
Damping Ring
Interaction point
e-
e+
3
Sources

## Slide 4
Overview of linear collider
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
    SRF
    Sources
    Nanobeam
  Worldwide ITN status
Others
Summary

## Slide 5
e- Source
e+ Main Liinac
e+ Source
e- Main Linac
Damping Ring
Beam dump
Interaction point
Physics Detectors
ILC Technology Network
WPP | 1 | Cavity production | Jp., Eu. ,Kr.
WPP | 2 | CM design | Jp., Eu. ,Kr.
WPP | 3 | Crab cavity | 
WPP | 4 | E- source | 
WPP | 6 | Undulator target | Ger.
WPP | 7 | Undulator focusing | Ger.
WPP | 8 | E-driven target | Jp.
WPP | 9 | E-driven focusing | Jp.
WPP | 10 | E-driven capture | Jp.
WPP | 11 | Target replacement | Jp.
WPP | 12 | DR System design | Jp. Kr., Au.
WPP | 14 | DR Injection/extraction | UK
WPP | 15 | Final focus | Jp., Eu., Kr.
WPP | 16 | Final doublet | 
WPP | 17 | Main dump | Jp.
SRF
e-, e+
Sources
Nano-
Beam
Creating particles Sources
  polarized elections / positrons
High quality beams Damping ring
  Low emittance beams
    Small beam size (small beam spread)
    Parallel beam (small momentum spread)
Acceleration Main linac
  superconducting radio frequency (SRF)
Getting them collided Final focus
  nano-meter beams
Go to Beam dumps
Time-consuming and essential work packages for ILC are summarized as ILC Technology Network (ITN). (from 2023 ~4-year plan)
https://linearcollider.org/wp-content/uploads/2023/09/IDT-EB-2023-002.pdf
ILC Technology Network (ITN)
-- global collaboration program--
  Acc. R&Ds focusing on
    SRF
    e- & e+ Sources
    Nano-beam
ITN is useful not only for the ILC but also for various advanced accelerators.

## Slide 6
e- Source
e+ Main Liinac
e+ Source
e- Main Linac
Damping Ring
Beam dump
Interaction point
Physics Detectors
KEK’s efforts
WPP | 1 | Cavity production
WPP | 2 | CM design
WPP | 3 | Crab cavity
WPP | 4 | E- source
WPP | 6 | Undulator target
WPP | 7 | Undulator focusing
WPP | 8 | E-driven target
WPP | 9 | E-driven focusing
WPP | 10 | E-driven capture
WPP | 11 | Target replacement
WPP | 12 | DR System design
WPP | 14 | DR Injection/extraction
WPP | 15 | Final focus
WPP | 16 | Final doublet
WPP | 17 | Main dump
SRF
e-, e+
Sources
Nano-
Beam
Collaboration with
Europe, Korea,
Experiences at SuperKEKB
ATF collaboration
KEK started the activity from April,2023.
MEXT development of key element technologies to improve the performance of future accelerators program
文科省補助金 将来加速器の性能向上に向けた重要素技術開発
advanced Accelerator element Technology Development (MEXT-ATD) funded by MEXT (7oku-yen(5M dollars)/year)
(2023-2027) -> important budget to operate ATF

## Slide 7
ILC Technology Network (ITN) since 2023
CERN, German, UK,
France, Italy, Spain
Agreement: KEK and CERN
KEK, Korea,
Australia
Agreement: KEK and Korean Univ.
US Labs. join
using Japan-US funding frame (2023-2025)
Global framework

## Slide 8
Overview of linear collider
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
    SRF
    Sources
    Nanobeam
  Worldwide ITN status
Others
Summary

## Slide 9
Production
Component Test
Installation
CM Test
Preparation
L-band SC 9-cell cavity
Power coupler
SCQ magnet
Frequency tuner
Magnetic shield
Vertical test for cavity
High power test for coupler
Cold test for motor
Demagnetization of cryo-vessel
Cryomodule assembly
Cryogenic
CM assembly hall
Radiation shield
Waveguide assembly
Cold test at bunker
Installation into bunker
Conduction cooling system for SCQ
WPP-1/2 cavity fabrication & cryomodule (KEK plan)
~2025
~2027
~2026
2025/26

## Slide 10
Specifications
Type | B
Thermal shield | Single
Vacuum vessel length | 12,652 m
Vacuum vessel diameter | OD965mm, ID946mm
Coupler pitch distance | 1326.7 mm
Cavity length | 1247.4 mm
Takeshi Dohmae/Tomohiro Yamada/Takafumi Hara
3D model of CM with waveguide system
Thermal analysis for 40K shield
ILC “Type B” CM chosen (eight cavities + one SC magnet/BPM)
Single thermal shield @40K (5K dropped (t.b.d.))
Tuner access available
3D model completed
Heat load simulation done (dynamic under progress)
Waveguide support frame designed
Total cost for contract under estimation
A. Kumar
WPP-2 Cryomodule design in KEK
BPM design and test is important for this cryomodule  to be test in ATF

## Slide 11
Overview of linear collider
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
    SRF
    Sources
    Nanobeam
  Worldwide ITN status
Others
Summary

## Slide 12: Undulator scheme and e-driven scheme positron source
Undulator method (baseline): 125 GeV electrons are passed through a helical undulator, and the produced gamma rays hit the target to produce electron-positron pairs. Polarized positrons (30%) are obtained. Need 125 GeV electron beam.
Electron driven method：3GeV electrons hit the target to produce electron-positron pairs. High-energy electrons are not required, and the commissioning of the positron production is independent from electron beam commissioning.
Developed mainly in Japan.
Developed in mainly EU.
Both needs strong target and sophisticated design of Flux concentrator and capture section (cavity and solenoid)  In KEK, prototype of positron source based on e-driven method start to develop.

## Slide 13: WPP-8/9/10: e-Driven positron source in KEK
Fabrication of Target disk (W-Cu)
Install Flux Concentrator (FC)
Fabrication of collimator with pillow seal
Fabrication of solenoid
The infrastructure for positron test stand was developed until JFY2024, including a cold fit test of the W-Cu target. From 2025, we will conduct the accelerator structure fabrication.
Build these parts
Until FY2024
About 200 r p m
with water cooling.
Vacuum is around 10^-6 Pa level. (last year & this year)
rotating target.
Flux concentrator
Movie
Stable rotating target was produced under good vacuum condition.  impressive progress for future e+e- colliders

## Slide 14
Overview of linear collider
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
    SRF
    Sources
    Nanobeam
  Worldwide ITN status
Others
Summary

## Slide 15: WPP-15: Final focus at ATF in KEK
Goal 1: Establish the ILC final focus method with same optics and comparable beamline tolerances
ATF2 Goal : 37 nm  ILC 7.7 nm (ILC250); achieved 41 nm (2016)
Goal 2: Develop the position stabilization for the ILC collision
FB latency 133 nsec achieved (target: < 366 nsec)
positon jitter at IP: 106  41 nm (2018) (limited by the BPM resolution)
History of ATF2 small beam
Nano-meter stabilization at IP
(2018)
FB off
FB on
Long-term (a few days) stabilization is the goal of WPP-15

## Slide 16: WPP-15: Final focus at ATF in KEK
16
Increased operating weeks to 20 weeks in JFY2024.
JFY2024
Install to ATF beamline step-by-step
Magnet mover control system
Skew Sextupole magnets
Wakefield evaluation
Details will be discussed in this project meeting

## Slide 17
Upgrade vacuum chamber to suppress wakefield （JFY2023 prototype、JFY2024 install）
Upgrade precise position control system of magnet（JFY2023 prototype、JFY2024 upgrade、JFY2025 upgrade all）
Upgrade focal magnet
（JFY2024 buy、JFY2025 install）
Upgrade Skew sextupole magnet for beam size adjustment (JFY2023 buy、JFY2024 install)
Upgrade beam size monitor in IP（JFY2024 Upgrade target, JFY2025 Buy Laser）
Development Extraction kicker（JFY2023 buy ceramic chamber、JFY2024 install ceramic chamber、JFY2025 test kicker）
Improvement of timing system（JFY2023 partially upgrade、JFY2024 upgrade completed）
Five-Year Plan and Progress in midterm (nanobeam) (ATF)
under MEXT-ATD program  our mission
The first three years (FY2023-2025) will focus primarily on updating ATF equipment necessary for advancing the nanobeam. The subsequent two years will realize nanobeam generation and stabilization using the updated equipment.
The procurement of equipment, its installation on the beamline, and performance test of the installed equipment have proceeded on schedule until now.
Following picture is our progress of preparing items. Procurement of major equipment for the ATF2 beamline will be completed in JFY2025.
 | 2023 | 2024 | 2025 | 2026 | 2027
Nanobeam | Procurement of High-Order magnets Upgrade of beam operation and equipment | Reduction of wake field and higher order aberration Upgrade of beam operation and equipment | Precise measurement of nanobeam, Upgrade of beam operation and equipment | Improvement of beam turning method (incl. AI) Vertical beam size on IP <37nm | Improvement of beam turning method (incl. AI) Long-term stabilization of nanobeam (for a few days)
The current status is as planned.
(important message)
Next two years is very important to fulfill nanobeam generation (<37nm) and stabilization (for a few days)
(Mission of MEXT-ATD program (ATF operation budget come from this MEXT-ATD program)
ITN goal is same as our MEXT-ATD program

## Slide 18
Overview of linear collider
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
    SRF
    Sources
    Nanobeam
  Worldwide ITN status
Others
Summary

## Slide 19
European ITN related studies (dedicated funding from Japan combined with European resources) are distributed over five main activity areas:
ML related tasks
SRF and ML elements: Cavities and Cryo Module,
Crab-cavities, ML quads and cold BPMs
Sources
Pulsed magnet and wheel/target for undulator scheme
Damping Ring including kickers
Low Emittance Rings
ATF activities, final focus and nanobeams
ATS and MDI
Implementation
CE, Cryogenics
Sustainability, Life Cycle Assessments
EAJADE (EU funding) for training of young scientists (linear and circular machines)
Studies in labs distributed across CERN, UK, Germany, France, Italy, Spain
On-going technical studies in Europe – the ILC technology network topics
See more details in the Venice presentation of Peter McIntosh (LINK)
and
Angeles Faus-Golfe on ATF2-3 (LINK)
Steinar Stapnes

## Slide 20
Worldwide ITN activity
For WPP-1&2 (SRF cavity, CM), single cell cavity production in Korea/Europe started.
U. Hamburg is working for WPP-6/7 (undulator scheme).
JAI (UK) started WPP-14 (DR Injection/extraction, synergy with Diamond Light Source upgrade)
For WPP-15 (Final Focus System), European and Korean researchers have joined to the ATF experiments since 2023.
WPP-1/2 in Asia
WPP-1 in Europe
WPP-2 in Europe
WPP-6 in Europe
WPP-8 in Japan
WPP-14 in Europe
WPP-15 (ATF in KEK)
WPP-9 in Japan
WPP-10 in Japan
WPP-11 in Japan
WPP-17 in Japan
WPP-7 in Europe
The recent status will be reported at the ITN information meeting this week!
Important contribution to ITN from ATF

## Slide 21
Overview of linear collider
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
    SRF
    Sources
    Nanobeam
  Worldwide ITN status
Others (Application & KEK-CERN collaboration)
Summary

## Slide 22
① SRF
Superior energy efficiency has been demonstrated and is expected to be deployed in a wide range of applications (such as semiconductor lithography, compact accelerator for medical/industrial applications)
② Source (especially positron source)
High-intensity positron sources will be required for future collider accelerators (circular colliders such as FCCee and CEPC, linear colliders such as ILC and CLIC, muon colliders (LEMMA), etc.).
Positrons are also useful for exploring physical properties, and high-intensity, slow-positrons are expected for surface structure analysis.
Positron source targets and beam dumps are also closely related to targets for neutron generation and beam irradiation targets used in industrial/medical applications.
③ Nanobeam
  Nano-beam technology can be applied to new-generation synchrotron radiation facilities, etc..
  Advanced beam tuning techniques such as machine learning can be applied to a wide range of accelerators.
Determination of atomic arrangement using slow positrons
https://www.kek.jp/ja/newsroom/attic/PR20191114.pdf
Compact accelerator
Mobile accelerator
ITN WPs can be applied not only to ILC but also to a wide range of advanced accelerators
Advanced Accelerator Development through ITN
Extreme ultraviolet (EUV) lithography based on ERL technology
Synergy about new-generation light source (ex. Diamond Light source)
We want to express our nanobeam technology to other application.
Do you have some other idea except for the following items ?

## Slide 23
Overview of linear collider
ILC technology Network (ITN)
  ILC Accelerator
  R&D of ILC Technology Network (ITN)
    SRF
    Sources
    Nanobeam
  Worldwide ITN status
Others
Summary

## Slide 24: Summary
Linear colliders such as ILC, LCF and CLIC are promising to realize higher CM energy than 350 GeV.
ILC is a global project to realize 250 GeV CM by using SRF technology.
Current ILC global organization is ILC International Development Team (IDT) .
The ILC key technologies are “SRF”, “Sources” and “Nano-beam”, which are carried out through “ILC Technology Network” (ITN) by IDT.
KEK obtained a budget for these R&Ds and started the activity from April,2023.
Worldwide ITN activities - the European part - is well underway (ref page 25).
ITN WPs (SRF, Sources and Nano-beam) can be applied to various advanced accelerators (and industry/medical).
Future development of LCF at CERN strongly linked to the ITN technical WPs
(Now we are summarizing “ITN midterm report”.)

## Slide 25: Thank you for your attention

## Slide 26: Manufacture methods of Fine-Grain / Medium-Grain Nb discs
Fine Grain Nb fabrication
Forging
Niobium ingot
(Raw material)
Nb melting
Nb Ingot
Ingot, forged
and annealed
Direct slice of MG ingot
Ingot
Slicing image by wire-saw
Fine Grain (FG) Disc
Grain Size: 50 - 100 um
A New Approach:
Medium Grain (MG) Disc
Grain Size < 1 mm
Aiming for clean, mechanically stable, and cost-effective SRF cavity production.
FG Nb
MG Nb
Rolling

## Slide 27
Six 1-cell cavities produced
Three 9-cell cavity produced
Six 9-cell cavities are under production
Takayuki Saeki/Takeshi Dohmae
The world’s first MG cavity!
These cavities are made by RI!
(for the first time at KEK)
Cavity Fabrication Facility
Large EBW
Small EBW
Chemical polish
Press machine
3D measurement device
New cryopump replaced
Large/Small EBW machines
Categories related to HPGS
WPP-1 cavity fabrication by KEK

## Slide 28
Based on the results of past R&D, we chose 2-step baking for this project.
VT for six 1-cell cavities was successfully done, 9-cell cavities will start from next year.
Cold EP
Baking
Heat treatment
VT
Kensei Umemori/Ryo Katayama
All cavities passed the spec. ±20%!
KEK’s recipe
Surface treatment recipe at KEK