## Slide 1
Flight Simulator (CERN)
P. Korysko*, A. Latina, Wiktoria Malek
ATF Project Meeting
November 28, 2025
*pierre.korysko@cern.ch

## Slide 2
Outline
2
P. Korysko - ATF Project Meeting - Nov. 28, 2025
CERN Python ATF Flight Simulator.
DFS & WFS Results.
RF-Track Simulation Results.
Future Steps.
Plans for ATF3.
Conclusions

## Slide 3
One-to-One, Dispersion Free Steering (DFS) and Wakefield Free Steering (WFS)

## Slide 4
One-to-One, DFS and WFS
4
P. Korysko - ATF Project Meeting - Nov. 28, 2025
The One-to-One correction consists of minimizing the transverse position of the beam, with respect to the beam pipe centre measured at BPMs (inside quadrupoles in this case), using steering magnets [3].
One-to-One
Dispersion Free Steering
The DFS correction consists of minimizing the dispersion effect. In practice, it reduces the orbit difference between two beams with different energies [4].
Wakefield Free Steering
The WFS correction consists of minimizing the orbit difference introduced by wakefields. In practice, it reduces the orbit difference between two beams with different charges [5].

## Slide 5
The ATF Flight Simulator

## Slide 6
P. Korysko - ATF2 Weekly Meeting - June 20, 2025
A first version of the ATF Flight Simulator has been written and tested at ATF2 (called SysID for System Identification).
4 available interfaces for now: - ATF Damping Ring - ATF Extraction Line - ATF LINAC - RF-Track Simulations
The ATF Flight Simulator
6

## Slide 7
P. Korysko - ATF2 Weekly Meeting - June 20, 2025
A tool dedicated to compute Response Matrices
List of correctors to use.
List of BPMs to use.
7

## Slide 8
Response Matrices measured in ATF
8
P. Korysko - ATF Project Meeting - Nov. 28, 2025
LINAC Damping Ring ATF2 Beamline

## Slide 9
A tool dedicated to corrections
9
P. Korysko - ATF Project Meeting - Nov. 28, 2025
List of correctors to use.
List of BPMs to use.
Orbit weight Dispersion weight Wakefield weight Nb. of iteration etc

## Slide 10
One-to-One correction in ATF
10
P. Korysko - ATF Project Meeting - Nov. 28, 2025
LINAC Damping Ring ATF2 Beamline

## Slide 11
DFS in the ATF LINAC
To change the beam energy in the LINAC, the Phase of the Klystron #1 is increased by 5 degrees:
11
P. Korysko - ATF Project Meeting - Nov. 28, 2025
Response Matrix for DFS in the ATF LINAC with R0 (nominal energy) and R1 (lower energy)
R1 – R0

## Slide 12
DFS in the ATF2 Beamline
To change the beam energy in the ATF2 beamline, the DR Delta-F is decreased by 2 kHz:
12
P. Korysko - ATF Project Meeting - Nov. 28, 2025
Response Matrix for DFS in the ATF2 Beamline with R0 (nominal energy) and R1 (lower energy)
R1 – R0

## Slide 13
WFS in the ATF2 Beamline
13
P. Korysko - ATF Project Meeting - Nov. 28, 2025
To change the beam charge in the LINAC/ATF2 beamline, the Laser amplitude is decreased by 20%:
Response Matrix for WFS in the ATF2 Beamline with R0 (nominal charge) and R1 (lower charge)
R1 – R0

## Slide 14
DFS and WFS Impact
14
P. Korysko - ATF Project Meeting - Nov. 28, 2025

## Slide 15
RF-Track Simulations Interface
15
P. Korysko - ATF Project Meeting - Nov. 28, 2025
List of correctors to use.
List of BPMs to use.
Maximum transverse orbit excursion
Path to file
https://gitlab.cern.ch/rf-track
RF-Track is a tracking code developed at CERN for the design and optimisation of particle accelerators, offering outstanding flexibility and rapid simulation speed.

## Slide 16
RF-Track Simulations Interface
16
P. Korysko - ATF Project Meeting - Nov. 28, 2025
Simulation of the excitation of ATF2 beamline correctors with RF-Track:
https://gitlab.cern.ch/rf-track

## Slide 17
RF-Track Simulation Results
17
P. Korysko - ATF Project Meeting - Nov. 28, 2025
Simulations of the one-to-one/DFS/WFS corrections with RF-Track:

## Slide 18
Next Steps?
18
P. Korysko - ATF Project Meeting - Nov. 28, 2025
The following modules could be added to the CERN Flight Simulator:
Control of the mOTR system.
TWISS parameters measurement.
Emittance measurement.
GUI for CCD Cameras (OTR/YAG screens).
Wakefield Knobs.
EXT/FF Orbit Bump

## Slide 19
Towards ATF3 goals
19
P. Korysko - ATF Project Meeting - Nov. 28, 2025
The Flight Simulator and the embedded corrections will be useful tools to sustain a 37nm beam for couple days by:
Correcting the Dispersion and Wakefield effects.
Correcting the impact of the slow drifts.
Correcting the incoming position and angle jitters.
Simulation

## Slide 20
Plans for ATF3
20
P. Korysko - ATF Project Meeting - Nov. 28, 2025
Use of Machine Learning, directly implemented to the Flight Simulator for a better and faster tuning and correction. There would be 3 approaches:
Supervised Learning: The computer is presented with example inputs and their desired outputs (useful for corrections like one-to-one, DFS, WFS).
Unsupervised Learning: No labels are given to the learning algorithm, leaving it on its own to find structure in its input (useful to understand problems like intensity-dependent effects).
Reinforcement Learning: a raw data input is given to a “agents” who learn to make decisions by interacting with their environment.

## Slide 21
Plans for ATF3
21
P. Korysko - ATF Project Meeting - Nov. 28, 2025
Example of Unsupervised Learning: Singular Value Decomposition (SVD)

## Slide 22
Conclusions
22
P. Korysko - ATF Project Meeting - Nov. 28, 2025
A new Python Flight Simulator has been developed and tested at ATF.
Dedicated tools for Response Matrix calculations and One-to-One correction were implemented in the Flight Simulator and give good results.
Other BBA corrections (DFS and WFS) were tested and give promising results. They will soon be implemented in the Flight Simulator.
A new RF-Track interface has been implemented and tested to simulate, compare and optimise the results directly on the control room computers.
New tools could be implemented in the next version (mOTR system, emittance calculations, etc.).
Several Machine Learning techniques for tuning & corrections are being studied.
The Flight Simulator would be a useful tool to help achieving ATF3 goals.

## Slide 23
Thank you