DHCAL Acquisition with HaRDROC VFE
Vincent Boudry
LLR – École polytechnique

---
Preliminary remarks
My current understanding...
First detector with 2nd generation ASICs and 2nd generation DAQ
  - Integration of HaRDROC VFE chip in the PCB
1m³ ≡ (here!) 70×70×100 cm³
1×1 cm² cells (plus margins)
  - ➔ 4096 channels / layer
    × 40 planes = 163 840 channels
Occupancy: ~1000 channels/layer after zero suppression

---
HaRDROC
(Hadronic RPC Detector Read Out Chip)
64 channels	➔ 2560 Chips in 1m³
2 thr. with integrated DAC
External or internal trigger
power pulsing + full storage (depth: 128 )
Data format :
  - Energy: 2 bits / ch
  - 2bit × 64ch+24bit(BCID)+8bit(Header)
    = 160 bits per ASIC and per event
  - × 128 (full depth) = 20kbits per ASIC
1 serial link @ 1 Mhz for readout
One additional seried analog output
Vincent Boudry

---
DAQ with VFE
DIF
USB
SCS
I
FE-FPGA
BOOT CONFIG
Data Format
Zero Suppress
Protocol/SerDes
FPGA Config/Clock Extract
Clk
Clock
VFE ASIC
Bunch/Train Timing
Config Data
I/O
Buffer
ADC
Data
Slab
FE
FPGA
PHY
Data
Clock+Config+Control
VFE
ASIC
Conf/
Clock
VFE
ASIC
VFE
ASIC
VFE
ASIC
RamFull
Analog output
8×32 test card (Being equiped)

---
Timeline (reminder)
Test assembly of RPC on PCB in may-june 07
  - Load parameters
  - Analog readout (cosmics)
Beam test in Jul/Aug 07:
  - a single slab in beam @ DESY
  - Needs a Single Slab DAQ (Digi & Analog readouts)
    on 4 ASICs (256 ch.)
End '07 – Beg '08: a full layer (8×8 ASICs, 4096 ch.)
  - DAQ0 Digital & Analog readout for at least one PCB
End of 2008: full 1 m³ module
  - Full DAQ2 (digital readout of ~160k channels)

---
Single Slab DAQ (SSD): Digital
For test of single 8x32 slab
        - Debug of digi readout;	Assembly test
Loading of parameters
USB based
Readout of digital part through the daisy link
2 implementations being developped
  - LabView based
    [R. Dellanegra – IPNL]
    - LAL Code for HaRDROC test card
    - To be extended for
      4 ASICs
    - Work just started
      ➔ fast working setup
  - C based
    [C. Jauffret – LLR]
    - Firmware + software being written and tested on HaRDROC testcards (1 ASIC)
    - ➔ 8x32 cards (4 ASICs) next week
    - Aims higher perf & developpement
      ➔ DIF card & Analog readout

---
SSD (Analogue)
  - Backup (local) plan
  - Use the LLR ECAL cosmic test DAQ for analog readout
    - was used for ECAL cosmic test
    - full Compatibility with CRC
      ➔ minimal adaptation needed
    - Nat. Instr. commercial acq. card
      & CPLD based controller card
    - All HW elements avail. in double
  - To do [C. Jauffret]
    - modify PCB firmware from C based
      DAQ (cycling readout / delays)
    - Small modif software / firmware
      (written for ECAL)
  - Initial plan:
  - Readout of analog part by a CRC card
  - To do [...?]
    - Write DIF firmware (cycling readout)
    - Modified software (data integration) & CRC firmware
  - Pbm:
    - availability of CRC (in DESY ?)
    - manpower ?

---
Cosmic test bench DAQ
    - Designed to be compat. with the CRC
    - 24 diff. Channels
    - Multiplexed readout at 1.25Mb/s (total)
    - 12bit dynamics
    - DAC output for calibration
    - Minimal changes in readout sequences
18

---
DAQ2 (needed for the m³)
DIF: Det. Specific. FE
  - To be defined next...
Constraints (M. Wing):
LDA: concentrator card
  - 1 Gbits/s output
  - Up to 50 DIF input (#pins of the FPGA)
    ➔ 20 Mbits/s per DIF
ODR: readout card
  - Can reads 2 LDA @ 1 GB/s
  - Links are expensive
DHCAL

---
DIF card
Reads out a complete Slab
Load and control HaRDROC's
Zero suppression (& compression ?)
Reads serially HaRDROC's (serial link @ 1 Mhz)
  - 160bits per ASIC × number of BC (<128) ≤ 20480 bits/ASIC
  - Readout time ≤ 20 ms/ASIC
    - Evently a problematic for testbeams, not for final det.
Optimal number of ASIC / DIF ?
  - Ideally (for TB): 20 ASIC lines per DIF read in parallel
  - But:
Interface with LDA
    - Data, Clock & Control
Size of PCB (1 ASIC ➔ 8×8 cm²) ➔ price, ...
Serial lines on PCB += 8 cm / ASIC,
non terminated (to lower power cons.)

---
DIF/PCB configurations
On PCB DIF
1 line of 4 ASICs
16 DIF / layer
➔ 16×1 Mb/s
Intermediate concentrator
Option
2 lines of 4 interleaved ASICs
➔ reduces
readout time
occupancy / line
32×16
4 lines of 8 ASICs
readout in //
2 DIF / layer
➔ 8×2 Mb/s
2 LDA / Module
32×8
8 lines of 4 ASICs
readout in //
2 DIF / layer
➔ 2×8 Mb/s
2 LDA / Module
Separated DIF
64×8
+++
8 (16) ASICs readout in //
1 DIF / layer
➔ 16 Mb/s
1 LDA / Module
---
Bigger FPGA
Length of lines

---
LDA & ODR cards
        - Need 1 LDA (prototype ?) for end 2007...
        - Q? integration with data flux of other det.
OK for 1 layer
Challenging for 1 m³ ???
✔

---
Conclusion
Schedule is tight
2 solutions for digi readout of a ”8×32” SLAB
2 possible solutions for a analog Single Slab DAQ for july test
  - Using 1 DESY CRC if avail.
  - LLR Cosmics Test bench for backup/local solution
Full layer beg. '08 needs functionnal
  - DIF proto(s) (being defined)
  - ODR + LDAs protos
Good training field for the DAQ2 preparation

---
VFE DAQ code (C. Jauffret)
Local
State Machine
ASICs
Interface
Acquisition
ReadOut
Monitoring
1st DAQ
Interface
USB
Interface
Blocs
RAM
Driver Interface
Local State Machine
Driver Hardware interface
API
Data
Config
Protocol
CMD|ADDR
2nd ADDR,
Data
Config,
Readout