Integrating Magnet Mover Limits into Tuning Simulations
Stephen Molloy
13th November, 2007
SLAC

---
Mover Geometry
Cams
  - R = 31.0 mm
  - L = 1.5875 mm
Magnet support
  - (taken from FFTB database)
  - a = 145.25 mm
  - b = 115.036 mm
  - c = 123.952 mm
  - S1 = 34.925 mm
  - S2 = 290.5 mm

---
Calculate cam angles from magnet position

---
X = 0, Tilt = 0

---
X = 0, Tilt = 4 mrad

---
Magnet movers in tuning code
Include mover limits in tuning algorithms
  - Stop simulation if mover attempts to break limit
100 seeds – 28 failed due to mover limits
  - 14 during initial steering
  - 10 during BPM-quad alignment
  - 4 during the final sextupole tuning
The 4% failure for sext tuning may ignored as negligible
  - These could be fixed by realigning the machine.
24% failure during initial steering and alignment not negligible
  - Must alter algorithms
    - Tighter constraints on magnet motion?

---
ATF2 Simulation GUI
Live demo...