SiTRA test beams at CERN: infrastructure developments and results
Annual EUDET meeting
NIKHEF
Alexandre CHARPY

---
General Overview
Mechanics
  - Module conception
  - Tools development
  - Clean room
  - Modules manufacturing
DAQ
  - FEE electronics
  - ALTERA 2
  - Software development
Status of the last test beam
  - Overview
  - Some results
Project
  - Test SiTr130-88 chip
  - Alignment study

---
Status of the 2007 beam-test and testbench with source @ Paris
Faraday cage @ Paris:
3D table
PM + Scintillator for triggering
Infrared laser
Radioactive source	Sr90

---
Status of the 2007 beam-test and testbench with source @ Paris
Some results of VA1
Pedestal subtraction
Common noise study
Signal to Noise

---
Status of the 2007 beam-test and testbench with source @ Paris
Some results of SiTr130-4:
Pedestal study (vs channel, sample ...)
Signal to noise Vs Channel
Signal to noise
Linearity

---
Project
Testing the SiTr130-88 chips
  - New HPK sensors performance characterization
  - Performance extraction of the new chip SiTr130-88 (more statistics)
  - Alignement system (M.Fernandez Garcia, I.Villa)
Develop an environnement for modules manufacturing for EUDET collaboration (G.Badet, A.Charpy, G.Daubard, C.Evrard, P.Ghislain, D.Imbault, P.Repain)
  - parameters of HPK sensors: dimension, pitch, transparency
  - Front-end electronics
  - Development of toolbox
  - Clean room installation

---
Mechanic development
Module conception (LPNHE team)
Modules with two sensors
Different FEE (chip development)
Bonding constraints (I.McGill)
Faraday cage integration
Alignment study
Easy and secure handle
Study for global structure
Schematic view
0.6
15.71
PA
FEE
VA1
1.6
0.14
5.0
0.3
1.24

---
Mechanic development
Tools conception for “automated” manufacturing
Precise alignment of the different
parts of the modules:
silicon strips
pitch adapter connectivity
FEE
Analogical video camera
Suction system with micro metric screw
System tolerance
Perfect integration on the carbon fiber support during the gluing

---
Mechanic development
Tools conception for “automated” manufacturing
Keep alignement during the gluing process
Perfect integration on the carbon fiber support during the gluing
Gluing tool
Suction transfert tool

---
Mechanic development
Work environement
Definition of the procedure and the critical point during the assembly
Installation of the cleanroom and the first module is done

---
Mechanic development
Work environement
Definition of the procedure and the critical point during the assembly
Installation of the cleanroom and the first module is done

---
Mechanic development
Work environement
Definition of the procedure and the critical point during the assembly
Installation of the cleanroom and the first module is done

---
Mechanic development
Work environement
Definition of the procedure and the critical point during the assembly
Installation of the cleanroom and the first module is done

---
Mechanic development
Faraday cage (I.Villa and V.Saveliev)
Example of configuration:
Two reference sensors equipped
with the VA1' chip
Sensors equipped with SiTr130-88 chip
Collimator for alignment study
Possibility to do a “standalone” tracking
+ EUDET tracking

---
Data Acquisition System
Flexible system: work with VA1 chip, SiTr130-88 (A.Comerma, H.PHAM, R.Sefri), and future
Idea: develop a DAQ, can work in EUDET environnement or on standalone for local test
Easy upgradable system → FPGA board with USB output/input
Real tool box to automatize the different study: pedestal, calibration, alignment etc ....

---
Data Acquisition System
Hardware parts
FPGA board with USB connexion (A.Comerma) – VHDL code to manage (M.Dhellot, A.Charpy):
SiTr-130 and FEE acquisition for tracking
VA1 acquisition for reference tracking

---
Data Acquisition System
Software parts
Slow control is managed by Labview code (J.F.Huppert)
DAQ system is written in C++ and using the Root framework (C.Ciobanu, A.Charpy):
Set the DAQ system and chip configurations
Written the raw data
Possibility of on-line monitoring
Send the data to EUDET DAQ system if needed

---
Data Acquisition System
Software parts
DAQ system is written in C++ and using the Root framework (C.Ciobanu, A.Charpy):
XML Documentation generated by Doxygen (Activity diagram, time diagram)
Universal raw data format
Unified the control command for the DAQ system
Possibility of on-line monitoring
Send the data to EUDET DAQ system if needed

---
Summary
Mechanical status
  - Tools are ready to produce the module sensors
  - Availability for EUDET collaboration → Need to know new specification for tool customization or if changes is needed
DAQ status
  - VHDL and C++ code is under development (will be ready for the next testbeam)
  - Next step: SiTr130 management
Next tasks
  - Validation of the DAQ system
  - Behaviour study of the electronics and sensors with local tests
  - Characterization of the new SiTr130-88 chips → beam test @ DESY in March 2009
Status is available on the following link: http://lpnhe-lc.in2p3.fr/internal/Status.html

---
Thanks