ATF2 IP Tuning Task Simulation Updates
Glen White, SLAC
January 28 2009

---
IP Tuning Simulations with Lucretia Update
Tuning performance including Multipole effects with rematched optics.
Effect of Kubo DR simulation match parameters.
Performance with measured vertical alignment.
Effect of more realistic mover performance settings.
TO DO list

---
Vertical Survey Data
Use vertical alignment data from Sugahara-san.

---
Multipole Measurements
Measured multipoles exist for final focus bends, sextupoles and final doublet quads.
All have minimal effect on beam size and tuning process other than those highlighted above.
<0.12
<0.05
<~0.01
<0.025
 <0.03
Tolerance
(tightest)*
0.0027
0.036
0.0128
0.0058
0.0274
QF1 at
77.5 amps
0.0027
0.036
0.007
0.0052
0.0255
QD0 at
132.2 amps
20pole/quad
12pole/quad
10pole/quad
Octupole/quad
Sextupole/quad
Magnet Name

---
Tuning Results
MAPCLASS rematching improves performance even over case where no multipoles were added.
Better vertical alignment has noticable effects in tail of tuning distribution
90% seeds tune < 41-42nm
50% seeds tune <37-39nm
No QF1 12 pole

---
Tuning Results with QF1 12-pole
Tuning results including QF1 12-pole component, with horizontal emittance = 3um.

---
QF1 12-pole
MADX (left) Lucretia (right)
IP vertical beamsize scales strongly with horizontal emittance

---
QF1 12-pole Tilt
6 um Horizontal
Emittance
Effect of 12-pole changes dramatically with tilt angle.
Around measured value- effect ~875urad/nm
Magnetic measurement error ~0.01% (~40urad).

---
Horizontal Emittance at ATF
Only get simulated 3e-6 emittance at low charge. 1E10 charge implies min RMS y size of ~60nm.
Get large RMS sigma_y due to high tail-population (will be measured by shintake monitor?).

---
Increase Horizontal IP Beta
Horizontal (right) and vertical (left) beam size at IP with increasing horizontal emittance with normal and 2* normal IP horizontal beta function.

---
Beam measurement of 12-pole?
Scan beam past QF1 (need ~ +/- 15mm)
Possible with +/- 60urad kick from ZV11X
Plots show how p5 term of polynomial fit to curve at IP assuming 100nm resolution measurement (left) and 10nm (right)

---
Introduce Skew Dodecapole Magnet
Skew dodecapole 0.7456m from QF1 front face, strength: K5Ls=1424122.25 m^{-5}

---
Input Parameters from Ring Extraction point
Input match conditions used from Kubo DR simulation input (100 seeds), red line shows design model parameters.

---
Tuning Simulation Results
Vertical waist size at Shintake IP compared with last simulation (left)
IP vertical size in comparison with best achievable given input emittances (right)

---
Tuning Time
Comparison of tuning time with previous simulation (left) (adds ~4 hours tuning time in slowest 10% of seeds)
Effect of adding finite mover speed (right) (adds ~6 hours of tuning time in slowest 10% of seeds)

---
Relaxed Mover Precision
Effect of reducing mover precision to 1um
Tunes faster due to relaxed tolerance on where sextupoles move to during multi-knob moves.

---
Tasks to do
Full tuning sim with 12-pole
Lucretia/PLACET cross-checks
Performance vs. IP beta_y and beta_x
Write tool to keep track of magnet mover in/out of range for FS
  - Use to check not move out of range in simulations.
Use SM sim in main simulation.
Dynamic simulations with tuned lattice.
Faster Sext mover system project.
Start writing FS tuning tools now.