## Slide 1: Hadron Shower Development in BGO, Take II
Adam Para
January 23, 2009

## Slide 2: Goals and Purposes
Study the spatial (and temporal) distribution of energy deposition inside hadronic showers in BGO (and other crystals)
To optimize the dimensions of the test beam hadron calorimeter prototype
Test beam module must be ‘right-sized’ to serve its function as a proof of the high resolution calorimetry:
  If it is ‘too small’ than the leakage fluctuations will dominate the energy resolution
  If it is ‘too big’ it is too expensive to be constructed
Goal: demonstrate the resolution ~0.1/sqrt(E), hence need the leakage fluctuations to be well below that:
  0.7% @ 100 GeV, 1.5% at 25 G2V, 2% at 10 GeV ?

## Slide 3: Tools
SLIC-framed Geant 4 (Hans Wenzel)
3 x 3 x 3 m cube of material, subdivided into 1 cm3 volumes
BGO, density of 7.13, n=2.21
Particles deposited at z=-100 cm in a positive z direction
Pions, protons and muons, energies 1,2,5,10,20,50 and 100 GeV
Cube center = x = y = z = 0

## Slide 4: Average hadron shower Profile: p-.10 GeV

## Slide 5: Average Hadron Shower Profile
On average: hadron shower is a very narrow central tube with an radius of few centimeters and a diffused cloud extending to the radii of 50-60 cm

## Slide 6: Average Transverse Shower Profile

## Slide 7: Average Transverse Shower Profile
On average:
There is a significant amount of energy back-scattered. It is emitted in a cone with a radius ~ 20 cm
Shower is very collimated in the first 50-100 cm of the detector
Bayond ~ 1m after the particle entry point the energy is diffused over the radii up to 40-50 cm

## Slide 8: Longitudinal Shower Profiles: Muons, Pions and Protons

## Slide 9: Integrated Longitudinal Shower Profiles (Containment)

## Slide 10: Longitudinal Shower Containment
For 1 meter long detector there is a significant fraction of energy leaking, this fraction grows with the incoming particle energy.
Leaking energy will degrade the intrinsic energy resolution
Restricting the analysis to the events with no leakage (transverse or longitudinal) has a potential of biasing the sample to produce too optimistic energy resolution
The longitudinal leakage has two contributions: some showers are longer than the detector, some showers start very late and only see the small fraction of the calorimeter
Selection of ‘early’ starting showers is provides an unbiased sample of interactions.

## Slide 11: Interaction length, pions

## Slide 12: Interaction length, protons

## Slide 13: Interaction length
Protons have ~ 20 cm interaction length
Pions have ~ 24 cm interaction length
Selecting events starting within the first 10 cm will provide a reasonable size sample of interactions to study the detector performance

## Slide 16: Shower Containment
Careful optimization is necessary
Large transverse size (R~50-60 cm) and a long (-130-150 cm) calorimeter is necessary to reduce the leakage to 2-3%, even for early starting showers.
The quantity of primary interest is the energy resolution, not a leakage per se.
Leakage causes, in general, deviations from the gaussian shape of the response and long asymmetric tails. Simple RMS is not necessarily a good measure of the resolution.
Need to find a sensible Figure of Merit to optimize the size of the detector