CLIC Main Beam RTML
- Overview
- Comparison to ILC RTML
- Status / Outlook

---
Functions
- Transport
=>	Transport Lines, Turn Around Loops, Arcs
- 6D Phase Space Shaping / Matching
longitudinal	=> Bunch Compressors incl. RF for Energy Chirp, Collimators
transverse	=> Optics, Collimators
- Acceleration
=>	Booster Linac
- Re-Orientation of Polarizationvector
=>	Spin Rotator
- Characterization
=>	Diagnostics (Position, RMS Length, longitudinal and
transverse Profiles, Energy, Energy Spread, Emittance,
Charge, Phase, Polarization,...)
- Correction / Tuning
=>	Dispersion Correction (at ILC: normal and skew quads integrated in BCs, Loop, Arcs),
Coupling Correction,
Phase Correction / Synchronization,
Feedback, Feedforward
- Others
=>	Intermediate Beam Dumps, Spectrometer Beam Lines...
= ILC RTML, but beam dynamics challenges are different!

---
Functional Layout CLIC RTML (Draft)
IP
Main Linac
Main Linac
Turn Around
Loop
Turn Around
Loop
Diagnostics Station
Coupling Correction
BC RF (4 GHz BC1, 12 GHz BC2)
Booster Linac 4 GHz
Spin Rotation
BC1, BC2
Collimation
Vertical Transfer
Spectrometer / Dump
Damping
Ring
Damping
Ring
Injector

---
Functional Layout ILC RTML
IP
Main Linac
Damping
Ring
Turn Around
Loop
Injector
BC RF
Vertical Transfer
BC1, BC2
Coupling Correction
Emittance Measurement
Spin Rotation
Spectrometer / Dump
Collimation

---
Comparison CLIC and ILC RTML
-	In both projects the RTML integrates the same functions
-	But since the beam parameters are different
also the beam dynamics challenges are different
-	Consequently, the beam lines are different
(example: Turn around loops,
at CLIC major issue, since beam energy and energy spread large,
but bunch length and emittance small)

---
Turn Around Loop (old lattice)
matrix{ E_0 # "=" # alignr 9 # "GeV" ## Q_0 # "=" # alignr 0.65 # "nC" ## %sigma_{"s"} # "=" # alignr 175 # "µm" ## I_{"peak"} # "=" # alignr 460 # "A" ## %epsilon_{"n,x"} # "=" # alignr 520 # "nm rad" ## %epsilon_{"n,y"} # "=" # alignr 5 # "nm rad" ## {alignc %sigma_{"E,unc"}} over {alignc E_0} # "=" # alignr 0.32 # "%" ## {alignc 1} over {alignc E_0} {alignc dE} over {alignc ds} # "=" # alignr 0.0 # "m"^{-1} }
CSR
color red matrix{ %sigma_{"s"} # "=" # alignr 175 # "µm" ## I_{"peak"} # "=" # alignr 460 # "A" ## %epsilon_{"n,x"} # "=" # alignr 580 # "nm rad" ## %epsilon_{"n,y"} # "=" # alignr 5 # "nm rad" ## {alignc %sigma_{"E,tot"}} over {alignc E_0} # "=" # alignr 0.32 # "%" }
longitudinal
phase space
ISR
transverse
phase space
initial
final

---
Turn Around Loop (old lattice)
7.5 deg
240 deg
60 deg
Total length = 1096 m

---
Comparison CLIC and ILC RTML
-	In both projects the RTML integrates the same functions
-	But since the beam parameters are different
also the beam dynamics challenges are different
-	Consequently, the beam lines are different
(example: Turn around loops,
at CLIC major issue, since beam energy and energy spread large,
but bunch length and emittance small)
-	Nevertheless, there are some issues where the projects can profit from each other:
e.g., simulation of wake fields in cavities, CSR in chicanes, (other collective effects),
magnetic stray fields along transfer line, ground vibrations,...
(basically any effect we would like to see in the simulations)
-	Lattices of spin rotators could be similar,
but beam parameters at CLIC might be too different
(in any case, ILC spin rotator will be basis for CLIC spin rotator)
-	Correction / Tuning Algorithms, ideas on lattice,... (anything else?)

---
Status / Outlook
-	Initial and final parameters (almost) fixed,
(to ease design of turn around loop we try to lower energy,
but this has an impact on main linac and BC2 RF)
-	Beam line design is advancing,
we have first lattices for BC1 RF and Chicane, Booster Linac,
Transfer Line, BC2 RF and Chicane
-	Turn Around Loop lattice recently improved in terms of
quadrupole and sextupole strengths and better general layout,
but it became longer by several 100 m and emittance growth did not improve
-	Soon, we need to discuss requirements for diagnostics, feedback and feedforward
-	Critical item: not yet started to design Spin Rotator