## Slide 1: Hadron Showers in TOTAl Absorption Calorimeter (progress Report)
Adam Para, Fermilab
May 26, 2009

## Slide 2: Hadron Showers in a Hydrogen Calorimeter
Material properties:
  Radiation length = 63.04 g/cm2 or 7.88 cm
  Hadronic interaction length = 50.8 g/cm2 or 6.35 cm
  dE/dx (@10 GeV) = 32 MeV/cm
Incoming hadron loses energy by ionization up to the interaction point. It creates a fluctuating number of new hadrons.
Pi-zeros develop electromagnetic showers
Other hadrons ionize(if charged), interact producing more hadrons
Until all hadrons loose energy by ionization and come to rest
And then they decay into muons and neutrinos
Neutrinos leave the detector

## Slide 3: Pions, 50 and 100 GeV
At high energies the produced pions dominate the energy deposition, the relative difference between the response becomes very small

## Slide 4: !00 GeV Showers in 250 cm Deep Calorimeter
r = 8 g/cc, DE/E = 1.07%
= 8 g/cc, DE/E = 1.51%,
visible tails of leakage
Excellent energy resolution even with ‘observed scintillation energy’ only

## Slide 5: 100 GeV Showers: Scintillation-Cherenkov Correlation
Observed energy
Reminder: this is hydrogen calorimeter. No nuclear binding energy loss, no neutrons, nothing..
Correlation between the Cherenkov and scintillation still exists. It reflects the fact that the primary origin of the ‘missing energy’ are decays of charged pions and before the decay pions slow down and produce less Cherenkov light

## Slide 6: Dual Readout Correction
Exploiting the C-S correlation one can perform the usual dual readout correction.
As the result the average corrected energy is 99.99 GeV It was 97.54 GeV, uncorrected) and the resolution is 0.47% (RMS) or 0.37% (gaussian fit).
This is for a total absorption calorimeter.

## Slide 7: Sampling Fluctuations ?
Calorimeter is constructed from 1 cc ‘crystals’. Sum up the energy deposition in every n-th plane and multiply by n, call it En.
To remove any contributions from the fluctuations of the deposited energy itself use
DEsampling = Eobs tot – En
This procedure corresponds to the sampling fractions of 0.5, 0.33, 0.25 and 0.2 for n = 2,3,4,5.
Sampling degrades the energy resolution visibly.

## Slide 8: Sampling Frequency
Sampling fraction (i.e. fraction of the energy deposited in the active material is only a part of the story. Sampling frequency (i.e. frequency of the active material in terms of the interaction length is another aspect.
Here: the contribution of the sampling fluctuations at the same sampling fractions but in a calorimeters with the density of 4 and 16 g/cc

## Slide 9: Contribution of Sampling to Energy Resolution, E = 100 GeV
 | 50% | 33% | 25% | 20%
4 g/cc | 0.83 | 1.36 | 1.83 | 2.29
8g/cc | 1.16 | 1.92 | 2.60 | 3.20
16g/cc | 1.63 | 2.74 | 3.72 | 4.61
Sampling ‘frequency’ = 1 cm. It corresponds to:
0.08l at 4 g/cc
0.16l at 8 g/cc
0.32l at 16 g/cc