Analysis of PCB Exposure Tests
        Roman Pöschl
        LAL Orsay
- Motivation
- Experimental Setup
- Data Samples
- Analysis and Results
- Summary, Conclusion and Outlook
Calice Collaboration Meeting Lyon Feb. 2009

---
Introduction
Calorimeter Electronics to be interleaved with layer structure
Do high energetic showers create signals directly in electronics ?
If yes, Rate of faked signals ?

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup I
Test PCB
- equipped with
  PHY3 Chip Set
Prepared Slab
- W dummy
- capton and paper
  for electrical shielding
Usual Slab
Picture courtesy of B.Lutz

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup II
- PCB positioned at place of layer 12 in Ecal ~ shower maximum
  x,y position identical to layer 2
- Schematic view of test PCB - 'Expect' signals from 72 pads, 4x18 = 2 Wafer
Nominal
positions
of
Chips
Scanning
points
Sketch by M.Reinhard/F.Salvatore
- 2.6 106 Events with 90 GeV Electrons (- 5.8 105 with 70 GeV Electrons)
  At least 70 K at each scanning point (Details see later)
  Runs 331462 – 331518
  Today: Full Statistics
- First Step: Runs were subject to the same data processing chain as 'usual' runs

---
Basic Spectra and Alignment
90 GeV run (331495)
- Clear Energy Peak
- Special Board place at
  ~ shower maximum
Projected Chip
Position
Hit Maps
- Layer 2
  Same xy-Position as
  Special Board
- Layer 14
  First instrumented Layer
  after Special board
Chip(s) well within
lateral shower extension
Paper Plot
Paper Plot

---
   So far all runs have been reconstruction using usual reco software
        Now
        Disabling of zero suppression in reco output
- Three Scenarios:
1) No pedestal correction
2) Full pedestal Corrections
3) Pedestal Corrections restricted to signals from Chips
    Remember that there are still 216 entries for the layer in the data files
- General Methodology:
  Subdivision of Runs into BeamTrigger and
  Pedestal Trigger Events (Oscillator Trigger) interleaved with beam events
  Corrections are applied (or not) to pedestal as well as to signal events
  Note: The reconstruction s/w had to be tweaked a bit for that
   Three 'Standard Candles'
   1) Development of MIP Peak in Energy Spectrum
   2) Correlation between Chip Signals
   3) 'Noise History' within run

---
Statistics of Analysis
Scan 3
Scan 4
Run331513: e- 90 GeV
Signal: 216877 Evts.
Pedestal: 9831 Evts.
Run331495: e-90 GeV
Signal: 314275 Evts.
Pedestal: 15264 Evts.
Run331518: e-90 GeV
Signal: 90395 Evts.
Pedestal: 4347 Evts.
Run331511: e-?? GeV
Signal: 86989 Evts.
Pedestal: 3909 Evts.
Run331498: e- 90 GeV
Signal: 66655 Evts.
Pedestal: 4223 Evts.
Run331493: e- 90 GeV
Signal: 85884 Evts.
Pedestal: 4949 Evts.
Run331512: e- 90 GeV
Signal: 218519 Evts.
Pedestal: 9462 Evts.
Run331516: e- 90 GeV
Signal: 228138 Evts.
Pedestal: 10926 Evts.
Run331497: e- 90 GeV
Signal: 214418 Evts.
Pedestal: 13666 Evts.
Run331494: e- 90 GeV
Signal: 217415 Evts.
Pedestal: 11698 Evts.
Scan 1
Scan 2
Run331473: e- 70 GeV
Signal: 209312 Evts.
Pedestal: 38361 Evts.
Run331488: e- 90 GeV
Signal: 213369 Evts.
Pedestal: 13719 Evts.
Run331470: e- 70 GeV
        331471
Signal: 78293 Evts.
Pedestal: 14624 Evts.
Run331479: e- 90 GeV
Signal: 85543 Evts.
Pedestal: 4306 Evts.
Run331480: e- 90 GeV
Signal: 85188 Evts.
Pedestal: 4678 Evts.
Run331492: e- 90 GeV
Signal: 89435Evts.
Pedestal: 4254 Evts.
Run331472: e- 70 GeV
Signal: 189966 Evts.
Pedestal: 37137 Evts.
Run331478: 90 e- GeV
Signal: 65249 Evts.
Pedestal: 3602 Evts.
Run331491: e- 90 GeV
Signal: 217711Evts.
Pedestal: 11053 Evts.
Run331486: e- 90 GeV
Signal: 129778 Evts.
Pedestal: 6146 Evts.
Run331518: e-90 GeV
Signal: 90395 Evts.
Pedestal: 4347 Evts.
Run331516: e- 90 GeV
Signal: 228138 Evts.
Pedestal: 10926 Evts.
Run331513: e- 90 GeV
Signal: 216877 Evts.
Pedestal: 38295 Evts.
Run331511: e-?? GeV
Signal: 86989 Evts.
Pedestal: 3909 Evts.
Run331512: e- 90 GeV
Signal: 218519 Evts.
Pedestal: 9462 Evts.
Scan 4

---
On Run Selection and Observations
- Run Selected according to entries in the logbook
  No comments on bad quality by Shift Crew
- Switch of energy between Run 331473 and Run 331478
  - Change in Pedestal Rate
    20% of all events -> 5% of all events
    Still at least 3500 of (valuable) pedestal events
- at least 70k Events at each point
   - mostly 90 kEvents for off center runs
   - > 200k at (nomincal) Chip Center

---
Pedestal Correction Disabled
MIP Peak vanishes entirely
Large Correlation between
Signals O(35%)
Noise History
- 'Grey' Band “Other signals”
- Colored Lines
  Signals from Chips
  Large Fluctuations
  [-30,30] ADC Counts

---
Pedestal Correction Fully Enabled
MIP Peak restored
Correlation between
Signals slightly reduced
O(25%)
Noise History
- 'Grey' Band “Other signals”
- Colored Lines
  Signals from Chips
  Fluctuations largely tamed
  [-6,6] ADC Counts
  with occasional correlated spikes

---
Pedestal Correction Restricted to four Chips
MIP Peak slightly washed out
- Reason: Pedestal Correction
calculated for Chips applied to
all 216 signals
less important for this study
Correlation between
Signals strongly reduced
O(5%) on average
More details -> see later
Noise History
- 'Grey' Band “Other signals”
- Colored Lines
  Signals from Chips
  Fluctuations tamed
  [-4,4] ADC Counts
  no spikes

---
Average Correlation within Chips
Slightly positive correlation within a Chip O(4%)

---
Average Correlation among different Chips
Chip 1 <-> Chip2
Chip 1 <-> Chip3
Chip 1 <-> Chip4
Chip 2 <-> Chip3
Chip 2 <-> Chip4
Slight negative correlation
between Chips
O(4%)
Chip 3 <-> Chip4

---
Scenario for extraction of results I
- No zero suppression
- Pedestal Correction applied to Chips only
  Major Change w.r.t. to results shown at Daegu
  Not a sensation but now well investgated
- Only 'electron' events/entries
  Low energetic entries may bias the results

---
Scenario for extraction of results II
Discarding of Signals
- Closer Look reveals strong correlation between first signals of each chip
  These signals arrive together in the multiplex series of the data acquistion
  (Remember all 216 cells of a board are transmitted in 12x18
  chunks to the CRC boards)
  Reason is unknown but it rings a bell ...
=> First signal of each chip discarded in analysis

---
Noise Spectra Scan 4
Signal Events
Pedestal Events
Scan ID
C
h
I
p
ID
Paper Plot

---
Discussion of Noise Spectra
Did show only a selection of spectra
- Full set of scan plots in Annex to talk
- First Order: No difference between signal and pedestal events
  visible
- No obvious dependency on scan position
- No Hits above MIP threshold
  Assume 45 ADC counts for a MIP
  Quantitative results -> Next Slides

---
Average Mean and RMS for Scan 1
Difference
normalized
to MIP
<< 1% of MIP
Difference
normalized
to MIP
<<0.5% of MIP
No dependency on scan position visible
Paper Plot

---
Average Mean and RMS for Scan 2
Difference
normalized
to MIP
<< 1% of MIP
Difference
normalized
to MIP
<<0.5% of MIP
No dependency on scan position visible
Paper Plot

---
Average Mean and RMS for Scan 3
Difference
normalized
to MIP
<< 1% of MIP
Difference
normalized
to MIP
<<0.5% of MIP
No dependency on scan position visible
Paper Plot

---
Average Mean and RMS for Scan 4
Difference
normalized
to MIP
<< 1% of MIP
Difference
normalized
to MIP
<<0.5% of MIP
No dependency on scan position visible
Paper Plot

---
Probability of fake hits - Estimation
Binomial Distribution
P=Nsig/Ntot , Ntot = Nevents x 17 (17 independent signals/Chip)
        Nsig = #Signals > |n| ADC Counts
σP = [P(1-P)/Ntot]1/2
N=45, 38: Nsig = 0 for all runs and all chips !!!!
  First signals seen for n=30 <=> 2/3 MIP

---
Probability for #Hits > |2/3| MIP
        Probability < 10-5
No evidence for beam induced signals
Same level of 'outliers' in Signal and Pedestal Events
Chip 1 looks like being a bit noisier than the others
Largest 'Hit Probability' when beam was targeted on other Chips
Given number is upper limit
Paper Plot

---
Influence of other Chips
Probability of finding a Signal > 2/3 MIP if
a) There was a signal > 15 ADC Counts in another Chip (“Hits”)
b) There was no signal > 15 ADC Counts in another Chip (“No Hits”)
Tendency that Signal in
one Chip induce Signals
in the other Chips
- Consistent with residual
Correlation (see above)
- Allows for conclusion
that 'real' probability is
yet smaller than given
here!

---
Summary, Conclusion and Outlook
- Analysis of PCB exposure test with full statistics
  Study is finished
- Pedestal Correction necessary for analysis
- No signals above 1 MIP observed
- Probability to find signals with > |2/3| MIPS < 10-5
  'Real' probability looks like being much smaller
- No evidence that shower particles create fake hits in detector or
  even influence noise distribution at smaller level
- All observed 'effects' seem to be independent of scan position
- Presented results summarised in note for CALICE
  (waiting for approval by referees)
- Can be “immediately” sent to NIM

---
Annex: Noise Spectra in other scans

---
Scan 1

---
Scan 2

---
Scan 3