## Slide 1: Installation status of the HLS system
Aug. 12, 2009
G. Gassner, M. Masuzawa, R. Ruland, M. Satoh and
R. Sugahara

## Slide 2
SLAC agreed to give us 5 sensors
Mid July Preparation
(pipes, pipe supports, etc.)
Aug. 3~Aug.7 HLS sensor installation with Georg.
No major problem, a small modification needed.
Aug.6~Aug.10 Test run
Aug.10~Aug.11 Modification of the vessel,
re-wiring of the cables
Aug.11 ~ Long run
(with a few day interruption due to the "lab-wide planned power outage” next week.

## Slide 3: Small modification
Cut the second (extra) outlet and sealed it yesterday.

## Slide 4: Small problem
One vessel ( out of 5 ) has some
brown deposition. Corrosion??
No problem with 4 vessels.

## Slide 5: Data acquisition
HLS PC in the “FF power supply room” outside of the ATF2 beam line

## Slide 6
QD2AFF
QD4AFF
QF7FF
QM11FF
QF16FF
5 HLS capacitive sensors
(made by BINP) from SLAC
Each sensor 6~9 m apart
Covering ~ 35 m span

## Slide 7
with respect to QD16FF
QD16FF
Aug.6 (Thurs) Aug.7 (Fri) Aug.8 (Sat) Aug.9 (Sun)
?
24 hours
Tidal motion + pitch
QD2AFF
QD4AFF
QF7FF
QM11FF
QF16FF

## Slide 8
Aug. 9 (Sun) 20:25
3 on the Japanese seven‐stage seismic scale at Tsukuba
Data acquisition
at every 2 seconds

## Slide 9: Summary
HLS installation went well.
Many thanks to Georg Gassner and the SLAC alignment group.
Small problems
  A modification needed to three vessels, from two outlets to one.
    Cut the second outlet and sealed it.
  One vessel got corroded ? ( Chemical analysis is underway) .
    We cleaned the surface and painted with epoxy.
Data are collected using a PC in the “FF power supply room”
outside of the beam line.

## Slide 10: Future plan
  Collect more data
    Will report them periodically.
  Integrate the HLS system with the ATF2 EPICS database so that we can use the mover position data.
  More sensors?