## Slide 1: Simulation of Crystal Calorimeters
Adam Para, Nayeli Azucena Rodríguez Briones
July 7, 2009

## Slide 2: Crystal Calorimeter Version of SiD
Use SiD02 detector geometry
Replace the EM and HAD calorimeters by the crystals
Two version of the crystal calorimeters (to examine the importance of the calorimeter segmentation)
Fine
EM section: 6 layers of crystals, 3 cm thick, 3 cm x 3 cm transverse segmentation
HAD section: 22 layers of crystals, 5 cm thick, 5 cm x 5 cm transverse segmentation
Coarse
EM section: 3 layers of crystals, 6 cm thick, 6 cm x 3 cm transverse segmentation
HAD section: 11 layers of crystals, 10 cm thick, 10 cm x 10 cm transverse segmentation

## Slide 3: Mechanics of the Geometrical Description
Start with the parameterized detector description in fine.xml file
Create fine.lcdd and fine.heprep files
Automated edit of the fine.lcdd file to create a detector template.lcdd file:
  Replace calorimeter by optical calorimeter (for all detecotrs)
  Insert optical properties parameterized by refind
  Change the calorimeter material to crystal
  Add material crystal, parameterized by Element and Density
  Parametize the B field value by BValue
  Values of refind , Element, Density and BValue defined by the job submission

## Slide 4: Created Data Sets
Fine version of the detector, for now. Coarse will come
Electrons, p- and muons at 1,2,5,10,20,50 and 100 GeV, emitted at 90 degrees
‘jets_(1.0-7.0)’, where:
  jets_1.0 -> W_Theta90_0_100GeV
  jets_2.0 -> W_Theta90_100_200GeV
  jets_3.0 -> Z0_Theta90_0_100GeV
  jets_4.0 -> Z0_Theta90_10-250GeV
  jets_5.0 -> Z0_Theta90_50GeV
  jets_6.0 -> Z0_Theta90_100GeV
  jets_7.0 -> Z0_Theta90_200GeV

## Slide 5: Fine Print
Data location: /ilc/sid/chercal/para/results/. Files like: fine_QGSP_BERT_BGO_d7.13_n2.15_pi-_50.0_0_B5.0.slcio
Data also accesble via WEB interface at http://docdb.fnal.gov/ILC/sid/chercal/para/results/
Very fine print: jets data files not accessible via WEB (too large data files)
Data files analyze-able with JAS3 after aliasing to ccal01, version from Steve Magill
Beware: single W/Z files created with Pythia with variable boson mass. W/Z momentum varies from event-to-event (jets 1-4) and the W/Z mass varies too. In fact the mass spectrum has a remarkable tail toward low masses.