     CALICE Software
      Niels Meyer
   DESY Hamburg
     Roman Pöschl
        LAL Orsay
- Calice Testbeam Data Taking
- Data Management
- Event Building and Reconstruction Software
- Summary and Outlook
       LCTW09 Orsay/France November 2009

---
CALICE Testbeam Data Taking
CALICE collaboration is preparing/performing large scale testbeam
Data taking in Summer 2006/2007
Testbeam program poses
software/computing “
challenges”
- Data processing from
  Raw Data to final
  Clusters in a
  coherent way
- Handling of Conditions Data
  Detector Configuration
  Calibration, Alignment etc.
-Comparison with simulated
 data
 'Physics' Output
Testbeam Setup at CERN 2007
TCMT
TCMT
Analogue
HCAL
ECAL
O(15000) calorimeter cells
readout by Calice DAQ
No Zero Suppression

---
CALICE “TIER 0” – Infrastructure in the Control Room
Gigabit Uplink
- High Speed Connection to the outside
  world
- Serves all Calice Control Room Computers
caliceserv.cern.ch
  - Online Monitoring
  - Grid Transfers
Disk Array
DAQ Computer
Well organized setup of computing
Thanks to B. Lutz
Picture courtesy of C. Rosemann DESY

---
Data Handling and Processing
Experimental Site e.g. CERN, FNAL
Local Storage for online monitoring and fast checks
Data Transfer using Grid Infrastructure
Speed up to 240 MBit/s
Mass Storage
   Data
Replication
~40 TByte of Calice Date 2/3 binaries 1/3 converted files
     Grid UI
for direct access
MC Production
       Grid CE
for massive processing
DESY
dcache
(backbone)
in2p3
Lyon
fallback site

---
The Virtual Organisation - vo calice
Hosted by DESY:
Page for registration is https://grid-voms.desy.de:8443/voms/calice
~60 Members
   and
counting ...
VO Manager: Niels Meyer/DESY, Deputy: A. Gellrich/DESY
8

---
Institutes which provide Grid support for Calice
Supported by: DESY Hamburg Hosting, Computing and Storage
        LAL Computing and Storage
        LLR Computing and Storage
        DESY Zeuthen Computing and Storage
        Imperial College Computing and Storage
        Birmingham Computing and Storage
        cc in2p3 Lyon Computing and Storage
        Cambridge Computing and Storage
        Institute of Physics Computing and Storage
        Prague
        University College Computing and Storage
        KEK Computing and Storage
        Manchester Computing and Storage
        CIEMAT Madrid Computing and Storage
        Fermilab Computing and Storage
        NIKHEF Computing and Storage
        University of Bonn Computing and Storage
        Univ. Liverpool Computing and Storage
        Univ. Oxford Computing and Storage
- Most of the sites have been involved in recent data and MC processing
  Connectivity to Asian Sites still and Issue
- Full set of Rawdata avalaible at DESY HH and CC in2p3 Lyon!!!
  Grid exploitation of Calice paved the way for successful
  mass production for ILC detector LOIs

---
Conversion to LCIO
       DAQ data types are converted/wrapped into LCIO on the basis of LCGenericObjects
DAQ Data Files/Types
Configuration Data
        +
Slow Control Data
Event Data
Trigger Data
 Event Building
in lcioconverter
Conditions Data ...
Run stable over all ~100 Mio. Events
       LC Event
Preliminary checks of data integrity
Conversion of 2 Gbyte 'native' file with
80-100 Hz on a standard Grid WN
Calice db
at DESY
  MySQL
Further Processing
within MARLIN
Framework
... are handled with LCCD
Installation of Software using tools developped in EUDET NA2 task
ilcinstall, cmake

---
Intermezzo – Conditions Data Handling
LCCD – Linear Collider Conditions Data Framework:
  - Software package providing an Interface to conditions data
    - database
    - LCIO files
    - Author Frank Gaede, DESY
LCCD works and is heavily used within calice !!!
Still too much an expert tool (No real development since 2005)
The importance of conditions data (not only) for 'real' data
renders the development of a fully functional cd data toolkit
to be a fundamental !!! piece of the ILC Software
- Efficient storage and access to conditions data
  Browsing, convenient interfaces
- How to 'distribute' conditions data (e.g w.r.t to grid) ?
  BTW.: LHC does have some headache with that!

---
Calice Software
        Three main packages
    Contributions by groups from
 DESY, Imperial, LAL, LLR, NIU, RHUL
calice_lcioconverter
calice_userlib
calice_reco
Current version
     v04-06-05
  (v04-07 in prep.)
RawData into
CalorimeterHits
(standard LCIO)
TrackerHits
First stages of
higher level analysis
MARLIN processors
Current version
      v04-10
Interface classes to
LCGenericObjects
(these classes should
be defined by LCIO)
utililty functions e.g.
For TriggerHandling
Current version
v04-02-06
converts
calice DAQ format
into LCIO (LCGenericObjects
needs DAQ software
expert work
MARLIN processors
        ~250 classes or functions
        Data of four different Calorimeter Prototypes are
        available in LCIO format

---
LCIO
No data model for conditions- and meta-data, have to be implemented as LCGenericObjects
This is fine, because most of these structures are easily generalized (e.g. slow control data, detector configuration, beam-line status)
Current problem: object is bare LCGenericObject after storage/re-read
  - danger of confusing different objects with identical size
  - dynamic_cast for read-back collections does not work
    => need to work with constructors to be transparent
    => unnecessary increase of memory footprint

---
LCCD
In principle, the LCIO/Marlin concept is thread-save - if it was not for the change listener pattern for conditions handling. Is there a better way, e.g. by 'collection has changed'-flags?
The only available database implementation for LCCD is based on (non-maintained) CondDBMySQL. How to provide 'code reliability' here? Who takes care of fixes, e.g. removing I/O overhead to DB server?
Scalability: Conditions for full scale detector will be huge (current HCal calib: ~50 floats per channel). Need clever memory  CPU  I/O balancing in the future, preferably steerable.

---
Alignment
For PFlow calorimeters, cells are smaller than Moliere radius => mis-alignment in data affects the energy distribution over cells
At least for TB: need to have this mis-alignment also in MC in order to do cell-to-cell comparisons (crucial to proof detector understanding at least for Tile HCal)
Thus: alignment is conditions data and should be handled using LCCD interfaces
Closely linked to geometry description (e.g. cell neighbours, cell positions, ...)

---
Geometry
GEAR is NOT a generic geometry interface, it is the geometry parameterization used for ILD
currently simulation-driven: geometry defined in MOKKA, fed to reconstruction by XML file - this is not a useful ansatz for test beam setups (which are very flexible) and most probably also not for a full-scale detector with floating alignment
Would want to have some LCIO-embedded data model that is good for calibration, simulation, and analysis alike. Something more object oriented (hit has pointer to cell rather than complex 'find cell by index from somewhere') would be much easier to use in the end, but this is re-discussing basic LCIO paradigms...

---
Next Generation Protoypes – EUDET Modules
-
- From the beginning coherent interface between DAQ
  and offline processing (D. Decotigny et al.)
  LCIO will remain backbone!!!
  Consistent Handling of Low Level Data
  Coordinated handling of potentially frequent
  changes in startup phases
- Will continue to apply and help to develop
  ILC Software tools
  - Need for geometry package
    Consistent between Data and Simulation

---
Summary and Outlook
- Calice uses ILC Software for processing of Testbeam Data
   ILC Datataking in a (big) nutshell
    Allows users to switch easier between testbeam data analysis and
    physics/simulation studies
- Calice uses systematically Grid tools
   24h/24h 7h/7h during CERN, FNAL testbeams 2006-2009
- Experience with testbeam data clearly reveals the needs for
  a coherent concept to handle 'low level' data within ILC Software
- Effort will continue with EUDET Modules on an even broader basis
  Using of ILC s/w tools already in testbeams is (in the mean time)
  well established and accepted concept
CALICE did/does not only hardware-prototyping but also 'computing prototyping'
Computing benefits from collaborative effort and application of
ILC software toosl