## Slide 1: A Study of SB2009 by CAIN
Akiya Miyamoto
14-Oct-2009
KEK
ILD-Optimization meeting

## Slide 2: Introduction
Study of ILD performance with new ILC beam parameter is urgent. Comments on SB2009 should be by early December(?)
No solid official parameters yet
  250 GeV parameter
  Energy spread at 500/250 GeV, …
While waiting, I have created a few plots by CAIN.
  SB2009, 500 GeV parameter
  CAIN version 240, include simulation with traveling focus
I expect that
  SLAC colleagues will create standard samples by GunieaPig as soon as parameters are fixed.

## Slide 3: Beam Parameters
 |  | RDR LowP | RDR Nominal | SB2009 | 
Beam and RF Parameters |  |  |  |  | 
No. of bunches |  | 1330 | 2625 | 1312 | 
Bunch spacing | ns |  | 370 | 740 | 
IP Parameters |  |  |  |  | 
Norm. horizontal emittance | mm.mr | 10 | 10 | 10 | 
Norm. vertical emittance | mm.mr | 0.035 | 0.040 | 0.035 | 
bunch length | mm | 0.2 | 0.3 | 0.3 | 
horizontal b* | mm | 10 | 20 | 11 | 
horizontal beam size | nm | 452 | 640 | 470 | 
 |  |  |  | no trav. focus | with trav. focus
vertical b* | mm | 0.2 | 0.40 | 0.48 | 0.2
vertical beam size | nm | 3.8* | 5.7 | 5.8 | 3.8
Luminosity | cm-2s-1 | 2×1034 | 2×1034 | 1.5×1034 | 2×1034
Parameters used for CAIN. SB2009 parameters are taken from ALCPG09 talk by N.Walker.
*) typo in the original slide was modified(2009/11/11)

## Slide 4: Differential Luminosity
SB2009 is about in the middle of RDR nominal and RDR lowP

## Slide 5: Differential Luminosity: Values
 | Total Lum | Lum. in E0~E0-2.5GeV |  | Lum in E0~E0-25.0GeV | 
 |  | Lum | Lum/Total(%) | Lum. | Lum/Total(%)
RDR LowP | 2.01 | 0.89 | 44 | 1.68 | 84
RDR nominalA | 2.00 | 1.20 | 60 | 1.90 | 95
SB2009 w/o TF | 1.55 | 0.74 | 48 | 1.37 | 88
SB2009 w.TF | 2.01 | 0.96 | 48 | 1.77 | 88
Peak luminosity ( with in 2.5GeV) of SB2009 w. TF (0.96x1034) is about
20% less than that of RDR nominal (1.2x1034)
Lum. with Traveling Focus/ Lum. without Traveling Focus ~ 1.3
E0=500GeV, Lum. in unit of 1034cm-2s-1

## Slide 6: Pair : Energy spectrum
Pair energy is 2~3 times larger than RDR nominal, but lower than RDR lowP ( Number of bunch of SB2009 is a half of the RDR nominal )

## Slide 7: Beamstrahlung Photon : Energy Spect.

## Slide 8: CAIN samples
Information about CAIN background data are available at
http://ilcphys.kek.jp/soft/ILCBeam/index.html

## Slide 9: Summary
Luminosity and background distribution were studied by CAIN.
(Total) luminosity of SB2009 w. TF is same as the RDR nominal, but luminosity within 2.5GeV from the nominal energy is about 20% less than the RDR nominal.
Pair backgrounds per bunch of SB2009 w.TF is 2~3 larger than RDR nominal. Backgrounds per pulse would be 1~1.5 lager than RDR nominal.

## Slide 10: Next step
Coordinate efforts in ILD to study new ILC parameter is necessary
Background study by Mokka/Marlin, etc.
  Samples for background study at 500 GeV are available.
    CAIN
    GunieaPig samples produced by SLAC colleague
  Some study would be possible
Study impact on physics
  Concrete parameters are not available.
    500 GeV physics:
      Need information about the energy spread ?
    Parameter for 250 GeV
  If StdHep samples have to be re-created, we need to start to negotiate with SLAC colleagues soon.