## Slide 1: Signal port flange and beam pipe
Norihito Ohuchi

## Slide 2: Signal cable assignment on A and B flanges
Original design of signal cables for A and B flanges
  A flange
    2 ×Piezo
    4 ×WPMs
  B flange
    2×e‐pickup coupler
    2 ×cavity HOM
    1 ×cavity pickup
    2 ×PT1000 coupler
    1 ×STC He vessel
  D flange
    Stepping motor, BPM, Piezo vibration sensors
Signal cables from cavities for S1-G Module-C
  A flange
    2 ×Piezo
  B flange
    2 × e‐pickup coupler
    2 ×cavity HOM
    1 ×cavity pickup
  D flange
    Stepping motor
Signals for WPMs and temperature sensors go through the KEK terminal ports.

## Slide 3
A-flange
2 ×Piezo
No use
No use
No use
No use

## Slide 4
B-flange
cavity Pickup
cavity HOM1
cavity HOM2
spare
e‐pickup coupler
e‐pickup coupler
No use

## Slide 5
Stepping motors
D-flange
No use

## Slide 6: D-flange location
Upper side
WPMs and D-flange
Temperature sensors, strain gauges, pin diodes

## Slide 7: Feedthroughs (From data of #M9)

## Slide 8: Confirmation for feedthroughs
Assignment of the cables to the A and B flanges is basically same as the #M9.
  #M9 is the module which DESY sent to FNAL as CM1.
  However, the cables for WPMs and temperature sensors go out via the KEK terminal ports.
D-flange locates at the downstream of Module-C.
  The cable lengths are same as the #M9 including the stepping motors.
The machine process of the A, B and D flanges
  The blind A and B flanges will be sent to KEK with Module-C components from INFN/Zanon.
  Proposal: the flanges would be machine-processed by FNAL or DESY, and be checked with feedthroughs for leak tightness.

## Slide 9: Beam pipe between gate valve and FNAL cavity
FNAL cavity
: fixed flange
KEK gate valve
: rotatable flange
KEK cavity group will prepare this components.
For checking leak tightness, the group needs the hexagon seals and the blind flange.