## Slide 1: Sorting out Hadronic Simulations?
Adam Para, Igor Rakhno,
Fermilab, December 22, 2009

## Slide 2: MC Simulation Credibility Problem
Different physics lists in GEANT lead to very different predictions of the energy lost due to nuclear effects
At low energies, in the ‘transition regions’, multiple models are sampled at random and the fluctuations of observed energy distribution is dominated by the difference between the models
Need external input do decide which of the models (if any) is applicable

## Slide 3: MCNPX
Total absorption calorimeter is particularly simple case: the total energy deposition depends primarily on the modeling of the nuclear processes and it depends very weakly on the high energy hadron interaction model
MCNPX is a general-purpose Monte Carlo radiation transport code for modeling the interaction of radiation with everything. MCNPX stands for Monte Carlo N-Particle eXtended. It utilizes the latest nuclear cross section libraries and uses physics models for particle types and energies where tabular data are not available. Applications range from outer space (the discovery of water on Mars) to deep underground (where radiation is used to search for oil.) MCNPX is used for nuclear medicine, nuclear safeguards, accelerator applications, homeland security, nuclear criticality, and much more.

## Slide 4: Total Absorption Calorimeter in MCNPX
Igor Rakhno: setup and the initial run
3 x 3 x 3 m3 block of BGO
MCNPX does not include Cherenkov radiation. Poor man’s Cherenkov simulation: tally the energy deposited by particles as a function of the velocity of the particle: b in bins: <0.4, 0.4 – 0.5, 0.5 – 0.6, 0.6 – 0.7, >0.7
Initial run of 600 negative pions at 10 GeV

## Slide 5: Which Particles Actually Deposit Energy?
Electrons 5.16 GeV
Protons 1.56 GeV
Charged pions 1.46 GeV
Neutrons 0.23 GeV
??? Neutrons?? Need to understand better the accounting

## Slide 6: Energy Deposition by Nuclear Fragments
Deuterons 0.137 GeV
Tritons 0.103 GeV
Helium-4 0.179 GeV
Heavy Ions 0.106 GeV
Scintillation light due to these contributions is likely to be suppressed (Birks!)

## Slide 7: Electrons Contribution: Breakdown by Velocity
More than half of the energy deposition by electrons due to rather slow, non-relativistic electrons (delta rays)

## Slide 8: Protons Contribution: Breakdown by Velocity
Most of the energy deposited by protons due to non-relativistic protons.

## Slide 9: Charged Pions Contribution: Breakdown by Velocity
Most of he energy deposited by pions which are relativistic, b>0.7 !

## Slide 10: Total Energy Deposition
Average loss of energy due to binding energy losses ~ 10%
Very good energy resolution, 6.5% at 10 GeV, even with ‘scintillation only’
occasional gain of energy due to fission

## Slide 11: Dual Readout?
Approximate simulation of Cherenkov:
Chrenkov signal proportional to the energy deposited by particles with b>0.6
Clear correlation of the total energy deposition and the amount of Cherenkov light
further improvement of the resolution expected

## Slide 12: Conclusions
MCNPX a good alternative to GEANT simulation. May provide a valuable input regardig the choice of the GEANT models
It is a very preliminary stage, but it looks like QGSP_Bert is the best of the GEANT physics lists
A very good resolution of a total absorption calorimeter, ~ 20%/sqrt(E), even with the single readout
Even better resolution with the double readout
Need more studies