Recent & future developments
in the DAQ2 integration
Vincent Boudry
Rémi Cornat
David Decotigny
Franck Gastaldi
Antoine Matthieu
CALICE Week
U. of Texas at Arlington
11/03/2010

---
TOC
- Foreword/Key dates
- Availability of HW
  - DHCAL DIF production (talk of Julie)
- Status of FW
  - Connectivity tests
    - DCC ←→ DHCAL DIF
    - CCC ←→ DHCAL DIF
  - FW advance
- Status of SW
  - Data formats
- Next activities
- Calice vs the rest of the world (aka combined TB)

---
Forewords
- Key dates
  - AHCAL
    - Now (LabView + USB)
    - TB end of 2010 / 2011
  - SDHCAL
    - TB 3×m² Mai—Fall 2010
      - USB + CCC (+ DCC) → DAQ-II
    - Cosmics tests : Summer—Fall check of 40 planes
      - probably on USB (rates ~ 100 Hz)
    - M3 → Spring 2011
  - ECAL
    - Cosmic in Summer
      - FEV COB ; 1 chip; 1 Wafer
      - Lecture DIF USB then USB+DCC+DIF
    - Some short Slabs in Spring 2011
    - Full set-up end 2011 ?
- Imprecise view → needs sharping up
  - Un-even view
  - Reschuffling due to stepping down of UK
  - New actors ? AIDA ?

---
EUDET DAQ2 (for the DHCAL)
Clk ~ 100 MHz
(N×MClk)
DIFs
(×120)
ASUs
DAQ PC
DCC
Clock
& Control
LDA-DIF on HDMI (Config, Control, Data, Clock, Trig, Busy, Sync)
Clock, Trig, Busy & Sync on HDMI (compatible LDA-DIF)
LDA
ODR
LDA
DCC
×10
⋮×9
Optical (alt. Cable) GigE
Debug USB
×40
:
×14
:
External Trigger
Machine
clock
(5 MHz)
External
Trigger,
Spill

---
Gig Eth validated
⚠ Big effort done ⚠

---
HW status (DIFs)
- DIF ECAL OK
  - A few (~15 [⊃ 6 in LLR]) for tests
  - Material for 40 more available in total
- DIF AHCAL
- DIF DHCAL
  - 20 protos available
    - 1-2 defects
    - Tests of μMegas & Dirac
    - 1 DAQ test (LLR)
    - 5 (soon 9) for 3 RPCs m²
  - “Emergency” prod of 20
  - Additionnal prod of 150 cards (prod by LAPP funded ANR DHCAL +LLR)
    - See Julie's talk

---
Tests with DHCAL DIF
Two weeks ago, Guillaume went to LLR, to make the first tests with the LAPP DIF and the DCC
We passed the tests successfully :
Send Fast commands from DCC.
Send Block Transfer command from DCC.
Received an “acknowledge” from the DIF on DCC after sending	the commands above.
Remarks :
All commands were sent through the USB connection on the DCC
The received data (acknowledge) were checked by Chipscope (Xilinx logic analyzer).

---
DCC — DHCAL DIF comm test
Result seen on Chipscope
DATA
Sent by the DIF
CRC
Sent by the DIF
IDLE
SOF
EOP
IDLE
CRC
Sent by the DCC
Start Frame (h#B0B0)
PC_usb
PC
chipscope
Readout
J-tag connect
Fast & BT command
Readout
Fast & BT command
DCC
(LDA like)
DCC
DIF LAPP
Can be ECAL DIF
USB Access
LDA

---
Summary
Firmware :
  - USB : Some bugs for the readout are under investigation and will be solved in a few days.
  - HDMI link : the link is locked when the DCC is connected with the DIF or the LDA. About LDA, only the connection have been tested.
  - Next step of tests with LDA : command & readout.
  - Some improvements are needed on main firmware to work with a full DCC
DCC card :
  - Improvements on routing are made before the launch of the production

---
HW Status (DCC)
- 2 protos + 1 proto0 available
- Prod of 20 cards (funded ANR DHCAL +LLR)
  - Proto ~ OK.
  - → End of March
    - Components schuffling (improvement of routing)
    - Bigger (and cheaper) FPGA
    - Launch of prod → April-May
  - until June
    - Improvement of firmware and tests with DIF and LDA
  - June-July
    - Complete stress tests
  - avail in Sept 2010 for TB

---
FW status
- SVN repositories @ CAM, Lyon, CCIN2P3, Cambridge, CERN → listed on Calice DAQ pages (to be updated)
- DIF task force (RC (LLR), JP (LAPP), BH (CAM), MR (DESY)
  - Definition of DIF φ connection LDA ←→ DIF ←→ ASU/HBU
    - Reference document
    - Some specification forgotten (value of VCC on one pair)
  - Definition of DIF link protocol done
    - Needs reference document
  - Cooperation on blocs in FW
    - See Rémi's Talk
    - DIF task force Meeting
      end of March
ASIC interface:
ECAL → link to Spiroc/Skiroc
AHCAL: Exists
DHCAL: JP, GV working with USB
Comm. bus (RC)
Now “Hardwired comm.” → end of March
Bus for re—usability & usable devt
USB “standard” (FTDI chip)
HDMI interface (bloc from M. Kelly :left in nov.)
Adapt ECAL ✔ (RC, FG) → AHCAL
Adapt DHCAL (Xilinks) on going (JP, GV)

---
FW status (DCC)
- same blocs as LDA & DIF
  - Good way to learn & integrate code of MK
  - Now @ 50 MHz
- Connection 1 ch. USB→DCC→DCC→DIF (Physical test)
  - OK data readout
  - OK fast commands
  - OK config commands
- Connection many channels
  - Simulated: 4 channels ✔
    - Space limitation removed → OK for 9 channels
- USB will be used for first test
  - DHCAL TB in Mai ? (Aggressive)

---
FW Status (LDA)
- Code taken over by BH & MW
  - First test OK (see Rémi's talk)
- Complete review / hand over on the 17th of Match → UCL
  - Link LDA_DIF
  - DIF = DIF module + pattern gen.
  - ODR ou GEth ?
  - LDA code
    - Checking of IP licences
    - Discussion on maintenance / needed completion
      - Good experience from FG on this code
      - Devt @ LLR on G-Eth

---
FW status (CCC)
- Working CCC code
  - MW follows the code & ready to adapt
    - trigger logic
    - Busy logic etc.
- Shipping of 3 cards
  - 1 LLR for test bench
  - 1 LAPP, 1 IPNL for sync of many DIF
- direct connections CCC-DIF
  - clock & trigger distribution
  - Sync commands (Sync, Reset)
    - FW by LAPP ←→ MW
    - for TB in May...
- Could be also used for AHCAL TB as asap.
  - needs DIF FW adapt (clock, trigger)

---
Next actions
- "Validation of complete chain" with support for intermediate steps
- Feb.
  - Inclusion CCC-Dhcal DIF (on going)
    - synch.
- March
  - Code DIF ⊃ 8b10b ✔
  - Launch of DHCAL DIF prod ✔
  - DIF Common framework (on going)
- End of spring
  - Validate first setup with DCC+CCC  controlling a m² over USB → TB ?
- May
  - System test
- June
  - Geth+LDA+DCC+DIF (Done)
  - Stress tests

---
Next activities (2)
- Fall
  - DIF FW complete
  - integrate the LDA In parallel
    - R/O by Ethernet
- End of 2010:
  - Integrated the ODR
- Jan 2011
  - Ready for 1 m³
    - 2 LDA
    - 14 DCC
    - 120 DHCAL DIFs
- Pending
  - Stress tests
  - 50 MHz
    - 80-100 MHz for 2011

---
Software status (General)
- Devt in DOOCS on hold
  (since departure of TW, VB)
  - DD has collected the code & experience
  - Mainly ODR driver & config Database
- “Small works”
  - Simulation of DAQ data flow SDHCAL, ECAL
    - System C
  - Evaluation of reassembly & stability
  - Evaluate LCIO storage on real PC (simulated DAQ2 hardware)
- Fall 2010: Topology-aware slow-control config database + tools to generate the SC blocks
- Fall 2010: Abstract SW layer to indifferently drive LDA/Ethernet or DCC/USB
    - Xdaq + DOOCS + Tango
- Data format
  - Identifier & Headers formalized
  - incl for LCIO
Possible integration of all detectors there
*ROC, DIRAC, DCAL's

---
RAW data proposal (suitable for ROCs)
 * Event:
 * - DetectorName <- runHdr::DetectorName
 * - RunNumber <- runHdr::RunNumber
 * - EventNumber <- ROEventId::toUnsigned()
 * - TimeStamp: default
 * - Weight: default
 * - LCCollection "rawdata_DIF:str(DIF_id)":
 *	+ param "id_ODR" (unsigned): from raw event
 *	+ param "id_LDA" (u32b)
 *	+ param "id_LDA_diflink" (unsigned)
 *	+ param "id_DIF" (unsigned)
 *	+ param "TrainNumber" (unsigned)	// since DAQ start
 *	+ param "BC_DIF" (unsigned)	// since RUN start
 *	+ param ”DeltaCounter” (unsigned)	// 40 MHz counter
 *	+ param optional extra DIF info (type, temp, adc) ???
 *	+ elt[0]: LCGenericObject
 * + int[0]: id_roc_chain
 * + int[1]: id_roc
 * + int[2]: index_in_dif_dump (starts at 0)
 * + int[3]: chipType
 * + int[4]: acqMode
 * + For HR2 chips:
 * + int[5]: nframes (< 128)
 * + int[6 + i*5]: bcid for frame i (i in [0, nframes])
 * + int[7 and 8 + i*5]: t0 vector (msb 7=t0_63, lsb 8=t0_0)
 * + int[9 and 10 + i*5]: t1 vector (msb 9=t0_63, lsb 10=t0_0)
 * + int[11 + i *5...]: additional data ??
 * + elt[1]: other LCGenericObject (ROC event)
 * ...
 * - other LCCollection "rawdata_DIF:str(DIF_id)":
 * ....
V. Boudry, R. Cornat,
D. Decotigny
LCIO format (source):
https://svn.in2p3.fr/calice/
online-sw/trunk/daq/
reassembler/
lcio_dump.hpp?view=markup
Physical address
(⊃ redundancy)
Event Counter/Tagging
Event Timing
Compacity
vs
Redundancy (debugging)
namespace IO
{
  class LCWriter;
};
/**
 *
 * Run Header:
 * - RunNumber: user-specified
 * - DetectorName: user-specified
 * - Description: user-specified
 * - ActiveSubdetectors: [ "DIF_rawdata" ]
 *
RAW Data ”in the tubes” format:
https://svn.in2p3.fr/calice/online-sw/trunk/daq/
calice_packets/calice_raw_formats.h?view=markup

---
LCIO format for reconstructed DHCAL
Calorimeter hits (proposal v0.01)
EVENT::RawCalorimeterHit
{
    int	_cellID0; // Chan (64 ==> 6b)
        // + Asic (max 420 ==> 9-10b)
        // + Dif_Id (48-144 ==> 7-8b)
        // + Module_Id (40 Barrel + 24 Endcap ==> 6b)
        // == 28-30b (remain 2-4b) [6+6+7 == 19b in TB]
     int	_cellID1; // Time2Previous (in BC) ==> 24b (remain 8b) (CHBIT_ID1 must be set)
    int	_amplitude; // 3 Thr ==> 2b (remains 30)
    int	_timeStamp; // Rec Time on 32b wrt (Spill start | Ext. Trigger)
}
EVENT::CalorimeterHit
// Recontructed Hits
{
    int	_cellID0; // Idem RAW
    int	_cellID1; // Idem RAW (CHBIT_ID1 must be set)
    float	_energy; // Rec Energy
    float	_time; // time from ref (in ns).(LCIO::RCHBIT_TIME must be set)
    (float	_position [3]); // Position (unit not fixed) (LCIO.CHBIT_LONG must be set)
    int	_type; // Deposit type (mip, EM, noise, ...)
    EVENT::LCObject *	_rawHit; // Link to RAW hit
}
One also needs the mapping functions:	int[3] GetIJK(cellID);
float[3] GetXYZ(cellID);
Error on Energy => to be recalculated, or integrated to energy.
ILD and TB compatible

---
SW status (XDAQ)
- XDAQ (see Christophe's talk)
  - Very well advanced for DHCAL
    - TB at CERN
    - Cosmics test
  - Very Strong support from
    L. Mirabito
    - Wrote CMS tracking DAQ
    - Participated to devt of the FrameWork
  - Natural candidate for Data stream
    - ~all outside DB, SC, Display (rootbased)
  - Interest at ILD // DAQ session from other R&D collaboration/projects
    - for combined TB

---
Conclusions
- slow Pull-out of UK but
  - HW is OK (last part GigE of LDA ✔)
  - FW → LDA critical pt
    - Will see in march
    - should be OK with synergy with DCC
- Manpower
  - “Not too bad”
    - too French ?
      - AIDA might help (RHUL, Bristol part of AIDA)
    - Sharing ok BUT needs coordination
    - Thanks to various delais (esp. ECAL)
- Slowly converging
  - In time for large TB
  - ILC-like tests will require additionnal HW : Beam InterFace (BIF) card

---
AIDA sub package 8.6.2 (!)
- Development of combined beam tests and common DAQ
  - Merge the EUDAQ and CALICE DAQ software framework providing the base for a common DAQ, including access to the test beam facility information (LLR, UNIGE, LAPP, RHUL, UNIBRIS);
  - Develop the hardware part of the common DAQ to allow the synchronisation of all the systems and to permit the work in ILC like mode (post-readout of bunch trains) (LLR, UNIGE, LAPP, RHUL, UNIBRIS);
  - Develop System Interfaces to existing LC detector subsystems (LUND, ULB, LPNHE, TAU, IFJPAN);
  - Extend the readout for high fluxes (LUND, ULB, RHUL)
    (TPC specific; μTCA testing)
- 400k€ requested
- All ILC Detector R&D involced (CALICE, TPC, VTX, SiTr, FwdCal)
  - Critical for EUDET telescope
- First “pre-AIDA” meeting in Palaiseau before ILD meeting
  http://ilcagenda.linearcollider.org/conferenceDisplay.py?confId=4333
EUDET TLU
our CCC
new BIF card

---
Who's who
- MK = Mark Kelly – formy CAM (since Oct 09 in private cie)
- BH = Bart Hommels – CAM
- MW = Matt Warren – UCL
- VB = Valeria Bartsch – formy UCL (since June 09 at Bristol)
- TW = Tao Wu – fromy UCL (left since march 09)
- FK = Frantisek Krivan – DESY
- MR = Matthias Reinecke – DESY
- GV = Guillaume Vouters – LAPP
- JP = Julie Prast – LAPP
- CC = Christophe Combaret – IPNL
- LM = Laurent Mirabito – IPNL
- RDN = Rodolphe Della Negra - IPNL
- RC = Rémi Cornat – LLR
- FG = Franck Gastaldi – LLR
- DD = David Decotigny – LLR