Analysis of PCB Exposure Tests
        Roman Pöschl
        LAL Orsay
- Motivation
- Analysis and Results
- Summary, Conclusion and Outlook
        Calice Analysis Meeting 8/2/2010

---
Introduction
Calorimeter Electronics to be interleaved with layer structure
Do high energetic showers create signals directly in electronics ?
If yes, Rate of faked signals ?

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup I
Test PCB
- equipped with
  PHY3 Chip Set
Prepared Slab
- W dummy
- capton and paper
  for electrical shielding
Usual Slab
Picture courtesy of B.Lutz

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup II
- PCB positioned at place of layer 12 in Ecal ~ shower maximum
  x,y position identical to layer 2
- Schematic view of test PCB - 'Expect' signals from 72 pads, 4x18 = 2 Wafer
Nominal
positions
of
Chips
Scanning
points
Sketch by M.Reinhard/F.Salvatore
- 2.6 106 Events with 90 GeV Electrons (- 5.8 105 with 70 GeV Electrons)
  At least 70 K at each scanning point (Details see later)
  Runs 331462 – 331518
  Today: Full Statistics
- First Step: Runs were subject to the same data processing chain as 'usual' runs

---
        Disabling of zero suppression in reco output
- Three Scenarios:
1) No pedestal correction
2) Full pedestal Corrections
3) Pedestal Corrections restricted to signals from Chips
    Remember that there are still 216 entries for the layer in the data files
- General Methodology:
  Subdivision of Runs into BeamTrigger and
  Pedestal Trigger Events (Oscillator Trigger) interleaved with beam events
  Corrections are applied (or not) to pedestal as well as to signal events
  Note: The reconstruction s/w had to be tweaked a bit for that

---
Statistics of Analysis
Scan 3
Scan 4
Run331513: e- 90 GeV
Signal: 216877 Evts.
Pedestal: 9831 Evts.
Run331495: e-90 GeV
Signal: 314275 Evts.
Pedestal: 15264 Evts.
Run331518: e-90 GeV
Signal: 90395 Evts.
Pedestal: 4347 Evts.
Run331511: e-?? GeV
Signal: 86989 Evts.
Pedestal: 3909 Evts.
Run331498: e- 90 GeV
Signal: 66655 Evts.
Pedestal: 4223 Evts.
Run331493: e- 90 GeV
Signal: 85884 Evts.
Pedestal: 4949 Evts.
Run331512: e- 90 GeV
Signal: 218519 Evts.
Pedestal: 9462 Evts.
Run331516: e- 90 GeV
Signal: 228138 Evts.
Pedestal: 10926 Evts.
Run331497: e- 90 GeV
Signal: 214418 Evts.
Pedestal: 13666 Evts.
Run331494: e- 90 GeV
Signal: 217415 Evts.
Pedestal: 11698 Evts.
Scan 1
Scan 2
Run331473: e- 70 GeV
Signal: 209312 Evts.
Pedestal: 38361 Evts.
Run331488: e- 90 GeV
Signal: 213369 Evts.
Pedestal: 13719 Evts.
Run331470: e- 70 GeV
        331471
Signal: 78293 Evts.
Pedestal: 14624 Evts.
Run331479: e- 90 GeV
Signal: 85543 Evts.
Pedestal: 4306 Evts.
Run331480: e- 90 GeV
Signal: 85188 Evts.
Pedestal: 4678 Evts.
Run331492: e- 90 GeV
Signal: 89435Evts.
Pedestal: 4254 Evts.
Run331472: e- 70 GeV
Signal: 189966 Evts.
Pedestal: 37137 Evts.
Run331478: 90 e- GeV
Signal: 65249 Evts.
Pedestal: 3602 Evts.
Run331491: e- 90 GeV
Signal: 217711Evts.
Pedestal: 11053 Evts.
Run331486: e- 90 GeV
Signal: 129778 Evts.
Pedestal: 6146 Evts.
Run331518: e-90 GeV
Signal: 90395 Evts.
Pedestal: 4347 Evts.
Run331516: e- 90 GeV
Signal: 228138 Evts.
Pedestal: 10926 Evts.
Run331513: e- 90 GeV
Signal: 216877 Evts.
Pedestal: 38295 Evts.
Run331511: e-?? GeV
Signal: 86989 Evts.
Pedestal: 3909 Evts.
Run331512: e- 90 GeV
Signal: 218519 Evts.
Pedestal: 9462 Evts.
Scan 4

---
On Run Selection and Observations
- Run Selected according to entries in the logbook
  No comments on bad quality by Shift Crew
- Switch of energy between Run 331473 and Run 331478
  - Change in Pedestal Rate
    20% of all events -> 5% of all events
    Still at least 3500 of (valuable) pedestal events
- at least 70k Events at each point
   - mostly 90 kEvents for off center runs
   - > 200k at (nomincal) Chip Center

---
Average Mean and RMS for Scan 1
Difference
normalized
to MIP
<< 1% of MIP
Difference
normalized
to MIP
<<0.5% of MIP
No dependency on scan position visible
Paper Plot

---
Average Mean and RMS for Scan 2
Difference
normalized
to MIP
<< 1% of MIP
Difference
normalized
to MIP
<<0.5% of MIP
No dependency on scan position visible
Paper Plot

---
Average Mean and RMS for Scan 3
Difference
normalized
to MIP
<< 1% of MIP
Difference
normalized
to MIP
<<0.5% of MIP
No dependency on scan position visible
Paper Plot

---
Average Mean and RMS for Scan 4
Difference
normalized
to MIP
<< 1% of MIP
Difference
normalized
to MIP
<<0.5% of MIP
No dependency on scan position visible
Paper Plot

---
Probability of fake hits - Estimation
Binomial Distribution
P=Nsig/Ntot , Ntot = Nevents x 17 (17 independent signals/Chip)
        Nsig = #Signals > |n| ADC Counts
σP = [P(1-P)/Ntot]1/2
N=45, 38: Nsig = 0 for all runs and all chips !!!!
  First signals seen for n=30 <=> 2/3 MIP

---
Today's starting Point – Figure Shown on CALICE Collab. Meeting at Lyon
Probability for #Hits > |2/3| MIP
No evidence for beam induced signals
Same level of 'outliers' in Signal and Pedestal Events
Chip 1 looks like being a bit noisier than the others

---
Calculation of upper Limits
- Probabilities shown on slide 13 not adequate for 0 counts
- Upper Limits/Probabilities as a function of the Threshold
- Requires calculation of limits with underlying background
Probability Density Function (Frequentist Approach):
color red {f'(n;%lambda_S + %lambda_B)=f(n;%lambda_S+%lambda_B) / sum from{n_B = 0} to {k} f(n_B;%lambda_B ) " f, f' are Poissonnian Densities"}
Presence of Background via numerator (Approach a la Zech NIM A277)
Using this pdf the Confidence Limits/Upper Limits
can be calculated using regular statistics techniques
Here: S. Brandt, Datenanalyse, pp.183
Developed (“c++ fied”) program to calculate upper limits in the presence
of known background.

---
Estimation of Background
Several Approaches:
- “Gaussian Background”
  Assume gaussian distribution of noise spectra
  mean and sigma from measured noise spectra
- “Detailed Background”
   Create pdf from measured noise spectra and generate
   noise background from these pdfs
- “Cross Modelled Background”
  Create pdf of a Chip x from measured Signal spectra when
  scanned over a Chip opposite to Chip x
  E.g. spectra for Chip 1 from Scan over Chip 4

---
Gaussian Background
Comparison between Signal and Pedestal Distributions – ² Test (root 5.22/00)
Scan 1
Scan 2
Scan 4
Scan 3
In general good agreement ²/ndf ≈ 1.5, however some serious outliers
Paper Plot ?

---
        Gaussian Background
Hit Probability as a Function of Threshold – Chip 1 – “Positive” Hits
Remark: Two Outer and two “next to central” impact points are joined
Central
Next-to-Central
Outer
Shape of Signal and Background nearly identical

---
        Gaussian Background
Hit Probability as a Function of Threshold – Chip 1 – “Negative” Hits
Remark: Two Outer and two “next to central” impact points are joined
Central
Next-to-Central
Outer
Shape of Signal and Background nearly identical

---
        Gaussian Background
Upper Limits from Central Impacts – “Positive” Hits
- 95% Confidence Limits
  Upper Limit < 1.5x10-3
  for threshold ≈ ¼ MIP
  Upper Limit < 2x10-4
  for threshold ≈ 0.4 MIP
- Limits depend on
   thresholds
- Convolution of
  Detector effects and
  Parasitic Hits
  Currents from imperfect
  grounding
  of special PCB and
  entire detector
  => residual baseline
  shifts
- Very slight tendency
  that
  Chips reach maximum
  upper limit when
  scanned over
Scan 1
Scan 2
Scan 3
Scan 4
Paper Plot
(after beautification)
Paper Plot
(after beautification)

---
        Gaussian Background
Upper Limits from Central Impacts – “Negative” Hits
- 95% Confidence Limits
  Upper Limit < 10-3
  for threshold ≈ -¼ MIP
  Upper Limit < 10-4
  for threshold ≈ 0.4 MIP
- Limits dependent
  on thresholds
- Convolution of
  Detector effects and
  Parasitic Hits
  Currents from imperfect
  grounding
  of special PCB and
  entire detector
  <=> residual baseline
  shifts
- Upper Limits on average
  smaller than for positive
  Hits
  Signal Events lead
  preferrably to positive
  ADC Counts
Scan 2
Scan 1
Scan 3
Scan 4
Paper Plot
(after beautification)

---
“Absolute Upper Limits”
At each threshold the scanned chip with the highest upper limit delivers entry
Measured rate
Upper Limit on parasitic Hits
Compare with MIP ≈ 45 ADC Counts
Effect cannot be excluded but order of magnitude smaller than noise rate
One cell out of thousand might carry additional 10-15 ADC Counts
Paper Plot and Conference Plot
        (after beautification)

---
Summary, Conclusion and Outlook
- No signals above 1 MIP observed
- Upper limit on finding signals with > 0.4 MIPS < 2x10-4
- Influence of shower on noise distributions cannot entirely be
  excluded
  Noise distribution is shifted towards positive values
  Whatever it is, the influence can be neglected for all
  practical purposes!!!!
- Observed 'effects' however influenced by details of
  detector behaviour
  Further insight could only be gained by detailed modelling of detector
  effects on noise distributions (at least very challenging!!!)

---
Backup Slides

---
Basic Spectra and Alignment
90 GeV run (331495)
- Clear Energy Peak
- Special Board place at
  ~ shower maximum
Projected Chip
Position
Hit Maps
- Layer 2
  Same xy-Position as
  Special Board
- Layer 14
  First instrumented Layer
  after Special board
Chip(s) well within
lateral shower extension
Paper Plot
Paper Plot