Hadronic shower sizes in WHCAL prototype
Jan BLAHA
WHCAL Workshop, 1 March 2010, DESY

---
Overview
The main aim is to determine the optimal dimensions
of the tungstate HCAL prototype for a future test beam campaign
Stress is put on comparison of different dedicated studies done recently at LAPP (J. Blaha), CERN (C. Grefe), and DESY (A. Lucaci-Timoce)
N.B. Studies are shown for 10 GeV pions as a typical energy in T9 PS line

---
Prototype configurations
   Detectors:
Micromegas with analog and 1 bit digital readout
Scintilator with analog readout
   Absorber:
W with thickness between 10 to 12 mm
Pure W vs W alloy (92.5% W + 4% Cu + 3.5% Ni)
W + Fe (supporting material) vs W
   Studies:
Energy shower size
Comparison of different absorber
materials (W, Fe)
Comparison of different physics list
WHCAL prototype

---
Energy shower profiles
10 mm W + 2 mm air + 5 mm scint,
38 layers AHCAL
10 mm WMix + µMegas (two 2 mm Fe covers)
Jan
Angela
Angela

---
Longitudinal containment
Christian
~ 94%
~ 72%
Infinite calorimeter
10 GeV pions	20 layers	40 layers
60 x 60 cm2	68 %	89 %
80 x 80 cm2	69 %	91 %
Difference between Micromegas and scintillator prototype is due to absorber
composition (W alloy vs pure W), its thickness, detector materials and active
medium, and lateral prototype size. Each of that can contribute in order of percent
Generally the longitudinal size is not a critical issue for WHCAL prototype,
we can simply add more layers when they are available
12 mm W + 5 mm scint + 2.5 G10

---
Fraction of 95 % contained events
12 mm W + 5 mm scint + 2.5 G10
80 %
20 %
Christian
10 GeV pions	20 layers	40 layers
60 x 60 cm2	12 %	41 %
80 x 80 cm2	16 %	60 %

---
Lateral containment
12 mm W + 5 mm scint + 2.5 G10
95 %
95 %
Christian
In deep calorimeter (80 layers or “infinite”), 95 % of energy is contained in calorimeter with lateral size ~ 60 cm

---
Lateral containment
10 mm W + 2 mm air + 5 mm scint,
38 layers AHCAL
Angela
95 %
95 %
In a short calorimeter, as it is case of the WHCAL prototype, only a fraction of the shower will be measured
Larger lateral size should be consider in comparison with a deep calorimeter or select only contained events (reduced statistics)

---
Fraction of 95% contained events
12 mm W + 5 mm scint + 2.5 G10
60 %
60 %
Christian
Significant difference in number of fully contained events for W alloy and pure W → larger lateral size should be considered for
WHCAL prototype with alloy absorber in comparison with pure W

---
Conclusions
Presented studies are consistent in their results when one consider
differences in calorimeter geometry, materials, etc.
For choice of suitable lateral size of the prototype, one must take into
account: limited size of prototype depth, absorber material (W alloy and
not pure W), energy containment and fraction of fully contained events
→ larger lateral size (~ 80 cm) is a safer choice