## Slide 1: Hadron Showers in GEANT4 (progress report)
Adam Para,
Fermilab, March 9, 2010

## Slide 2: Reminder (if we need one)
The concept of high resolution dual readout calorimeter is ‘proven’ using extensive GEANT simulations
How accurate/realistic is the hadron shower simulation?
How sensitive is the statement about the performance of the hadron calorimeter to the details of the shower simulation?

## Slide 3: Peek Under the Hood of the Shower Simulation
Geant 4.9.2.p03
BGO and Pb as target materials
QGSP_BERT
Pions, protons, neutrons
1,5,10 and 50 GeV
A lot of material/plots. More conditions deserve the studies
Challenge: how to summarize/document/present the ‘data’
Caveat: no attempt, yet to do any validation. Just a survey of what is actually done.
Will show the data for 50 GeV protons on BGO, 1000 events

## Slide 4: Physics Processes
Processes included:
Hadron-nucleus and photon-nucleus inelastic collisions
neutron capture
muon capture
spallation
interactions of the spallation products (nucleons and nuclids)
Overall tally, per event:
~ 1000 neutron interactions and captures
~ 10 proton, pi+ and pi- interactions
~ 0.1 K interactions
~ 0.01 hyperons, antibaryons and light nuclei
(deuterium, tritium, alphas) interactions

## Slide 5: Processes, Parent Energy > 100 MeV
~ Most of inelastic hadron interactions occur at energies above 100 MeV (except for neutrons)
~ half of deuterium-nucleus interactions
No neutron/muon captures

## Slide 6: Processes, Parent Energy < 100 MeV
Most of neutron interactions
All of neutron captures
all of muon captures
~1/3 of proton interactions
~1/10 of other hadrons interactions
most of light nuclei

## Slide 7: ‘High Energy’ Protons, E > 100 MeV
leading particle effect included
Interactions quite prompt (~ within 10 nsec)
interactions confined to a very narrow cylinder along the beam axis

## Slide 8: ‘Low Energy’ Protons, E < 100 MeV
Coulomb barrier below ~ 15 MeV
prompt ~10 nsec
mostly confined to narrow tube
low multiplicities

## Slide 9: Mesons

## Slide 10: Baryons

## Slide 11: ‘High Energy’ Neutrons, E>100 MeV
similar to pions and other baryons
strong component at low energies (thermalization)
some late component
wide spatial distribution (presumably correlated with low E)

## Slide 12: ‘Low Energy’ Neutrons, E<100 MeV
a lot of them, strong peak around 0 MeV
surpringly(?) prompt
wide spatial distribution

## Slide 13: Neutron Capture
strongly peaked at E = 0
~ exponential time decay, t~ 1.3 msec (material depenent!!)
very wide spatial distribution
one or two photons in the final state

## Slide 14: Light Nuclides (deuterons, tritins, alphas)
very low energies
prompt
confined to a shower core
probably unimportant

## Slide 15: Coming soon
Spallation
Energy gains
Nuclides production
Binding energies
Etc..
General problems:
  how to store, analyze and present the distributions?
  Comparison with data
Suggestions welcome..

## Slide 16: Temporary Conclusions
Looks pretty sensible, so far..