## Slide 1: FLASH Long-train Workshop
Nikolay Solyak, Shinichiro Michizono
WG3 Summary
March 17, 2010

## Slide 2: WG3 Agenda, Feb.23,2010
Session 1: HOM absorbers
HOM absorber studies - J. Sekutowicz (DESY)
Study of absorber effectiveness in ILC cavities – C.Adolphsen,K.Bane
Session 2: Cavity and klystron overhead
Results on beam loaded experiments @ FLASH - (C.Adolphsen , S.Pei)
Results of high-gradient study S.Michizono (KEK)
High gradients with 9mA beam – J.Branlard (FNAL)
Session 3: WG2+3: LLRF experience from 9mA studies (WG2)
ILC SCRF Cavity Gradient and the Operational Margin (A.Yamamoto)
…
Session 4: WG2+3 (WG3 agenda)
  Study of stability requirements for ILC BC(beam off-crest) N. Solyak ,FNAL
  Comparison between ILC spec. and FLASH 9mA study - B.Chase (FNAL)
  Future works for long-pulse high beam loading demonstration –G. Cancelo (FNAL)

## Slide 3: Results and findings from the previous runs
Beam Line absorber tests (HOM studies, J.Secutowicz) in 2008-2009 runs shows reasonably good agreement with expectations for ~2mm bunch length. Only in Sept.09 run with long–time stable operations they reached steady-state temp. rise ~2.5 deg.
Study of Absorber Effectiveness in the ILC Main Linacs (C.Adolphsen, K.Bane)
  Simulation model to compute possible trap HOM in cryostats and cavity and the HOM monopole losses in NC beam pipe at 2K.
  Find low probability for trapped modes that produce significant (> 10%) losses in 2K normal conducting beam pipe versus absorbers.
 | Sept. 08 | Sept. 09
Computed /Measured Absorbed Power [W] | 0.180 / 0.143 | 0.255 / 0.325

## Slide 4: Results from the previous runs (2)
Cavity Gradient Stability studies (S.Pei, C.Adolphsen, …)
  Comparison of beam-off measurements of pulse-to-pulse cavity gradient jitter during the flattop period for different gradients and initial cavity detuning to a cavity fill model including Lorentz force detuning.
  Good agreement measurements with model prediction with two unknown fitting parameters (initial and initial rms detuning)
  Independently of working gradient proper cavity tuning decrease gradient jitter.
High Cavity Gradient Studies (S.Michizino). Study quench limit and gradient margin in No.2 cavity @ACC6 (>32 MV/m). Observations:
  Quench limit is not sensitive to rf flattop.
  It is confirmed that the cavities should be operated under the quench limit including the tilt effects under the beam loading.

## Slide 5: Results from the previous runs (3)
Analysis and modeling of High Gradient Operations with 9mA Beam Loading (J. Branlard)
  Simulation tool was validated with Sept. 09 DAQ data, good agreement with data
  Using simulations, a machine tuning optimization scheme (QL’s PK’s) was proposed to achieve higher operating gradient while preventing cavity quench
Comparison between ILC specification and FLASH 9mA study (B.Chase, J.Branlard, G.Cancelo)
  Observation and Analysis of long term stability of the machine (amplitude and phase of VS, energy)
  Mismatch between energy and VS, calibration problems ?

## Slide 6: Discussions
Cavity overhead and ILC requirements
  Akira, D.Kostin,…, WG2
Klystron overhead and future tests
  DESY experts, WG2
  Reduce voltage of klystron to study overhead
LLRF performance
  WG2, WG3

## Slide 7: Proposed studies from WG3
  LLRF
    - Long-term energy stability
    - Performance regulations at high gradient and high current
  Gradient overhead studies (ACC67)
  Optimization of Qext, prove concept for at least 3mA
  Microphonics and LFD studies, can be done w/o beam
  Klystron Overhead
    - Need high current (at least 3mA). For smaller current need re-tune Qext
  ILC Bunch compressor stability studies
    - 2 RF units ACC45 & ACC67 to demonstrate 0.25 deg phase stability
  HOM studies, better to use shorter bunches compare with Sept.2009 run
Beam requirements:
Most studies are require high current regime > 3mA
  - 1.5 nC, 3 MHz, 800 bunches: (XFEL goal 4.5 mA)

## Slide 8
Goal stabilize LLRF to reach long term energy stability within 0.1%.
  Start with a good simulation of FLASH current parameters including:
    Power limitations.
    Detunings.
    Major disturbances.
    Loop delays, bandwidth limitations, measurement noise.
    Calibration error.
  Use the simulation to verify current data and to plan improvements towards energy stability goal.
    Improve Kp and include Ki gain in the control.
    Improve VS calibration procedure.
    Include beam current information in the control.
    Try to define a phase reference for the VS.
LLRF: Moving forward
Gustavo Cancelo, FNAL

## Slide 9
  Quantification of control overhead and power overhead.
    1st approach based on simulations. Use realistic numbers of current cavity detunings and forward and reflected power, klystron saturation, disturbances, etc.
    Plan for FLASH study.
      Study power distribution of the new FLASH configuration. (ACC45 and ACC67).
      Define a configuration that avoids quenches when beam is OFF and ON and maximizes gradients as much as possible.
      Study control overhead as a function of increased VS gradient and klystron power, including klystron saturation region.
      Include piezo studies.
Request for LLRF studies at FLASH