## Slide 1: Vacuum system for the CLIC two-beam modules
C. Garion
CERN/TE/VSC
IWLC workshop, 18-22 October 2010

## Slide 2: Outline
Vacuum system in the CLIC module
  Overview
  Specificities
Vacuum dynamics for a non-baked system
Vacuum chambers for the main beam quadrupoles
Vacuum in the accelerating structures
  Different vacuums
  Static vacuum
  Dynamic vacuum
Interconnections
Conclusions

## Slide 3: Vacuum system in the CLIC module
Main quadrupole
Accelerating structures
Drive beam quadrupole
Vacuum tank
Pumps
Overview
Drift tube
PETS
Courtesy of A. Samoshkin

## Slide 4: Vacuum system in the CLIC module
Specificities
Non-baked system  vacuum is driven by water
Low conductance (beam pipe diameter ~ 10 mm) and large areas (~3000 cm2/AS)
Typical shape and dimensions of an accelerating structure disk
6
Field ionization studies resulted in a lowering of the vacuum threshold for fast ion beam instability to: pressure < 1 nTorr [G. Rumulo]
Requirements

## Slide 5: Vacuum dynamics for a non-baked system
Elements of theory
Non baked system: Main molecular specie is water sticking probability and sojourn time are not negligible (whereas for a baked system the time of flight is the most important parameter)
10-13 s
Temperature
Activation energy of desorption
Usually, vacuum technical surfaces exhibits a wide range of binding energy (distribution density).
Sticking probability depends also the sticking factor and also on the coverage.
Courtesy of M. Taborelli

## Slide 6: Vacuum dynamics for a non-baked system
Elements of theory
For the design of a vacuum system the outgassing rate is usually used. For an non baked system, a simplified evolution law is used:
From an engineering point of view:
D. Edwards Jr. Journal of Vacuum Science and Tech.,14(1977)606
q [mbar.l/s/cm2] ~ 2.10-9 / t[h] (valid for all metals)

## Slide 7: Vacuum chambers for the MB quadrupoles
Length L of the magnet is comprised between ~50cm and 2 m
The aperture diameter is around 10 mm
P
In steady state:
with c the unit conductance of the tube and a the gas desorption per unit length
q: outgassing rate
L
S
q = 2.10-11 mbar.l/s.cm2
(after 100 hours of pumping)
L = 2 m
 Distributed pumping is mandatory
~2.10-8 mbar

## Slide 8: Vacuum chambers for the MB quadrupoles
Present design:
Stainless steel vacuum chamber, squeezed in the magnet
NEG strips sited in 2 antechambers
Copper coated
NEG strip
10 mm
50 mm
Stainless steel
Ceramic support
Spacer
Effective pumping speed per unit length: SeffQh2/l
Pressure in the central part is determined by the gap  reduce the sheet thickness  stability becomes an issue (0.3 mm for the prototype)
Buckling mode
l
h
q = 2.10-11 mbar.l/s.cm2  P ~ 8.10-10 mbar
Prototype has been manufactured and is being tested.

## Slide 9: Dynamic vacuum in the accelerating structures
Different vacuum inside the PETS and the accelerating structures can be considered:
  Static: pressure after pump down without RF power and beams
  Dynamic: during breakdown
  Dynamic: during RF pulses without breakdown

## Slide 10
Vacuum analysis based on thermal/vacuum analogy
Implementation in a FE code and application to the CLIC module
Static pressure field
Heat transfer equation:
Gas flow equation (1D):
FE vacuum model
Pressure profile for the main beam
Pressure profile for the drive beam

## Slide 11
Assumptions:
  1012 H2 molecules released during a breakdown [Calatroni et al.]
  Gas is at room temperature (conservative)
Requirement: Pressure<10-9 mbar 20ms after breakdown
Monte Carlo simulation or thermal analogy
Dynamic vacuum in the accelerating structures
Longitudinal distribution as a function of time
Vacuum degradation remains localized close to the breakdown and seems not to be an issue.
Maximum pressure during time

## Slide 12: Vacuum in the accelerating structures with RF
Qualitatively:
Thermal effect related to the power dissipation leading to thermal outgassing (conditioning)
Field emission leading to electron stimulated desorption and/or to local heating
  Dark current simulations from SLAC
  ESD data on unbaked copper at high e- energy from CERN [Pasquino, Calatroni]
  Introduce these into MC models and get gas distribution, with reasonable assumptions on molecule’s speed.
  Direct measurements seem not to be feasible due to timescale
See S. Calatroni, Accelerator session: WG 4

## Slide 13
Intramodule: Standard module / drive beam
PETS/BPM
Rotatable flange
Conflat Flange DN63
RF fingers: 0.1 copper alloy
Bellows
Part of the BPM is installed in the magnet
Drive beam interconnections
Vacuum chamber
Courtesy of A. Samoshkin, D Gudkov

## Slide 14: Main beam interconnections
Intermodule:
T0T0/ main beam
Extremity to be adapted
Non standard flange study

## Slide 15: Conclusions
The vacuum system of the CLIC main linac is non-standard:
non-baked system with low pressure requirements, low conductances and large surface areas:
  Static vacuum seems to be achieved only marginally with present design
  Dynamic vacuum due to breakdowns seems to be under control
  Dynamic vacuum due to field emission: the problems seems to be real
extremely limited space for vacuum system and interconnections