## Slide 1: Status of Hybrid target R&D at KEK-LINAC
T.Takahashi
Hiroshima University
October 21 2010
LWLC10 Geneva
Collaborators:
V. Strakhovenko O. Dadoun, R. Chehab, A.Variola,
L. Renolfi, O. Dadoun,T.Kamitani, T.Suwada, T.Omori, J.Urakawa,K.Furukawa, K.Umemori,M.Satoh,T.Sugimura,
S.Kawada, T.Akagi

## Slide 2: Hybrid target for positron source
Chehab, Variola, Strakhovenko Scheme for LC positron sources
Experimental study for further development
e-
e+, e-, g
g
e-
e+

## Slide 3: experimental site KEKB LINAC
Switch yard
８GeV e-
～nc/bunch
upto 25Hz single bunch

## Slide 4: Setup
8GeV e-
1mm
W crystal
Sweeping Magnet
0.96T 0.75m
amorphous W
8 mm
18 mm
Analyzing magnet
5 ~ 30MeV

## Slide 5: pictures
e- 8GeV
W Crystal
on the goniometer
Sweeping
magnet

## Slide 6: pictures
movable stage
amorphous
targets
analyzer magnet
and detector behind
this lead briks
thermocoupoles

## Slide 7: The data
Hybrid
Conventional
e 8GeV
sweep mag
1mm W Crystal
on axis (aligned to the beam)
off axis (not aligned to the beam)
e 8GeV
amorphous W
1.75, 3.5, 5.25, 8, 18mm
temperature
at the end of
the targets by
thermocouples
and infrared camera
positrons from
the target
momentum
analyzed
g

## Slide 8: Data taken in 2010 September
e+ yield
  hybrid(on/off), conventional
    1.75mm, 3.5mm, 5.25mm, 8mm, 18mm
Temperature
  back end of 8mm，18mm thick amorphous target
  hybrid(on/off), conventional
    bunch/bunch,,, 1Hz ~ 1nc/bunch
    equilibrium 25Hz
beam profile,,,,,,, picture taken at
  surface of the crystal
  surface of amorphous target
    conventional, hybrid (sweep on/off)

## Slide 9: Rocking curve
positron yield (arb. unit)
angle of crystal w.r.t. beam (mr)
rot. in vertical plain
e
sweep mag
8 mm
same for horizontal rotation
Preliminary
factor 3
enhancement
it was 1.2 in 2009 Sep data
we found the detector was
saturated in previous exp.

## Slide 10: e+ yield
Chart: 
| 18 | 8 | 5.25 | 3.5 | 1.75
 | 2963.6033 | 1473.6048 | 792.3586 | 449.914 | 180.3299
 | 1546.4654 | 1402.5658 | 1131.1602 | 837.8964 | 542.8112
 | 639.3514 | 418.9482 | 278.6916 | 182.1514 | 98.3618
hybrid on axis
hybrid off axis
conventional
amorphous thickness [mm]
e+ detected [a.u]
P=20MeV
detected e+.
need to correct acceptance to compare absolute yield from target
or need simulation based on this date to estimate performance
as an e+ source

## Slide 11: momentum dependence
Chart: 
| 20 | 10 | 5
18mm | 2963.6033 | 793.1217 | 258.7
8mm | 1473.6048 | 349.0585 | 110.6
5.25mm | 792.3586 | 167.8516 | 22.8
3.5mm | 449.914 | 83.7741 | 6.3
1.75mm | 180.3299 | 28.8353 | 2.2
Chart: 
| 20 | 10 | 5
 | 1546.4654 | 444.3667 | 141.3
 | 1402.5658 | 363.3244 | 111
 | 1131.1602 | 255.8751 | 73.1
 | 837.8964 | 178.4752 | 48.1
 | 542.8112 | 97.7364 | 19.8
e+ momentum[MeV]
e+ detected [a.u.]
hybrid on axis
conventional
to be compared with simulation

## Slide 12: Temperature measurement w/ thermocouples
amorphous target
thermocouple
approximately 1mm x 1mm
to fast data logger
read temperature
each 10ms
bunch by bunch temperature variation
PEDD information by thermocouple
temperature at equilibrium
total energy deposit

## Slide 13: Example of Temperature Measurement
Chart: 
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30
 | 38 | 43.1 | 46.25 | 48.3 | 50.2 | 51.2 | 52.2 | 52.85 | 53.2 | 53.8 | 54 | 54.25 | 54.35 | 54.45 | 54.65 | 54.6
Temperature of the 8mm amorphous
target for the hybrid case
Time from Beam On (Minutes)
Temperature (degree Celsius)
Base temp. 23.3℃
DT～32℃
Preliminary

## Slide 14: T vs total energy deposit
hybrid
conventional
18mm
8mm
T at equilibrium has information for
total energy deposit except for 18mm hybrid
target is thicker than shower
max

## Slide 15: single bunch temperature rise
oscillation is due to AC power
noise (50Hz at KEK)

## Slide 16: ΔT measurements
hybrid
conventional
18mm
8mm
18mm
at 8mm, T at equilibrium is higher for
hybrid but dT/bunch is lower
hybrid
conventional
dT/bunch is roughly proportional
to the e+ yield
indicating higher total energy deposit but
lower PEDD

## Slide 17: beam profile

## Slide 18: beam profile
sigx = 0.26mm,
sigy =0.91mm
on amorphous
conventional
on amorphous
hybrid sweep on
beam div. ～0.25mr
sigx = 1.2mm,
sigy = 1.6mm
on the crystal
sigx = 3.4mm,
sigy = 3.7mm

## Slide 19: summary
we took systematic data for hybrid target R&D
  yield from various target thickness
  momentum 5, 10, 20 GeV
  temperature
    at equilibrium
    single bunch variation
  beam profile
what is missing;
  2D temperature distribution on the target
    an infra red camera is tricky  thermocouple array ?
  simulation needed for the detector system

## Slide 20: outlook
(we believe) we have a set of data to discuss feasibility of hybrid target
  some data such as 2D temperature profile is still yet to be taken but can be compensated by simulation with beam profile.
analyze data with simulation
further studies
  evaluate performance of hybrid target
  optimization
    crystal (thickness, material),
    beam energy,
    amorphous thichness
to be discussed at LAL next week

## Slide 21: Channeling Radiation
e-
Crystals: converter from high energy electrons to low energy photons
photon energy (MeV)
#g crystal
#g amorphous
relative intensity of phtons from
crystal and amorphous tungsten

## Slide 22: KEKB LINAC
KEKB LINAC
    E(beam) : 8GeV Bunch Charge: ~nC
Ideal for R&D for hybrid target
    Experiences with
    crystal targets for KEKB

## Slide 23: Around the crystal target
15f hole in the lead
shielding
gs
All charged particles are
dumped here when the Sweeping magnet ON
Shielding lead bricks

## Slide 24: Set up Site Looking up from Down stream

## Slide 25: e+ yield
hybrid on axis
hybrid off axis
conventional
amorphous thickness [mm]
e+ detected [a.u]
P=5MeV
Chart: 
| 18 | 8 | 5.25 | 3.5 | 1.75
 | 258.7 | 110.6 | 22.8 | 6.3 | 2.2
 | 141.3 | 111 | 73.1 | 48.1 | 19.8
 | 57.2 | 30.6 | 15.4 | 10.1 | 1.9

## Slide 26: e+ yield
hybrid on axis
hybrid off axis
conventional
amorphous thickness [mm]
e+ detected [a.u]
P=10MeV
Chart: 
| 18 | 8 | 5.25 | 3.5 | 1.75
 | 793.1217 | 349.0585 | 167.8516 | 83.7741 | 28.8353
 | 444.3667 | 363.3244 | 255.8751 | 178.4752 | 97.7364
 | 185.1528 | 104.7176 | 61.3129 | 34.9059 | 13.0518
 | 793.1217 | 349.0585 | 167.8516 | 83.7741 | 28.8353
 | 444.3667 | 363.3244 | 255.8751 | 178.4752 | 97.7364
 | 185.1528 | 104.7176 | 61.3129 | 34.9059 | 13.0518