Beam Test Report 2010:
FORTIS
TPAC
David Cussans
University of Bristol
for the SPiDeR collaboration
(slides from M. Stanitski, Pixel2010)
(Plus Eμ proposal)

---
Introduction
- SPiDeR = Silicon Pixel Detector R&D
- UK-centered Collaboration
  - generic CMOS Pixel R&D for future Colliders
  - Birmingham, Bristol, Imperial College, Oxford and RAL
  - recently Queen Mary College joined
- Develop CMOS Sensors to address requirements for future colliders
  - Granularity
  - Speed
  - Power
  - Material budget

---
The INMAPS Process

---
INMAPS features
- Standard CMOS Process
  - 180 nm
  - 6 metal layers
  - Precision passive components (R/C)
  - Low leakage diodes
  - 5/12/18 µm epitaxial layers
- Added features for INMAPS
  - Deep p-well
  - High resistivity epitaxial layer
  - 4T structures
  - Stitching

---
Deep p-well implants
INMAPS
Standard CMOS
- Eliminate parasitic charge collection by PMOS
  - Allow full CMOS in-pixel electronics

---
High resistivity Epi-layers
- Charge collection by diffusion in epitaxial layer
  - slow
  - radiation-soft
- INMAPS on high-res Epi
- Potential benefits
  - Faster charge collection
  - Reduced charge spread
  - Increased Radiation hardness
{}
{}
)
Typical resistivity ~ 10-100Ωcm
High resistivity
~ 1-10kΩcm

---
4T Pixels
- 3T MAPS
  - Readout and charge collection area are
    the same
- 4T MAPS
  - Readout and charge collection area are at different points
  - Charge transferred to floating diffusion
- Benefits
  - Low Noise & in-pixel CDS
  - High Gain
3T
4T
STFC Centre for Instrumentation
funded Fortis 1.0/1.1
as a technology prototype
(see later)

---
Stitched Sensors
- Standard CMOS limited to ~ 2.5 x 2.5 cm2
- Technique relatively new to CMOS
  - Stitching offered by some foundries
  - Allows wafer-scale sensors
- Example Sensor
  - LAS (For imaging)
  - Designed at RAL
  - 5.4x5.4 cm2
5.4 cm

---
Sensors & Results

---
Sensor Overview
Past
TODAY
Future
DECAL
TPAC 1.0
TPAC 1.1
TPAC 1.2
FORTIS 1.0
FORTIS 1.1
CHERWELL
CHERWELL2
TPAC for
SuperB
Deep p-well
High Res & 4T
Stitching
Calorimetry
Tracking
Vertexing
INMAPS

---
The TPAC 1.2 Sensor
- 8.2 million transistors
  - 28224 pixels , 50 x 50 µm
- Sensitive area 79.4 mm2
  - of which 11.1% “dead” (logic)
- Four columns of logic + SRAM
  - Logic columns serve 42 pixels
  - Record hit locations & timestamps
  - Sparsification on chip
- Data readout
  - Slow (<5Mhz)
  - 30 bit parallel data output
- Developed for
  - Digital ECAL as Particle Counter

---
TPAC Architecture Details
Trim+ Mask
7 bits
- PreShaper
  - 4 diodes
  - 1 resistor (4 MΩ)
  - Configuration SRAM & Mask
  - Comparator trim (6 bits)
- Predicted Performance
  - Gain 94 μV/e
  - Noise 23 e-
  - Power 8.9 μW
Deep p-well
Circuit N-Wells
Diodes

---
TPAC 1.X Results
- Using 55Fe sources and IR lasers
  - Using the test pixels (analog output)
  - IR laser shows impact of deep p-well implant
Pixel profiles
F
B

---
55Fe Spectrum with TPAC 1.2
- Using test-pixels with analog out
- Powerful 55Fe source
- Take 100k samples per sensor
12 µm No deep p-well
12 µm Deep p-well
12 µm High res
18 µm High res

---
55Fe Spectrum with TPAC 1.2
- 55Fe source
  - Deep p-well
  - High -res
- Separation of Kα and Kβ
- Hi-res sensor works

---
Common Testbeam setup
Scintillators
EUDET
Telescope
Fortis 1.x
TPAC
TPAC
W/Cu/Fe
if in CALORIMETER
mode

---
TPAC 1.2 Testbeam at DESY
4 TPAC
sensors
Tungsten
slab
Nigel
TPAC stack
EUDET
Telescope

---
TPAC 1.2 Testbeam
- Online plots
- 6 sensors (1 non deep p-well)
X-X correlation plot for
two layers (back-to-back)
Hits in time with Scintillator hits

---
TPAC Testbeam Results
- No absorbers
- Due to use of in-pixel PMOS transistors, standard CMOS sensors have low efficiency
- Deep P-well shields N-wells and raises efficiency by factor ~5
- Adding high-resistivity epitaxial layer makes further improvement with resulting efficiency close to 100%
Preliminary

---
Fortis
- Test sensor to evaluate 4T for tracking/vertexing
  - Simple readout architecture
  - Analog output
- 12/13 variants of pixels for Fortis 1.0/1.1
  - Size of source follower
  - size of the collecting diode
  - Pitch (6- 45 µm)
  - Combined diodes at floating diffusion node
- Made also on high-res substrate

---
Results with Fortis 1.x
- Noise Measurements
- Photon Transfer Curve technique
  - Average noise: 4.5 e-
  - Gain 65 µV/e-
- 55Fe source:
  - Gain 56 µV/e-
  - Noise 7.7 e- using all pixels
Average noise: 4.5e-
Noise (in e-, before board noise correction)
Noise histogram
Most probable noise: 3.6e-

---
Testbeam at CERN
- Test at CERN SPS in June 2010
  - 120 GeV Pions
- Taking advantage of EUDET telescope
EUDET Telescope
Fortis 1.1 on high-res
Fortis

---
First Fortis Test beam results
PRELIMINARY
PRELIMINARY
Standard CMOS C1 variant
C variants have 15 µm pitch and
different source follower transistor variants

---
Cont'd
PRELIMINARY
PRELIMINARY
C Variant
C Variant
Pixel Variants C1-C4

---
Cont'd
- Residual to track in “y” direction.
- Includes effect telescope resolution.
PRELIMINARY
Pixel Variants C1-C4

---
eμμ (Emu)

---
Proposal for eμμ Measurement
- Muon pair production in electromagnetic showers at TeV has been investigated
  - e.g. V.A.Kudryatsev and O.G.Ryazhskaya. Il Nuovo Cimento C, 21 (1998) 119.
- Propose to make a measurement at GeV scales
  - Near threshold.
  - Match against G4 cross-sections
  - Will be challenging. Initial simulations indicate a few pairs from one week's running (at most)
µ
e
µ

---
Proposal for eμμ Measurement
- Yield @ 5GeV ~ 10-9 muon pairs per 5GeV e-
- Standard spacing upstream, target, close spacing downstream (acceptance)
- P peaks at ~100MeV

---
Fortis Photon transfer curve
A photon transfer curve is a plot of the dark-corrected signal obtained from an image sensor against the noise for that signal. It is obtained via one of two methods; an intensity
sweep, where the integration time is fixed and the light level/temperature is varied, or via an integration sweep, where the light level/temperature is fixed and the integration time is varied.
At least two identical images are required for each step to obtain the PTC and the mean signal and variance are taken from these two frames. The subtraction of the two frames to calculate the variance removes fixed pattern noise, leaving only read noise (which is the noise of interest
for an image sensor) and shot noise. Shot noise scales with the square root of the signal, giving a characteristic 0.5 gradient when plotted on a log-log plot, and is the basis of the photon transfer curve.
Many parameters can be extracted from a photon transfer curve to give the basic characteristics of an image sensor. The noise is taken from the y-intercept of the graph (i.e. the noise for 0 signal). The gain is taken from the x-intercept of the best t line taken from the plot, which if plotted on a log-log scale, should give the characteristic gradient of 0.5. The linear
full well capacity is taken from the peak in the photon transfer curve. This is where the noise begins to reduce as the variation in signal is dampened as no more signal can be collected. The maximum full well capacity is taken as the maximum signal level which is plotted on the graph.
If an integration sweep was performed, the dark current can be obtained from the gradient of the dark signal level plotted against the integration time. A result for the PTC [9] from the best pixel variant for FORTIS 1.0 is shown in Figure 6. This pixel had a very low noise of 5.8 e􀀀, and
a high conversion gain of 61.4 V/e􀀀, demonstrating the benets of the 4T pixel architect
Conversion gain at output: 65.0μV/e-
Linear full well capacity: 17,900e-
Maximum full well capacity: 27,350e-
Linear dynamic range: 4,970
Maximum dynamic range: 7,597